#### UNITED

# NATIONS

Distr.

# GENERAL

# TRANS/WP.15/AC.1/2001/41

# 21 June  2001

Original: ENGLISH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the

Working Party on the Transport of Dangerous Goods

(Geneva, 10-14 September 2001)

### CONSEQUENTIAL AMENDMENTS FOR TANKS OF CLASS 2 IN 4.3.3 AND CLASSIFICATION OF TOXIC GASES IN 2.2.21.5

## Transmitted by the European Industrial Gases Association (EIGA) */

Introduction

The changes made below reflect the changes in definition of compressed gases, high pressure liquefied gases and low pressure liquefied gases.  Also, since the LC50 values of toxic gases are included in P200, it is no longer necessary to refer to the standard ISO 10289: 1995 in 2.2.21.5.

__________

*/	Circulated by the Central Office  for International Carriage by Rail

(OCTI) under the symbol OCTI/RID/GT/III/2001/41.

GE.01-

##### Proposal

Amend 4.3.3 as follows.

4.3.3	Special provisions applicable to Class 2

4.3.3.2	Filling conditions and test pressures

4.3.3.2.1	The test pressure for tanks intended for the carriage of compressed gases having a critical temperature below -50 °C shall be at least one and one half times the filling working pressure at 15 °C as defined in 1.2.1 for receptacles.

4.3.3.2.2.	The test pressure for tanks intended for the carriage of high pressure:

-	  compressed gases having a critical temperature of 50° C or above;

- liquefied gases having a critical temperature below 70 ° C; and

- gases dissolved under pressure

shall be such that, when the shell is filled to the maximum mass of the contents per litre of capacity, the pressure reached in the shell by the substance at 55° C for tanks with thermal insulation or 65° C for shells without thermal insulation does not exceed the test pressure.

4.3.3.2.3	The test pressure for tanks intended for the carriage of low pressure liquefied gases having a critical temperature of 70° C or above will be:

(a)	If the tank is equipped with thermal insulation, at least equal to the vapour pressure, reduced by 0.1 MPa (1 bar) of the liquid at 60 ° C, but not less than 1 MPa (10 bar);

(b)	If the tank is not equipped with thermal insulation, at least equal to the vapour pressure, reduced by 0.1 MPa (1 bar), of the liquid at 65 °C, but not less than 1 MPa (10 bar).

The maximum permissible mass of contents per litre of capacity is calculated as follows:

Maximum permissible mass of contents per litre of capacity = 0.95 x density of the           liquid phase at 50 °C (in kg/l)

Moreover the vapour phase shall not disappear below 60 °C.

If the shells are not more than 1.5 m in diameter, the values of the test pressure and maximum permissible mass of contents per litre of capacity conforming to packing instruction P200 in 4.1.4.1 shall be applicable.

        - The test pressure for tanks intended for the carriage of refrigerated liquefied gases shall be not less than 1.3 times the maximum allowable working pressure as defined in 6.7 and indicated on the tank but not less than 300 kPa (3 bar) (gauge pressure); for tanks with vacuum insulation the test pressure shall be not less than 1.3 times the maximum allowable working pressure increased by 100 kPa (1 bar).

4.3.3.2.5	Table of gases and gas mixtures which may be carried in fixed tanks (tank-vehicles), battery-vehicles, demountable tanks, tank-containers and MEGCs indicating the minimum test pressure for tanks and as far as applicable the filling ratio,

In the case of gases and gas mixtures classified under n.o.s. entries, the values of the test pressure and the filling ratio shall be prescribed by the expert approved by the competent authority.

When shells for compressed or high pressure liquefied gases having a critical temperature of -50 °C or above and below 70 °C have been subjected to a test pressure lower than shown in the table, and the tanks are fitted with thermal insulation, a lower maximum load may be prescribed by the expert approved by the competent authority, provided that the pressure reached in the tank by the substance at 55 °C does not exceed the test pressure stamped on the tank.

| UN No. | Name | Classification code | Minimum test pressure for tanks | Filling ratio |
| --- | --- | --- | --- | --- |
|  |  |  | With thermal insulation | Without thermal insulation |  |
|  |  |  | MPa | bar | MPa | bar |  |
| 1008 | Boron trifluoride, compressed | 1 2 TC | 22.5 30 | 225 300 | 22.5 30 | 225 300 | 0.715 0.86 |
| 1859 | Silicon tetrafluoride, compressed | 12 TC | 20 30 | 200 300 | 20 30 | 200 300 | 0.74 1.10 |
| 1962 | Ethylene, compressed | 12 F | 12 22.5 | 120 225 | 22.5 30 | 225 300 | 0.25 0.36 0.34 0.37 |
| 1982 | Tetrafluoromethane , compressed (Refrigerant gas R14, compressed) | 12 A | 20 30 | 200 300 | 20 30 | 200 300 | 0.62 0.94 |
| 2036 | Xenon, compressed | 12 A | 12 | 120 | 13 | 130 | 1.30 1.24 |
| 2193 | Hexafluoroethane, compressed (Refrigerant gas R116 compressed) | 12 A | 16 20 | 160 200 | 20 | 200 | 1.28 1.34 1.10 |
| 2203 | Silane, compressed b | 12 F | 22.5 25 | 225 250 | 22.5 25 | 225 250 | 0.32 0.41 |
| 2417 | Carbonyl fluoride, compressed | 12 TC | 20 30 | 200 300 | 20 30 | 200 300 | 0.47 0.70 |
| 2451 | Nitrogen trifluoride, compressed | 12 O | 20 30 | 200 300 | 20 30 | 200 300 | 0.50 0.75 |
| 3374 | Acetylene, solvent free | 2 F | only in battery-vehicles and MEGCs composed of receptacles |

Amend the appropriate paragraphs of 2.2.21.5 as follows:

Toxic gases

NOTE: Gases meeting the criteria for toxicity in part or completely owing to their corrosivity are to be classified as toxic. See also the criteria under the heading "Corrosive gases" for a possible subsidiary corrosivity risk.

Gases which:

(a)	are known to be so toxic or corrosive to humans as to pose a hazard to health; or

(b)	are presumed to be toxic or corrosive to humans because they have a LC50 value for acute toxicity equal to or less than 5 000 ml/m³ (ppm) when tested in accordance with 2.2.61.1.

In the case of gas mixtures (including vapours of substances from other classes) the following formula may be used:

where		fi	= 	mole fraction of the ith component substance of the mixture;

Ti	=	toxicity index of the ith component substance of the mixture.

The Ti equals the LC50 value as found in ISO 10298:1995 4.1.4.1 P200.

When no LC50 value is listed in ISO 10298:1995 P200, a LC50 value available in scientific literature shall be used.

When the LC50 value is unknown, the toxicity index is determined by using the lowest LC50 value of substances of similar physiological and chemical effects, or through testing if this is the only practical possibility.

Corrosive gases

Gases or gas mixtures meeting the criteria for toxicity completely owing to their corrosivity are to be classified as toxic with a subsidiary corrosivity risk.

A gas mixture that is considered to be toxic due to the combined effects of corrosivity and toxicity has a subsidiary risk of corrosivity when the mixture is known by human experience to be destructive to the skin, eyes or mucous membranes or when the LC50 value of the corrosive components of the mixture is equal to or less than 5 000 ml/m3 (ppm) when the LC50 is calculated by the formula:

where	fci	=	mole fraction of the ith corrosive component substance of the mixture;

Tci 	= 	toxicity index of the ith corrosive component substance of the mixture.

The Tci equals the LC50 value as found in ISO 10298:1995 4.1.4.1 P200.

When no LC50 value is listed in ISO 10298:1995 P200, a LC50 value available in scientific literature shall be used.

When the LC50 value is unknown the toxicity index is determined by using the lowest LC50 value of substances of similar physiological and chemical effects, or through testing if this is the only practical possibility.

____________

# Text boxes

E

Economic and Social

Council

SUMMARY

Executive summary:	Following the adoption of the P200 Packing Instruction based on the UN Model Regulations, consequential amendments are required to the use instructions for tanks of Class 2 in 4.4.3 of ADR. Also, the classification of toxic gas mixtures in 2.2.2.1.5 can be calculated using data in P200.

Action to be taken:	Amend Chapter 4.4.3 and 2.2.2.1.5 as indicated below

Relevant documents:	ST/SG/AC.10/27/Add.1