| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL TRANS/WP.15/AC.1/84/Add.2 5 September 2001 ENGLISH Original: ENGLISH and FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the

Working Party on the Transport of Dangerous Goods

REPORT OF THE SESSION*/

held in Bern from 28 May to 1 June 2001

Addendum 2

Draft amendments to Chapter 4.1 of the restructured RID/ADR

Texts adopted by the Joint Meeting

____________

*  Circulated by the Central Office for International Carriage by Rail (OCTI) under the symbol OCTI/RID/GT-III/2001-A/Add.2.

4.1.4.1	P200	Replace the existing P200 with the following:

P200 PACKING INSTRUCTION P200

Type of packagings: Cylinders, tubes, pressure drums and bundles of cylinders Cylinders, tubes, pressure drums and bundles of cylinders are authorised provided the special packing provisions of 4.1.6 and the provisions listed below under (1) to (9) are met. General Pressure receptacles shall be so closed and leakproof as to prevent escape of the gases; Pressure receptacles containing toxic substances with an LC50 less than or equal to 200 ml/m3 (ppm) as specified in the table shall not be equipped with any pressure relief device; The following three tables cover compressed gases (Table 1), liquefied and dissolved gases (Table 2) and substances not in Class 2 (Table 3). They provide: (a) the UN number, name and description, and the classification code of the substance; (b) the LC50 for toxic substances; (c) the types of pressure receptacles authorised for the substance, shown by the letter "X"; (d) the maximum test period for periodic inspection of the pressure receptacles; (e) the minimum test pressure of the pressure receptacles; (f) the maximum working pressure of the pressure receptacles for compressed gases or the maximum filling ratio(s) for liquefied and dissolved gases; (g) special packing provisions that are specific to a substance.

Test pressure and filling ratios (4) The minimum test pressure required for is 1 MPa (10 bar); (5) In no case shall pressure receptacles be filled in excess of the limit permitted in the following requirements: For compressed gases, the working pressure shall be not more than two thirds of the test pressure of the pressure receptacles. Restrictions to this upper limit on working pressure are imposed by special packing provision "o". In no case shall the internal pressure at 65 °C exceed the test pressure. For high pressure liquefied gases, the filling ratio shall be such that the settled pressure at 65 °C does not exceed the test pressure of the pressure receptacles. The use of test pressures and filling ratios other than those in the table is permitted provided that the above criterion is met, except where special packing provision "o" applies. For high pressure liquefied gases for which data is not provided in the table, the maximum filling ratio (FR) shall be determined as follows: FR = 8.5 (10-4 ( dg ( Ph where FR = maximum filling ratio dg = gas density (at 15 °C, 1 bar)(in kg/m3) Ph = minimum test pressure (in bar).

| P200 | PACKING INSTRUCTION (cont'd) | P200 |
| --- | --- | --- |
| If the density of the gas is unknown, the maximum filling ratio shall be determined as follows: where FR = maximum filling ratio Ph = minimum test pressure (in bar) MM = molecular mass (in g/mol) R = 8.31451 x 10-2 bar.l.mol-1.K-1 (gas constant). For gas mixtures, the average molecular mass is to be taken, taking into account the volumetric concentrations of the various components. (c) For low pressure liquefied gases, the maximum mass of contents per litre of water capacity shall equal 0.95 times the density of the liquid phase at 50 °C; in addition, the liquid phase shall not fill the pressure receptacle at any temperature up to 60 °C. The test pressure of the pressure receptacle shall be at least equal to the vapour pressure (absolute) of the liquid at 65 °C, minus 100 kPa (1 bar). For low pressure liquefied gases for which filling data is not provided in the table, the maximum filling ratio shall be determined as follows: FR = (0.0032 ( BP – 0.24) ( d1 where FR = maximum filling ratio BP = boiling point (in Kelvin) d1 = density of the liquid at boiling point (in kg/l). |
| (d) For UN No. 1001 acetylene, dissolved, and UN 3374 acetylene, solvent free, see (9), special packing provision "p". (6) Other test pressure and filling ratio may be used provided they satisfy the general requirements outlined in paragraphs (4) and (5) above; |
| Periodic inspections (7) Refillable pressure receptacles shall be subjected to periodic inspections in accordance with the requirements of 6.2.1.6. (8) If special requirements for certain substances do not appear in the tables below, periodic inspections shall be carried out: (a) Every 5 years in the case of receptacles intended for the carriage of gases of classification codes 1T, 1TF, 1TO, 1TC, 1TFC, 1TOC, 2T, 2TO, 2TF, 2TC, 2TFC, 2TOC, 4A, 4F and 4C; (b) Every 5 years in the case of receptacles intended for the carriage of substances from other classes; (c) Every 10 years in the case of receptacles intended for the carriage of gases of classification codes 1A, 1O, 1F, 2A, 2O and 2F. By derogation from this paragraph, the periodic inspection of pressure receptacles which make use of composite materials (composite receptacles) shall be carried out at intervals determined by the competent authority of the Member State of COTIF/ Contracting Party to ADR which has approved the technical code for the design and construction. |
| Special packing provisions (9) Keys for the column "Special packing provisions": Material compatibility (for gases see ISO 11114-1:1997 and ISO 11114-2:2000) a: Aluminium alloy pressure receptacles are not authorized. b: Copper valves shall not be used. c: Metal parts in contact with the contents shall not contain more than 65% copper. d: When steel pressure receptacles are used, only those resistant to hydrogen embrittlement shall be authorized. Requirements for toxic substances with an LC50 less than or equal to 200 ml/m3 (ppm) k: Valve outlets shall be fitted with gas tight plugs or caps which shall be made of material not liable to attack by the contents of the receptacle. Each cylinder within a bundle shall be fitted with an individual valve that shall be closed during carriage. After filling, the manifold shall be evacuated, purged and plugged. Pressure receptacles shall not be fitted with a pressure relief device. Cylinders and individual cylinders in a bundle shall be limited to a maximum water capacity of 85 litres. Each valve shall have a taper threaded connection directly to the pressure receptacle and be capable of withstanding the test pressure of the pressure receptacle. Each valve shall either be of the packless type with non-perforated diaphragm, or be of a type which prevents leakage through or past the packing. Carriage in capsules is not allowed. Each pressure receptacle shall be tested for leakage after filling. |
| Gas specific provisions l: UN No. 1040 ethylene oxide may also be packed in hermetically sealed glass or metal inner packagings suitably cushioned in fibreboard, wooden or metal boxes meeting the packing group I performance level. The maximum quantity permitted in any glass inner packaging is 30 g, and the maximum quantity permitted in any metal inner packaging is 200 g. After filling, each inner packaging shall be determined to be leak-tight by placing the inner packaging in a hot water bath at a temperature, and for a period of time, sufficient to ensure that an internal pressure equal to the vapour pressure of ethylene oxide at 55 °C is achieved. The total quantity in any outer packaging shall not exceed 2.5 kg. m: Pressure receptacles shall be filled to a working pressure not exceeding 5 bar. n: A pressure receptacle shall contain not more than 5 kg of the gas. o: In no case shall the working pressure or filling ratio shown in the tables be exceeded. |
| p: For UN No. 1001 acetylene, dissolved, and UN No. 3374 acetylene, solvent free: cylinders shall be filled with a homogeneous monolithic porous mass; the working pressure and the quantity of acetylene shall not exceed the values prescribed in the approval or in ISO 3807-1:2000 or ISO 3807-2:2000, as applicable. For UN No. 1001 acetylene, dissolved: cylinders shall contain a quantity of acetone or suitable solvent as specified in the approval (see ISO 3807-1:2000 or ISO 3807-2:2000, as applicable); cylinders fitted with pressure relief devices or manifolded together shall be carried vertically. Alternatively, for UN No. 1001 acetylene, dissolved: cylinders which are not UN certified pressure receptacles may be filled with a non monolithic porous mass; the working pressure, the quantity of acetylene and the quantity of solvent shall not exceed the values prescribed in the approval. The maximum test period for periodic inspection of the cylinders shall not exceed five years. A test pressure of 52 bar shall be applied only to cylinders conforming to ISO 3807-2:2000. q: The valves of pressure receptacles for pyrophoric gases or flammable mixtures of gases containing more than 1% of pyrophoric compounds shall be fitted with gas-tight plugs or caps which shall be made of material not liable to attack by the contents of the pressure receptacle. When these pressure receptacles are manifolded in a bundle, each of the pressure receptacles shall be fitted with an individual valve that shall be closed during carriage, and the manifold outlet valve shall be fitted with a gas-tight plug or cap. Carriage in capsules is not allowed. r: Allowed for carriage in capsules under the following conditions: The mass of gas shall not exceed 150 g per capsule; The capsules shall be free from faults liable to impair the strength; The leakproofness of the closure shall be ensured by an additional device (cap, crown, seal, binding, etc.) capable of preventing any leakage of the closure during carriage; The capsules shall be placed in an outer packaging of sufficient strength. A package shall not weigh more than 75 kg. s: Aluminium alloy pressure receptacles shall be: Equipped only with brass or stainless steel valves; and Cleaned for hydrocarbons contamination and not contaminated with oil. UN certified pressure receptacles shall be cleaned in accordance with ISO 11621:1997. t: [ADR only] Other criteria may be used for filling of welded steel cylinders intended for the carriage of substances of UN No. 1965: (a) with the agreement of the competent authorities of the countries where the transport is carried out; and (b) in compliance with the provisions of a national code or standard recognised by the competent authorities or standard EN 1439:1996 "Transportable refillable steel cylinders for liquefied petroleum Gases (LPG) - Procedures for checking before, during and after refilling". |
| When the criteria for filling are different from those in P200(5), the transport document shall include the statement "Carriage in accordance with packing instruction P200, special packing provision t" and the indication of the reference temperature used for the calculation of the filling ratio. |
| Periodic inspection u: The interval between periodic tests may be extended to 10 years for aluminium alloy pressure receptacles. This derogation may only be applied to UN certified pressure receptacles when the alloy of the pressure receptacle has been subjected to stress corrosion testing as specified in ISO 7866:1999. v: The interval between inspections for steel cylinders may be extended to 15 years: with the agreement of the competent authority (authorities) of the country (countries) where the periodic inspection and the carriage take place; and in accordance with the requirements of a technical code or a standard recognised by the competent authority, or standard EN 1440:1996 "Transportable refillable welded cylinders for liquefied petroleum gas (LPG) - Periodic requalification". Requirements for N.O.S. entries and for mixtures z: The construction materials of the pressure receptacles and their accessories shall be compatible with the contents and shall not react to form harmful or dangerous compounds therewith. The test pressure and filling ratio shall be calculated in accordance with the relevant requirements of (5). Toxic substances with an LC50 less than or equal to 200 ml/m3 shall not be carried in tubes, pressure drums or MEGCs and shall meet the requirements of special packing provision "k". For pressure receptacles containing pyrophoric gases or flammable mixtures of gases containing more than 1% pyrophoric compounds, the requirements of special packing provision "q" shall be met. The necessary steps shall be taken to prevent dangerous reactions (i.e. polymerisation or decomposition) during carriage. If necessary, stabilisation or addition of an inhibitor shall be required. Mixtures containing UN No. 1911 diborane, shall be filled to a pressure such that, if complete decomposition of the diborane occurs, two thirds of the test pressure of the pressure receptacle shall not be exceeded. |
| (10) The applicable requirements of this packing instruction are considered to have been complied with if the following standards, as relevant, are applied: |
| Applicable requirements | Reference | Title of document |
| (9) (p) | EN1801: 1998 | Transportable gas cylinders - Filling conditions for single acetylene cylinders (including list of permissible porous masses) |
| (9) (p) | EN 12755: 2000 | Transportable gas cylinders - Filling conditions for acetylene bundles |

| P200 | PACKING INSTRUCTION (cont'd) | P200 |
| --- | --- | --- |
| Table 1: COMPRESSED GASES |
| UN No. | Name and description | Classification code | LC50 ml/m3 | Cylinders | Tubes | Pressure drums | Bundles of cylinders | Test period, years a | Test pressure, bar b | Working pressure, bar b | Special packing provisions |
| 1002 | AIR, COMPRESSED | 1A |  | X | X | X | X | 10 |  |  |  |
| 1006 | ARGON, COMPRESSED | 1A |  | X | X | X | X | 10 |  |  |  |
| 1014 | CARBON DIOXIDE AND OXYGEN MIXTURE, COMPRESSED | 1O |  | X | X | X | X | 10 |  |  |  |
| 1016 | CARBON MONOXIDE, COMPRESSED | 1TF | 3760 | X | X | X | X | 5 |  |  | u |
| 1023 | COAL GAS, COMPRESSED | 1TF |  | X | X | X | X | 5 |  |  |  |
| 1045 | FLUORINE, COMPRESSED | 1TOC | 185 | X |  |  | X | 5 | 200 | 30 | a, k, n, o |
| 1046 | HELIUM, COMPRESSED | 1A |  | X | X | X | X | 10 |  |  |  |
| 1049 | HYDROGEN, COMPRESSED | 1F |  | X | X | X | X | 10 |  |  | d |
| 1056 | KRYPTON, COMPRESSED | 1A |  | X | X | X | X | 10 |  |  |  |
| 1065 | NEON, COMPRESSED | 1A |  | X | X | X | X | 10 |  |  |  |
| 1066 | NITROGEN, COMPRESSED | 1A |  | X | X | X | X | 10 |  |  |  |
| 1071 | OIL GAS, COMPRESSED | 1TF |  | X | X | X | X | 5 |  |  |  |
| 1072 | OXYGEN, COMPRESSED | 1O |  | X | X | X | X | 10 |  |  | s |
| 1612 | HEXAETHYL TETRAPHOSPHATE AND COMPRESSED GAS MIXTURE | 1T |  | X | X | X | X | 5 |  |  | z |
| 1660 | NITRIC OXIDE, COMPRESSED | 1TOC | 115 | X |  |  | X | 5 | 200 | 50 | k, o |
| 1953 | COMPRESSED GAS, TOXIC, FLAMMABLE, N.O.S. | 1TF |  | X | X | X | X | 5 |  |  | z |
| 1954 | COMPRESSED GAS, FLAMMABLE, N.O.S | 1F |  | X | X | X | X | 10 |  |  | z |
| 1955 | COMPRESSED GAS, TOXIC, N.O.S. | 1T |  | X | X | X | X | 5 |  |  | z |
| 1956 | COMPRESSED GAS, N.O.S. | 1A |  | X | X | X | X | 10 |  |  | z |
| 1957 | DEUTERIUM, COMPRESSED | 1F |  | X | X | X | X | 10 |  |  | d |
| 1964 | HYDROCARBON GAS MIXTURE, COMPRESSED, N.O.S. | 1F |  | X | X | X | X | 10 |  |  | z |
| 1971 | METHANE, COMPRESSED or NATURAL GAS, COMPRESSED with high methane content | 1F |  | X | X | X | X | 10 |  |  |  |
| 1979 | RARE GASES MIXTURE, COMPRESSED | 1A |  | X | X | X | X | 10 |  |  |  |
| 1980 | RARE GASES AND OXYGEN MIXTURE, COMPRESSED | 1A |  | X | X | X | X | 10 |  |  |  |
| 1981 | RARE GASES AND NITROGEN MIXTURE, COMPRESSED | 1A |  | X | X | X | X | 10 |  |  |  |
| 2034 | HYDROGEN AND METHANE MIXTURE, COMPRESSED | 1F |  | X | X | X | X | 10 |  |  | d |
| 2190 | OXYGEN DIFLUORIDE, COMPRESSED | 1TOC | 2.6 | X |  |  | X | 5 | 200 | 30 | a, k, n, o |
| 2600 | CARBON MONOXIDE AND HYDROGEN MIXTURE, COMPRESSED | 1TF |  | X | X | X | X | 5 |  |  | d, u |
| 3156 | COMPRESSED GAS, OXIDIZING, N.O.S. | 1O |  | X | X | X | X | 10 |  |  | z |
| 3303 | COMPRESSED GAS, TOXIC, OXIDIZING, N.O.S. | 1TO |  | X | X | X | X | 5 |  |  | z |
| 3304 | COMPRESSED GAS, TOXIC, CORROSIVE, N.O.S. | 1TC |  | X | X | X | X | 5 |  |  | z |
| 3305 | COMPRESSED GAS, TOXIC, FLAMMABLE, CORROSIVE, N.O.S. | 1TFC |  | X | X | X | X | 5 |  |  | z |
| 3306 | COMPRESSED GAS, TOXIC, OXIDIZING, CORROSIVE, N.O.S. | 1TOC |  | X | X | X | X | 5 |  |  | z |

a	Not applicable for receptacles made of composite materials.

b	Where the entries are blank, the working pressure shall not exceed two thirds of the test pressure.

| P200 | PACKING INSTRUCTION (cont'd) | P200 |
| --- | --- | --- |
| Table 2: LIQUEFIED GASES AND DISSOLVED GASES |
| UN No. | Name and description | Classification code | LC50 ml/m3 | Cylinders | Pressure drums | Bundles of cylinders | Tubes | Test period, years a | Test pressure, bar | Filling ratio | Special packing provisions |
| 1001 | ACETYLENE, DISSOLVED | 4F |  | X |  | X |  | 10 | 60 |  | c, p |
| 1005 | AMMONIA, ANHYDROUS | 2TC | 4000 | X | X | X | X | 5 | 33 | 0.53 | b, r |
| 1008 | BORON TRIFLUORIDE | 2TC | 387* | X | X | X | X | 5 | 225 300 | 0.715 0.86 |  |
| 1009 | BROMOTRIFLUORO-METHANE (REFRIGERANT GAS R 13B1) | 2A |  | X | X | X | X | 10 | 42 120 250 | 1.13 1.44 1.60 | r r r |
| 1010 | 1,2-BUTADIENE, STABILIZED or | 2F |  | X | X | X | X | 10 | 10 | 0.59 | r |
| 1010 | 1,3-BUTADIENE, STABILIZED or | 2F |  | X | X | X | X | 10 | 10 | 0.55 | r |
| 1010 | MIXTURES OF 1,3-BUTADIENE AND HYDROCARBONS, STABILIZED | 2F |  | X | X | X | X | 10 | 10 | 0.50 | r, z |
| 1011 | BUTANE | 2F |  | X | X | X | X | 10 | 10 | 0.51 | r, v |
| 1012 | BUTYLENES MIXTURES or | 2F |  | X | X | X | X | 10 | 10 | 0.50 | r, z |
| 1012 | 1-BUTYLENE or | 2F |  | X | X | X | X | 10 | 10 | 0.53 |  |
| 1012 | CIS-2-BUTYLENE or | 2F |  | X | X | X | X | 10 | 10 | 0.55 |  |
| 1012 | TRANS-2 BUTYLENE | 2F |  | X | X | X | X | 10 | 10 | 0.54 |  |
| 1013 | CARBON DIOXIDE | 2A |  | X | X | X | X | 10 | 190 250 | 0.66 0.75 | r r |
| 1015 | CARBON DIOXIDE AND NITROUS OXIDE MIXTURE | 2A |  | X | X | X | X | 10 | 250 | 0.75 | r |
| 1017 | CHLORINE | 2TC | 293 | X | X | X | X | 5 | 22 | 1.25 | a, r |
| 1018 | CHLORODIFLUORO-METHANE (REFRIGERANT GAS R 22) | 2A |  | X | X | X | X | 10 | 29 | 1.03 | r |
| 1020 | CHLOROPENTAFLUORO-ETHANE (REFRIGERANT GAS R 115) | 2A |  | X | X | X | X | 10 | 25 | 1.08 | r |
| 1021 | 1-CHLORO-1,2,2,2-TETRAFLUOROETHANE (REFRIGERANT GAS R 124) | 2A |  | X | X | X | X | 10 | 12 | 1.20 | r |
| 1022 | CHLOROTRIFLUORO-METHANE (REFRIGERANT GAS R 13) | 2A |  | X | X | X | X | 10 | 100 120 190 250 | 0.83 0.90 1.04 1.10 | r r r r |
| 1026 | CYANOGEN | 2TF | 350 | X | X | X | X | 5 | 100 | 0.70 | r, u |
| 1027 | CYCLOPROPANE | 2F |  | X | X | X | X | 10 | 20 | 0.53 | r |
| 1028 | DICHLORODIFLUORO-METHANE (REFRIGERANT GAS R 12) | 2A |  | X | X | X | X | 10 | 18 | 1.15 | r |
| 1029 | DICHLOROFLUORO-METHANE (REFRIGERANT GAS R 21) | 2A |  | X | X | X | X | 10 | 10 | 1.23 | r |
| 1030 | 1,1-DIFLUOROETHANE (REFRIGERANT GAS R 152a) | 2A |  | X | X | X | X | 10 | 18 | 0.79 | r |
| 1032 | DIMETHYLAMINE, ANHYDROUS | 2F |  | X | X | X | X | 10 | 10 | 0.59 | b, r |
| 1033 | DIMETHYL ETHER | 2F |  | X | X | X | X | 10 | 18 | 0.58 | r |
| 1035 | ETHANE | 2F |  | X | X | X | X | 10 | 95 120 300 | 0.25 0.29 0.39 | r r r |
| 1036 | ETHYLAMINE | 2F |  | X | X | X | X | 10 | 10 | 0.61 | b, r |
| 1037 | ETHYL CHLORIDE | 2F |  | X | X | X | X | 10 | 10 | 0.80 | a, r |
| 1039 | ETHYL METHYL ETHER | 2F |  | X | X | X | X | 10 | 10 | 0.64 | r |
| 1040 | ETHYLENE OXIDE, or ETHYLENE OXIDE WITH NITROGEN up to a total pressure of 1MPa (10 bar) at 50 °C | 2TF | 2900* | X | X | X | X | 5 | 15 | 0.78 | l, r |
| 1041 | ETHYLENE OXIDE AND CARBON DIOXIDE MIXTURE with more than 9% ethylene oxide but not more than 87% | 2F |  | X | X | X | X | 10 | 190 250 | 0.66 0.75 | r r |
| 1043 | FERTILIZER AMMONIATING SOLUTION with free ammonia | 2A |  | X | X | X |  | 5 |  |  | b, z |
|  |  | [RID] CARRIAGE PROHIBITED |
| 1048 | HYDROGEN BROMIDE, ANHYDROUS | 2TC | 2860 | X | X | X | X | 5 | 60 | 1.54 | a, d, r |
| 1050 | HYDROGEN CHLORIDE, ANHYDROUS | 2TC | 2810* | X | X | X | X | 5 | 100 120 150 200 | 0.30 0.56 0.67 0.74 | a, d, r a, d, r a, d, r a, d, r |
| 1053 | HYDROGEN SULPHIDE | 2TF | 712 | X | X | X | X | 5 | 55 | 0.67 | d, r, u |
| 1055 | ISOBUTYLENE | 2F |  | X | X | X | X | 10 | 10 | 0.52 | r |
| 1058 | LIQUEFIED GASES, non-flammable, charged with nitrogen, carbon dioxide or air | 2A |  | X | X | X | X | 10 | Test pressure = 1.5 x working pressure | r |
| 1060 | METHYLACETYLENE AND PROPADIENE MIXTURE, STABILIZED | 2F |  | X | X | X | X | 10 |  |  | c, r, z |
|  | Propadiene with 1% to 4% methylacetylene |  |  | X | X | X | X | 10 | 22 | 0.52 | c, r |
|  | Mixture P1 |  |  | X | X | X | X | 10 | 30 | 0.49 | c, r |
|  | Mixture P2 |  |  | X | X | X | X | 10 | 24 | 0.47 | c, r |
| 1061 | METHYLAMINE, ANHYDROUS | 2F |  | X | X | X | X | 10 | 13 | 0.58 | b, r |
| 1062 | METHYL BROMIDE | 2T | 850 | X | X | X | X | 5 | 10 | 1.51 | a |
| 1063 | METHYL CHLORIDE (REFRIGERANT GAS R 40) | 2F |  | X | X | X | X | 10 | 17 | 0.81 | a, r |
| 1064 | METHYL MERCAPTAN | 2TF | 1350 | X | X | X | X | 5 | 10 | 0.78 | d, r, u |
| 1067 | DINITROGEN TETROXIDE (NITROGEN DIOXIDE) | 2TOC | 115 | X |  | X |  | 5 | 10 | 1.30 | k |
| 1069 | NITROSYL CHLORIDE | 2TC | 35 | X |  | X |  | 5 | 13 | 1.10 | k, r |
| 1070 | NITROUS OXIDE | 2O |  | X | X | X | X | 10 | 180 225 250 | 0.68 0.74 0.75 |  |
| 1075 | PETROLEUM GASES, LIQUEFIED | 2F |  | X | X | X | X | 10 |  |  | v, z |
| 1076 | PHOSGENE | 2TC | 5 | X | X | X |  | 5 | 20 | 1.23 | k, r |
| 1077 | PROPYLENE | 2F |  | X | X | X | X | 10 | 30 | 0.43 | r |
| 1078 | REFRIGERANT GAS, N.O.S. | 2A |  | X | X | X | X | 10 |  |  | r, z |
|  | Mixture F1 |  |  | X | X | X | X | 10 | 12 | 1.23 |  |
|  | Mixture F2 |  |  | X | X | X | X | 10 | 18 | 1.15 |  |
|  | Mixture F3 |  |  | X | X | X | X | 10 | 29 | 1.03 |  |
| 1079 | SULPHUR DIOXIDE | 2TC | 2520 | X | X | X | X | 5 | 14 | 1.23 | r |
| 1080 | SULPHUR HEXAFLUORIDE | 2A |  | X | X | X | X | 10 | 70 140 160 | 1.04 1.33 1.37 | r r r |
| 1081 | TETRAFLUOROETHYLE-NE, STABILIZED | 2F |  | X | X | X | X | 10 | 200 |  | m, o, r |
| 1082 | TRIFLUOROCHLOROETHY-LENE, STABILIZED | 2TF | 2000 | X | X | X | X | 5 | 19 | 1.13 | r, u |
| 1083 | TRIMETHYLAMINE, ANHYDROUS | 2F |  | X | X | X | X | 10 | 10 | 0.56 | b, r |
| 1085 | VINYL BROMIDE, STABILIZED | 2F |  | X | X | X | X | 10 | 10 | 1.37 | a, r |
| 1086 | VINYL CHLORIDE, STABILIZED | 2F |  | X | X | X | X | 10 | 12 | 0.81 | a, r |
| 1087 | VINYL METHYL ETHER, STABILIZED | 2F |  | X | X | X | X | 10 | 10 | 0.67 | r |
| 1581 | CHLOROPICRIN AND METHYL BROMIDE MIXTURE | 2T | 850 | X | X | X | X | 5 | 10 | 1.51 | a |
| 1582 | CHLOROPICRIN AND METHYL CHLORIDE MIXTURE | 2T | * | X | X | X | X | 5 | 17 | 0.81 | a |
| 1589 | CYANOGEN CHLORIDE, STABILIZED | 2TC | 80 | X |  | X |  | 5 | 20 | 1.03 | k |
| 1741 | BORON TRICHLORIDE | 2TC | 2541 | X | X | X | X | 5 | 10 | 1.19 | r |
| 1749 | CHLORINE TRIFLUORIDE | 2TOC | 299 | X | X | X | X | 5 | 30 | 1.40 | a |
| 1858 | HEXAFLUOROPROPY-LENE (REFRIGERANT GAS R 1216) | 2A |  | X | X | X | X | 10 | 22 | 1.11 | r |
| 1859 | SILICON TETRAFLUORIDE | 2TC | 450 | X | X | X | X | 5 | 200 300 | 0.74 1.10 |  |
| 1860 | VINYL FLUORIDE, STABILIZED | 2F |  | X | X | X | X | 10 | 250 | 0.64 | a, r |
| 1911 | DIBORANE | 2TF | 80 | X |  | X |  | 5 | 250 | 0.07 | d, k, o |
| 1912 | METHYL CHLORIDE AND METHYLENE CHLORIDE MIXTURE | 2F |  | X | X | X | X | 10 | 17 | 0.81 | a, r |
| 1952 | ETHYLENE OXIDE AND CARBON DIOXIDE MIXTURE with not more than 9% ethylene oxide | 2A |  | X | X | X | X | 10 | 190 250 | 0.66 0.75 | r r |
| 1958 | 1,2-DICHLORO-1,1,2,2-TETRAFLUOROETHANE (REFRIGERANT GAS R 114) | 2A |  | X | X | X | X | 10 | 10 | 1.30 | r |
| 1959 | 1,1-DIFLUOROETHYLENE (REFRIGERANT GAS R 1132a) | 2F |  | X | X | X | X | 10 | 250 | 0.77 | r |
| 1962 | ETHYLENE | 2F |  | X | X | X | X | 10 | 225 300 | 0.34 0.37 |  |
| 1965 | HYDROCARBON GAS MIXTURE, LIQUEFIED, N.O.S. | 2F |  | X | X | X | X | 10 |  | b | r, t [ADR only], v, z |
|  | Mixture A |  |  |  |  |  |  | 10 | 10 | 0.50 |  |
|  | Mixture A01 |  |  |  |  |  |  | 10 | 15 | 0.49 |  |
|  | Mixture A02 |  |  |  |  |  |  | 10 | 15 | 0.48 |  |
|  | Mixture A0 |  |  |  |  |  |  | 10 | 15 | 0.47 |  |
|  | Mixture A1 |  |  |  |  |  |  | 10 | 20 | 0.46 |  |
|  | Mixture B1 |  |  |  |  |  |  | 10 | 25 | 0.45 |  |
|  | Mixture B2 |  |  |  |  |  |  | 10 | 25 | 0.44 |  |
|  | Mixture B |  |  |  |  |  |  | 10 | 25 | 0.43 |  |
|  | Mixture C |  |  |  |  |  |  | 10 | 30 | 0.42 |  |
| 1967 | INSECTICIDE GAS, TOXIC, N.O.S. | 2T |  | X | X | X | X | 5 |  |  | z |
| 1968 | INSECTICIDE GAS, N.O.S. | 2A |  | X | X | X | X | 10 |  |  | r, z |
| 1969 | ISOBUTANE | 2F |  | X | X | X | X | 10 | 10 | 0.49 | r, v |
| 1973 | CHLORODIFLUOROME-THANE AND CHLOROPENTAFLUORO-ETHANE MIXTURE with fixed boiling point, with approximately 49% chlorodifluoromethane (REFRIGERANT GAS R 502) | 2A |  | X | X | X | X | 10 | 31 | 1.05 | r |
| 1974 | CHLORODIFLUORO-BROMOMETHANE (REFRIGERANT GAS R 12B1) | 2A |  | X | X | X | X | 10 | 10 | 1.61 | r |
| 1975 | NITRIC OXIDE AND DINITROGEN TETROXIDE MIXTURE (NITRIC OXIDE AND NITROGEN DIOXIDE MIXTURE) | 2TOC | 115 | X | X | X |  | 5 |  |  | k, z |
| 1976 | OCTAFLUOROCYCLO-BUTANE (REFRIGERANT GAS RC 318) | 2.A |  | X | X | X | X | 10 | 11 | 1.34 | r |
| 1978 | PROPANE | 2F |  | X | X | X | X | 10 | 25 | 0.42 | r, v |
| 1982 | TETRAFLUOROMETHANE (REFRIGERANT GAS R 14) | 2A |  | X | X | X | X | 10 | 200 300 | 0.62 0.94 |  |
| 1983 | 1-CHLORO-2,2,2-TRIFLUOROETHANE (REFRIGERANT GAS R 133a) | 2A |  | X | X | X | X | 10 | 10 | 1.18 | r |
| 1984 | TRIFLUOROMETHANE (REFRIGERANT GAS R 23) | 2A |  | X | X | X | X | 10 | 190 250 | 0.87 0.95 | r r |
| 2035 | 1,1,1-TRIFLUOROETHANE (REFRIGERANT GAS R 143a) | 2F |  | X | X | X | X | 10 | 35 | 0.75 | r |
| 2036 | XENON | 2A |  | X | X | X | X | 10 | 130 | 1.24 |  |
| 2044 | 2,2-DIMETHYLPROPANE | 2F |  | X | X | X | X | 10 | 10 | 0.53 | r |
| 2073 | AMMONIA SOLUTION, relative density less than 0.880 at 15 °C in water, | 4A |  |  |  |  |  |  |  |  |  |
|  | with more than 35% but not more than 40% ammonia |  |  | X | X | X | X | 5 | 10 | 0.80 | b |
|  | with more than 40% but not more than 50% ammonia |  |  | X | X | X | X | 5 | 12 | 0.77 | b |
| 2188 | ARSINE | 2TF | 20 | X |  | X |  | 5 | 42 | 1.10 | d, k |
| 2189 | DICHLOROSILANE | 2TFC | 314 | X | X | X | X | 5 | 10 | 0.90 |  |
| 2191 | SULPHURYL FLUORIDE | 2T | 3020 | X | X | X | X | 5 | 50 | 1.10 | u |
| 2192 | GERMANE c | 2TF | 620* | X | X | X | X | 5 | 250 | 1.02 | d, r |
| 2193 | HEXAFLUOROETHANE (REFRIGERANT GAS R 116) | 2A |  | X | X | X | X | 10 | 200 | 1.10 |  |
| 2194 | SELENIUM HEXAFLUORIDE | 2TC | 50 | X |  | X |  | 5 | 36 | 1.46 | k, r |
| 2195 | TELLURIUM HEXAFLUORIDE | 2TC | 25 | X |  | X |  | 5 | 20 | 1.00 | k, r |
| 2196 | TUNGSTEN HEXAFLUORIDE | 2TC | 160* | X |  | X |  | 5 | 10 | 2.70 | a, k, r |
| 2197 | HYDROGEN IODIDE, ANHYDROUS | 2TC | 2860 | X | X | X | X | 5 | 23 | 2.25 | a, d, r |
| 2198 | PHOSPHORUS PENTAFLUORIDE | 2TC | 190* | X |  | X |  | 5 | 200 300 | 0.90 1.34 | k k |
| 2199 | PHOSPHINE c | 2TF | 20 | X |  | X |  | 5 | 225 250 | 0.30 0.45 | d, k, r d, k, r |
| 2200 | PROPADIENE, STABILIZED | 2F |  | X | X | X | X | 10 | 22 | 0.50 | r |
| 2202 | HYDROGEN SELENIDE, ANHYDROUS | 2TF | 2 | X |  | X |  | 5 | 31 | 1.60 | k |
| 2203 | SILANE c | 2F |  | X | X | X | X | 10 | 225 250 | 0.32 0.36 | d, q d, q |
| 2204 | CARBONYL SULPHIDE | 2TF | 1700 | X | X | X | X | 5 | 26 | 0.84 | r, u |
| 2417 | CARBONYL FLUORIDE | 2TC | 360 | X | X | X | X | 5 | 200 300 | 0.47 0.70 |  |
| 2418 | SULPHUR TETRAFLUORIDE | 2TC | 40 | X |  | X |  | 5 | 30 | 0.91 | k, r |
| 2419 | BROMOTRIFLUORO-ETHYLENE | 2F |  | X | X | X | X | 10 | 10 | 1.19 | r |
| 2420 | HEXAFLUOROACETONE | 2TC | 470 | X | X | X | X | 5 | 22 | 1.08 | r |
| 2421 | NITROGEN TRIOXIDE | 2TOC | CARRIAGE PROHIBITED |
| 2422 | OCTAFLUOROBUT-2-ENE (REFRIGERANT GAS R 1318) | 2A |  | X | X | X | X | 10 | 12 | 1.34 | r |
| 2424 | OCTAFLUOROPROPANE (REFRIGERANT GAS R 218) | 2A |  | X | X | X | X | 10 | 25 | 1.09 | r |
| 2451 | NITROGEN TRIFLUORIDE | 2O |  | X | X | X | X | 10 | 200 300 | 0.50 0.75 |  |
| 2452 | ETHYLACETYLENE, STABILIZED | 2F |  | X | X | X | X | 10 | 10 | 0.57 | c, r |
| 2453 | ETHYL FLUORIDE (REFRIGERANT GAS R 161) | 2F |  | X | X | X | X | 10 | 30 | 0.57 | r |
| 2454 | METHYL FLUORIDE (REFRIGERANT GAS R 41) | 2F |  | X | X | X | X | 10 | 300 | 0.36 | r |
| 2455 | METHYL NITRITE | 2A | CARRIAGE PROHIBITED |
| 2517 | 1-CHLORO-1,1-DIFLUOROETHANE (REFRIGERANT GAS R 142b) | 2F |  | X | X | X | X | 10 | 10 | 0.99 | r |
| 2534 | METHYLCHLOROSILANE | 2TFC | 600 | X | X | X | X | 5 |  |  | r, z |
| 2548 | CHLORINE PENTAFLUORIDE | 2TOC | 122 | X |  | X |  | 5 | 13 | 1.49 | a, k |
| 2599 | CHLOROTRIFLUORO-METHANE AND TRIFLUOROMETHANE AZEOTROPIC MIXTURE with approximately 60% chlorotrifluoromethane (REFRIGERANT GAS R 503) | 2A |  | X | X | X | X | 10 | 31 42 100 | 0.11 0.20 0.66 | r r r |
| 2601 | CYCLOBUTANE | 2F |  | X | X | X | X | 10 | 10 | 0.63 | r |
| 2602 | DICHLORODIFLUORO-METHANE AND DIFLUOROETHANE AZEOTROPIC MIXTURE with approximately 74% dichlorodifluoromethane (REFRIGERANT GAS R 500) | 2A |  | X | X | X | X | 10 | 22 | 1.01 | r |
| 2676 | STIBINE | 2TF | 20 | X |  | X |  | 5 | 20 | 1.20 | k, r |
| 2901 | BROMINE CHLORIDE | 2TOC | 290 | X | X | X | X | 5 | 10 | 1.50 | a |
| 3057 | TRIFLUOROACETYL CHLORIDE | 2TC | 10* | X | X | X |  | 5 | 17 | 1.17 | k, r |
| 3070 | ETHYLENE OXIDE AND DICHLORODIFLUORO-METHANE MIXTURE with not more than 12,5% ethylene oxide | 2A |  | X | X | X | X | 10 | 18 | 1.09 | r |
| 3083 | PERCHLORYL FLUORIDE | 2TO | 770 | X | X | X | X | 5 | 33 | 1.21 | k, u |
| 3153 | PERFLUORO(METHYL VINYL ETHER) | 2F |  | X | X | X | X | 10 | 20 | 0.75 | r |
| 3154 | PERFLUORO(ETHYL VINYL ETHER) | 2F |  | X | X | X | X | 10 | 10 | 0.98 | r |
| 3157 | LIQUEFIED GAS, OXIDIZING, N.O.S. | 2O |  | X | X | X | X | 10 |  |  | z |
| 3159 | 1,1,1,2-TETRAFLUOROETHANE (REFRIGERANT GAS R 134a) | 2A |  | X | X | X | X | 10 | 22 | 1.04 | r |
| 3160 | LIQUEFIED GAS, TOXIC, FLAMMABLE, N.O.S. | 2TF |  | X | X | X | X | 5 |  |  | r, z |
| 3161 | LIQUEFIED GAS, FLAMMABLE, N.O.S. | 2F |  | X | X | X | X | 10 |  |  | r, z |
| 3162 | LIQUEFIED GAS, TOXIC, N.O.S. | 2T |  | X | X | X | X | 5 |  |  | z |
| 3163 | LIQUEFIED GAS, N.O.S. | 2A |  | X | X | X | X | 10 |  |  | r, z |
| 3220 | PENTAFLUOROETHANE (REFRIGERANT GAS R 125) | 2A |  | X | X | X | X | 10 | 49 36 | 0.95 0.72 | r r |
| 3252 | DIFLUOROMETHANE (REFRIGERANT GAS R 32) | 2F |  | X | X | X | X | 10 | 48 | 0.78 | r |
| 3296 | HEPTAFLUOROPROPANE (REFRIGERANT GAS R 227) | 2A |  | X | X | X | X | 10 | 15 | 1.20 | r |
| 3297 | ETHYLENE OXIDE AND CHLOROTETRAFLUORO-ETHANE MIXTURE with not more than 8.8% ethylene oxide | 2A |  | X | X | X | X | 10 | 10 | 1.16 | r |
| 3298 | ETHYLENE OXIDE AND PENTAFLUOROETHANE MIXTURE with not more than 7.9% ethylene oxide | 2A |  | X | X | X | X | 10 | 26 | 1.02 | r |
| 3299 | ETHYLENE OXIDE AND TETRAFLUOROETHANE MIXTURE with not more than 5.6% ethylene oxide | 2A |  | X | X | X | X | 10 | 17 | 1.03 | r |
| 3300 | ETHYLENE OXIDE AND CARBON DIOXIDE MIXTURE with more than 87% ethylene oxide | 2TF | More than 2900 | X | X | X | X | 5 | 28 | 0.73 | r |
| 3307 | LIQUEFIED GAS, TOXIC, OXIDIZING, N.O.S. | 2TO |  | X | X | X | X | 5 |  |  | z |
| 3308 | LIQUEFIED GAS, TOXIC, CORROSIVE, N.O.S. | 2TC |  | X | X | X | X | 5 |  |  | r, z |
| 3309 | LIQUEFIED GAS, TOXIC, FLAMMABLE, CORROSIVE, N.O.S. | 2TFC |  | X | X | X | X | 5 |  |  | r, z |
| 3310 | LIQUEFIED GAS, TOXIC, OXIDIZING, CORROSIVE, N.O.S. | 2TOC |  | X | X | X | X | 5 |  |  | z |
| 3318 | AMMONIA SOLUTION, relative density less than 0.880 at 15 °C in water, with more than 50% ammonia | 4TC |  | X | X | X | X | 5 |  |  | b |
| 3337 | REFRIGERANT GAS R 404A | 2A |  | X | X | X | X | 10 | 36 | 0.82 | r |
| 3338 | REFRIGERANT GAS R 407A | 2A |  | X | X | X | X | 10 | 36 | 0.94 | r |
| 3339 | REFRIGERANT GAS R 407B | 2A |  | X | X | X | X | 10 | 38 | 0.93 | r |
| 3340 | REFRIGERANT GAS R 407C | 2A |  | X | X | X | X | 10 | 35 | 0.95 | r |
| 3354 | INSECTICIDE GAS, FLAMMABLE, N.O.S | 2F |  | X | X | X | X | 10 |  |  | r, z |
| 3355 | INSECTICIDE GAS, TOXIC, FLAMMABLE, N.O.S. | 2TF |  | X | X | X | X | 5 |  |  | r, z |
| 3374 | ACETYLENE, SOLVENT FREE | 2F |  | X |  | X |  | 5 | 60 |  | c, p |

a	Not applicable for receptacles made of composite materials.

b	For mixtures of UN No. 1965, the maximum permissible filling mass per litre of capacity is as follows:

c	Considered as pyrophoric.

| P200 | PACKING INSTRUCTION (cont'd) | P200 |
| --- | --- | --- |
| Table 3: SUBSTANCES NOT IN CLASS 2 |
| UN No. | Name and description | Class or Division | Classification Code | LC50 ml/m3 | Cylinders | Pressure drums | Bundles of cylinders | Tubes | Test period, years a | Test pressure, bar | Filling ratio | Special packing provisions |
| 1051 | HYDROGEN CYANIDE, STABILIZED containing less than 3% water | 6.1 | TF1 | 140 | X | X | X |  | 5 | 100 | 0.55 | k |
| 1052 | HYDROGEN FLUORIDE, ANHYDROUS | 8 | CT1 | 966* | X | X | X |  | 5 | 10 | 0.84 |  |
| 1745 | BROMINE PENTAFLUORIDE | 5.1 | OTC | 25* | X | X | X |  | 5 | 10 | ** | k |
| 1746 | BROMINE TRIFLUORIDE | 5.1 | OTC | 180 | X | X | X |  | 5 | 10 | ** | k |
| 2495 | IODINE PENTAFLUORIDE | 5.1 | OTC | 120 | X | X | X |  | 5 | 10 | ** | k |

a	Not applicable for receptacles made of composite materials.

* 	This LC50 value is under review.

** 	A minimum ullage of 8% by volume is required.

4.1.4.1	P601	Add a new special packing provision specific to RID and ADR to read as follows:

"RR3	Only receptacles which satisfy one of the special requirements listed in 4.1.4.4 shall be used.".

4.1.4.4	Add in the table a new particular pressure receptacle requirement as follows:

| Pressure receptacle requirements | UN Nos. | Applicable construction, testing, filling and marking requirements |
| --- | --- | --- |
| PR7 | 1614 | Liquid hydrogen cyanide, stabilized, when completely absorbed by an inert porous material, shall be packed in metal receptacles of a capacity of not more than 7.5 litres, placed in wooden cases in such a manner that they cannot come into contact with one another. Such combination packagings shall comply with the following conditions: (1) the receptacles shall be tested at a pressure of not less than 0.6 MPa (6 bar) (gauge pressure); (2) the receptacles shall be entirely filled with the porous material which shall not shake down or form dangerous spaces even after prolonged use or under impact, even at temperatures of up to 50 °C; (3) the date of filling shall be durably marked on the lid of each receptacle; (4) combination packagings shall be tested and approved, in accordance with 6.1.5.21 for packing group I; (5) a package shall not weigh more than 120 kg. |

4.1.6.5	Delete the whole paragraph and renumber existing paragraph 4.1.6.6 as 4.1.6.5.

4.1.6.6 	Add the following paragraphs after existing 4.1.6.6 (renumbered as 4.1.6.5) and renumber existing 4.1.6.7 as 4.1.6.10.

"4.1.6.6	Non-refillable pressure receptacles shall:

(a) 	be carried in an outer packaging, such as a box, or crate, or in shrink-wrapped trays or stretch-wrapped trays;

(b) 	be of a water capacity less than or equal to 1.25 litres when filled with flammable or toxic gas;

(c) 	not be used for toxic gases with an LC50 less than or equal to 200 ml/m3; and

(d)	not be repaired after being put into service.

4.1.6.7	Pressure receptacles shall not be subjected to repairs of any of the following;

(a)	weld cracks or other weld defects;

(b)	cracks in walls;

(c)	leaks or defects in the material of the wall, head or bottom.

4.1.6.8	Pressure receptacles shall not be offered for filling:

(a)	when damaged to such an extent that the integrity of the pressure receptacle or its service equipment may be affected;

(b)	unless the pressure receptacle and its service equipment has been examined and found to be in good working order; and

(c)	unless the required certification, retest, and filling markings are legible.

4.1.6.9 	Charged pressure receptacles shall not be offered for carriage;

(a)	when leaking;

(b)	when damaged to such an extent that the integrity of the pressure receptacle or its service equipment may be affected;

(c)	unless the pressure receptacle and its service equipment has been examined and found to be in good working order; and

(d)	unless the required certification, retest, and filling markings are legible.".

_______________

# Footnotes

* 	This LC50 value is under review.

* 	This LC50 value is under review.

* 	This LC50 value is under review.

* 	This LC50 value is under review.

# Text boxes

0.42

A

A01

propane

Commercial

utane

Commercial b

kg/l

Density at 50 °C in

Maximum permissible mass of contents per litre of capacity

0.525

0.516

0.505

0.495

0.485

0.474

0.463

0.450

0.440

0.50

0.49

0.48

0.47

0.46

0.45

0.44

0.43

A02

A0

A1

B1

B2

B

C