| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 1921 | PROPYLENEIMINE, STABILIZED | 3 | FT1 | I | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1922 | PYRROLIDINE | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1923 | CALCIUM DITHIONITE (CALCIUM HYDROSULPHITE) | 4.2 | S4 | II | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1928 | METHYL MAGNESIUM BROMIDE IN ETHYL ETHER | 4.3 | WF1 | I | 4.3+3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 1 |  |
| 1929 | POTASSIUM DITHIONITE (POTASSIUM HYDROSULPHITE) | 4.2 | S4 | II | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1931 | ZINC DITHIONITE (ZINC HYDROSULPHITE) | 9 | M11 | III | 9 |  | LQ27 |  | PP |  |  |  |  | 0 |  |
| 1932 | ZIRCONIUM SCRAP | 4.2 | S4 | III | 4.2 | 524 592 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1935 | CYANIDE SOLUTION, N.O.S. | 6.1 | T4 | I | 6.1 | 274 525 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1935 | CYANIDE SOLUTION, N.O.S. | 6.1 | T4 | II | 6.1 | 274 525 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1935 | CYANIDE SOLUTION, N.O.S. | 6.1 | T4 | III | 6.1 | 274 525 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 1938 | BROMOACETIC ACID | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1939 | PHOSPHORUS OXYBROMIDE | 8 | C2 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1940 | THIOGLYCOLIC ACID | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1941 | DIBROMODIFLUORO-METHANE | 9 | M11 | III | 9 |  | LQ28 |  | PP |  |  |  |  | 0 |  |
| 1942 | AMMONIUM NITRATE with not more than 0.2% total combustible material, including any organic substance calculated as carbon, to the exclusion of any other added substance | 5.1 | O2 | III | 5.1 | 306 611 | LQ12 | B | PP |  | ST01, CO02 | HA09 |  | 0 | CO02 and HA09 apply only when this substance is carried in bulk or without packaging |
| 1944 | MATCHES, SAFETY (book, card or strike on box) | 4.1 | F1 | III | 4.1 | 293 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1945 | MATCHES, WAX 'VESTA' | 4.1 | F1 | III | 4.1 | 293 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1950 | AEROSOLS, asphyxiant | 2 | 5A |  | 2.2 | 190 625 | LQ2 |  | PP |  |  |  |  | 0 |  |
| 1950 | AEROSOLS, corrosive | 2 | 5C |  | 2.2+8 | 190 625 | LQ2 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1950 | AEROSOLS, corrosive, oxidizing | 2 | 5CO |  | 2.2+5.1+8 | 190 625 | LQ2 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1950 | AEROSOLS, flammable | 2 | 5F |  | 2.1 | 190 625 | LQ2 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1950 | AEROSOLS, flammable, corrosive | 2 | 5FC |  | 2.1+8 | 190 625 | LQ2 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1950 | AEROSOLS, oxidizing | 2 | 5O |  | 2.2+5.1 | 190 625 | LQ2 |  | PP |  |  |  |  | 0 |  |
| 1950 | AEROSOLS, toxic | 2 | 5T |  | 2.2+6.1 | 190 625 | LQ1 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1950 | AEROSOLS, toxic, corrosive | 2 | 5TC |  | 2.2+6.1 +8 | 190 625 | LQ1 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1950 | AEROSOLS, toxic, flammable | 2 | 5TF |  | 2.1+6.1 | 190 625 | LQ1 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1950 | AEROSOLS, toxic, flammable, corrosive | 2 | 5TFC |  | 2.2+6.1+8 | 190 625 | LQ1 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1950 | AEROSOLS, toxic, oxidizing | 2 | 5TO |  | 2.2+6.1 +5.1 | 190 625 | LQ1 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1950 | AEROSOLS, toxic, oxidizing, corrosive | 2 | 5TOC |  | 2.2+6.1 +5.1+8 | 190 625 | LQ1 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1951 | ARGON, REFRIGERATED LIQUID | 2 | 3A |  | 2.2 | 593 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1952 | ETHYLENE OXIDE AND CARBON DIOXIDE MIXTURE with not more than 9% ethylene oxide | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1953 | COMPRESSED GAS, TOXIC, FLAMMABLE, N.O.S. | 2 | 1TF |  | 2.3+2.1 | 274 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1954 | COMPRESSED GAS, FLAMMABLE, N.O.S. | 2 | 1F |  | 2.1 | 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1955 | COMPRESSED GAS, TOXIC, N.O.S. | 2 | 1T |  | 2.3 | 274 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1956 | COMPRESSED GAS, N.O.S. | 2 | 1A |  | 2.2 | 274 567 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1957 | DEUTERIUM, COMPRESSED | 2 | 1F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1958 | 1,2-DICHLORO-1,1,2,2-TETRAFLUOROETHANE (REFRIGERANT GAS R 114) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1959 | 1,1-DIFLUOROETHYLENE (REFRIGERANT GAS R 1132a) | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1961 | ETHANE, REFRIGERATED LIQUID | 2 | 3F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1962 | ETHYLENE | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1963 | HELIUM, REFRIGERATED LIQUID | 2 | 3A |  | 2.2 | 593 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1964 | HYDROCARBON GAS MIXTURE, COMPRESSED, N.O.S. | 2 | 1F |  | 2.1 | 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1965 | HYDROCARBON GAS MIXTURE, LIQUEFIED, N.O.S. such as mixtures A, A01, A02, A0, A1, B1, B2, B or C | 2 | 2F |  | 2.1 | 274 583 | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1966 | HYDROGEN, REFRIGERATED LIQUID | 2 | 3F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1967 | INSECTICIDE GAS, TOXIC, N.O.S. | 2 | 2T |  | 2.3 | 274 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1968 | INSECTICIDE GAS, N.O.S. | 2 | 2A |  | 2.2 | 274 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1969 | ISOBUTANE | 2 | 2F |  | 2.1 |  | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1970 | KRYPTON, REFRIGERATED LIQUID | 2 | 3A |  | 2.2 | 593 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1971 | METHANE, COMPRESSED or NATURAL GAS, COMPRESSED with high methane content | 2 | 1F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1972 | METHANE, REFRIGERATED LIQUID or NATURAL GAS, REFRIGERATED LIQUID with high methane content | 2 | 3F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1973 | CHLORODIFLUORO- METHANE AND CHLOROPENTAFLUORO- ETHANE MIXTURE with fixed boiling point, with approximately 49% chlorodifluoromethane (REFRIGERANT GAS R 502) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1974 | CHLORODIFLUOROBROMOMETHANE (REFRIGERANT GAS R 12B1) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1975 | NITRIC OXIDE AND DINITROGEN TETROXIDE MIXTURE (NITRIC OXIDE AND NITROGEN DIOXIDE MIXTURE) | 2 | 2TOC |  | 2.3+5.1+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1976 | OCTAFLUOROCYCLO-BUTANE (REFRIGERANT GAS RC 318) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1977 | NITROGEN, REFRIGERATED LIQUID | 2 | 3A |  | 2.2 | 593 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1978 | PROPANE | 2 | 2F |  | 2.1 |  | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1979 | RARE GASES MIXTURE, COMPRESSED | 2 | 1A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1980 | RARE GASES AND OXYGEN MIXTURE, COMPRESSED | 2 | 1A |  | 2.2 | 567 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1981 | RARE GASES AND NITROGEN MIXTURE, COMPRESSED | 2 | 1A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1982 | TETRAFLUOROMETHANE, (REFRIGERANT GAS R 14) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1983 | 1-CHLORO-2,2,2-TRIFLUOROETHANE (REFRIGERANT GAS R 133a) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1984 | TRIFLUOROMETHANE (REFRIGERANT GAS R 23) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1986 | ALCOHOLS, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | I | 3+6.1 | 274 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1986 | ALCOHOLS, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | II | 3+6.1 | 274 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1986 | ALCOHOLS, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | III | 3+6.1 | 274 802 | LQ7 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 1987 | ALCOHOLS, N.O.S. (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 274 640C | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1987 | ALCOHOLS, N.O.S. (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 274 640D | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1987 | ALCOHOLS, N.O.S. | 3 | F1 | III | 3 | 274 | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1988 | ALDEHYDES, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | I | 3+6.1 | 274 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1988 | ALDEHYDES, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | II | 3+6.1 | 274 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1988 | ALDEHYDES, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | III | 3+6.1 | 274 802 | LQ7 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 1989 | ALDEHYDES, N.O.S. (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 274 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1989 | ALDEHYDES, N.O.S. (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 274 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1989 | ALDEHYDES, N.O.S. (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 274 640C | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1989 | ALDEHYDES, N.O.S. (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 274 640D | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1989 | ALDEHYDES, N.O.S. | 3 | F1 | III | 3 | 274 | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1990 | BENZALDEHYDE | 9 | M11 | III | 9 |  | LQ28 |  | PP |  |  |  |  | 0 |  |
| 1991 | CHLOROPRENE, STABILIZED | 3 | FT1 | I | 3+6.1 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. | 3 | FT1 | I | 3+6.1 | 274 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. | 3 | FT1 | II | 3+6.1 | 274 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. | 3 | FT1 | III | 3+6.1 | 274 802 | LQ7 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 1993 | FLAMMABLE LIQUID, N.O.S. (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 274 640A | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1993 | FLAMMABLE LIQUID, N.O.S. (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 274 640B | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1993 | FLAMMABLE LIQUID, N.O.S. (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 274 640C | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1993 | FLAMMABLE LIQUID, N.O.S. (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 274 640D | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1993 | FLAMMABLE LIQUID, N.O.S. | 3 | F1 | III | 3 | 274 640E | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1993 | FLAMMABLE LIQUID, N.O.S. (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | III | 3 | 274 640F | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1993 | FLAMMABLE LIQUID, N.O.S. (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | III | 3 | 274 640G | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1993 | FLAMMABLE LIQUID, N.O.S. (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | III | 3 | 274 640H | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1994 | IRON PENTACARBONYL | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1999 | TARS, LIQUID, including road asphalt and oils, bitumen and cut backs (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1999 | TARS, LIQUID, including road asphalt and oils, bitumen and cut backs (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1999 | TARS, LIQUID, including road asphalt and oils, bitumen and cut backs | 3 | F1 | III | 3 | 640E | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1999 | TARS, LIQUID, including road asphalt and oils, bitumen and cut backs (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) | 3 | F1 | III | 3 | 640F | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1999 | TARS, LIQUID, including road asphalt and oils, bitumen and cut backs (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | III | 3 | 640G | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2000 | CELLULOID in block, rods, rolls, sheets, tubes, etc., except scrap | 4.1 | F1 | III | 4.1 | 502 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2001 | COBALT NAPHTHENATES, POWDER | 4.1 | F3 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2002 | CELLULOID, SCRAP | 4.2 | S2 | III | 4.2 | 526 592 | LQ0 |  | PP |  |  |  |  | 0 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 2003 | METAL ALKYLS, WATER-REACTIVE, N.O.S. or METAL ARYLS, WATER-REACTIVE, N.O.S. | 4.2 | SW | I | 4.2+4.3 | 274 527 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2004 | MAGNESIUM DIAMIDE | 4.2 | S4 | II | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2005 | MAGNESIUM DIPHENYL | 4.2 | SW | I | 4.2+4.3 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2006 | PLASTICS, NITROCELLULOSE-BASED, SELF-HEATING, N.O.S. | 4.2 | S2 | III | 4.2 | 274 528 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 | S4 | I | 4.2 | 524 540 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 | S4 | II | 4.2 | 524 540 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 | S4 | III | 4.2 | 540 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2009 | ZIRCONIUM, DRY, finished sheets, strip or coiled wire | 4.2 | S4 | III | 4.2 | 524 592 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2010 | MAGNESIUM HYDRIDE | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2011 | MAGNESIUM PHOSPHIDE | 4.3 | WT2 | I | 4.3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 2 |  |
| 2012 | POTASSIUM PHOSPHIDE | 4.3 | WT2 | I | 4.3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 2 |  |
| 2013 | STRONTIUM PHOSPHIDE | 4.3 | WT2 | I | 4.3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 2 |  |
| 2014 | HYDROGEN PEROXIDE, AQUEOUS SOLUTION with not less than 20% but not more than 60% hydrogen peroxide (stabilized as necessary) | 5.1 | OC1 | II | 5.1+8 |  | LQ10 | T | PP, EP |  |  |  |  | 0 |  |
| 2015 | HYDROGEN PEROXIDE, AQUEOUS SOLUTION, STABILIZED with more than 70% hydrogen peroxide | 5.1 | OC1 | I | 5.1+8 |  | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 2015 | HYDROGEN PEROXIDE, AQUEOUS SOLUTION, STABILIZED with more than 60% hydrogen peroxide but not more than 70% hydrogen peroxide | 5.1 | OC1 | I | 5.1+8 | 640 O | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 2016 | AMMUNITION, TOXIC, NON-EXPLOSIVE without burster or expelling charge, non-fuzed | 6.1 | T2 | II | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2017 | AMMUNITION, TEAR-PRODUCING, NON-EXPLOSIVE without burster or expelling charge, non-fuzed | 6.1 | TC2 | II | 6.1+8 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2018 | CHLOROANILINES, SOLID | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2019 | CHLOROANILINES, LIQUID | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2020 | CHLOROPHENOLS, SOLID | 6.1 | T2 | III | 6.1 | 205 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2021 | CHLOROPHENOLS, LIQUID | 6.1 | T1 | III | 6.1 | 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2022 | CRESYLIC ACID | 6.1 | TC1 | II | 6.1+8 | 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2023 | EPICHLOROHYDRIN | 6.1 | TF1 | II | 6.1+3 | 279 802 | LQ17 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2024 | MERCURY COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | I | 6.1 | 43 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2024 | MERCURY COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | II | 6.1 | 43 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2024 | MERCURY COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | III | 6.1 | 43 274 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | T5 | I | 6.1 | 43 274 529 585 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | T5 | II | 6.1 | 43 274 529 585 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | T5 | III | 6.1 | 43 274 529 585 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | T3 | I | 6.1 | 43 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | T3 | II | 6.1 | 43 274 802 | LQ18 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | T3 | III | 6.1 | 43 274 802 | LQ9 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2027 | SODIUM ARSENITE, SOLID | 6.1 | T5 | II | 6.1 | 43 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2028 | BOMBS, SMOKE, NON-EXPLOSIVE with corrosive liquid, without initiating device | 8 | C11 | II | 8 |  | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 2029 | HYDRAZINE, ANHYDROUS | 8 | CFT | I | 8+3+6.1 | 802 | LQ20 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2030 | HYDRAZINE, AQUEOUS SOLUTION with more than 37% hydrazine, by mass | 8 | CT1 | I | 8+6.1 | 298 530 802 | LQ20 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2030 | HYDRAZINE AQUEOUS SOLUTION with more than 37% hydrazine by mass | 8 | CT1 | II | 8+6.1 | 530 802 | LQ22 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2030 | HYDRAZINE AQUEOUS SOLUTION with more than 37% hydrazine by mass | 8 | CT1 | III | 8+6.1 | 530 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2031 | NITRIC ACID, other than red fuming, with more than 70% nitric acid | 8 | CO1 | I | 8+5.1 |  | LQ20 | T | PP, EP |  |  |  |  | 0 |  |
| 2031 | NITRIC ACID, other than red fuming, with not more than 70% nitric acid | 8 | CO1 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 2032 | NITRIC ACID, RED FUMING | 8 | COT | I | 8+5.1+6.1 | 802 | LQ20 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2033 | POTASSIUM MONOXIDE | 8 | C6 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 2034 | HYDROGEN AND METHANE MIXTURE, COMPRESSED | 2 | 1F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2035 | 1,1,1-TRIFLUOROETHANE (REFRIGERANT GAS R 143a) | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2036 | XENON | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 2037 | RECEPTACLES, SMALL, CONTAINING GAS (GAS CARTRIDGES) without a release device, non-refillable | 2 | 5A |  | 2.2 | 191 303 | LQ2 |  | PP |  |  |  |  | 0 |  |
| 2037 | RECEPTACLES, SMALL, CONTAINING GAS (GAS CARTRIDGES) without a release device, non-refillable | 2 | 5F |  | 2.1 | 191 303 | LQ2 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2037 | RECEPTACLES, SMALL, CONTAINING GAS (GAS CARTRIDGES) without a release device, non-refillable | 2 | 5O |  | 2.2+5.1 | 191 303 | LQ2 |  | PP |  |  |  |  | 0 |  |
| 2037 | RECEPTACLES, SMALL, CONTAINING GAS (GAS CARTRIDGES) without a release device, non-refillable | 2 | 5T |  | 2.3 | 303 | LQ1 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2037 | RECEPTACLES, SMALL, CONTAINING GAS (GAS CARTRIDGES) without a release device, non-refillable | 2 | 5TC |  | 2.3+8 | 303 | LQ1 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2037 | RECEPTACLES, SMALL, CONTAINING GAS (GAS CARTRIDGES) without a release device, non-refillable | 2 | 5TF |  | 2.3+2.1 | 303 | LQ1 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2037 | RECEPTACLES, SMALL, CONTAINING GAS (GAS CARTRIDGES) without a release device, non-refillable | 2 | 5TFC |  | 2.3+2.1+8 | 303 | LQ1 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2037 | RECEPTACLES, SMALL, CONTAINING GAS (GAS CARTRIDGES) without a release device, non-refillable | 2 | 5TO |  | 2.3+5.1 | 303 | LQ1 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2037 | RECEPTACLES, SMALL, CONTAINING GAS (GAS CARTRIDGES) without a release device, non-refillable | 2 | 5TOC |  | 2.3+5.1+8 | 303 | LQ1 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2038 | DINITROTOLUENES, LIQUID | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2038 | DINITROTOLUENES, SOLID | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2044 | 2,2-DIMETHYLPROPANE | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2045 | ISOBUTYRALDEHYDE (ISOBUTYL ALDEHYDE) | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2046 | CYMENES | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2047 | DICHLOROPROPENES | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2047 | DICHLOROPROPENES | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2048 | DICYCLOPENTADIENE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2049 | DIETHYLBENZENE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2050 | DIISOBUTYLENE, ISOMERIC COMPOUNDS | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2051 | 2-DIMETHYLAMINO- ETHANOL | 8 | CF1 | II | 8+3 |  | LQ22 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2052 | DIPENTENE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2053 | METHYL ISOBUTYL CARBINOL | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2054 | MORPHOLINE | 8 | CF1 | I | 8+3 |  | LQ20 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2055 | STYRENE MONOMER, STABILIZED | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2056 | TETRAHYDROFURAN | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2057 | TRIPROPYLENE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2057 | TRIPROPYLENE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2058 | VALERALDEHYDE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2059 | NITROCELLULOSE SOLUTION, FLAMMABLE (vapour pressure at 50 °C more than 175 kPa) | 3 | D | I | 3 | 198 531 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2059 | NITROCELLULOSE SOLUTION, FLAMMABLE (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | D | I | 3 | 198 531 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2059 | NITROCELLULOSE SOLUTION, FLAMMABLE (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | D | II | 3 | 198 531 640C | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2059 | NITROCELLULOSE SOLUTION, FLAMMABLE (vapour pressure at 50 °C not more than 110 kPa) | 3 | D | II | 3 | 198 531 640D | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2059 | NITROCELLULOSE SOLUTION, FLAMMABLE | 3 | D | III | 3 | 198 531 | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2067 | AMMONIUM NITRATE FERTILIZERS | 5.1 | O2 | III | 5.1 | 186 193 306 307 | LQ12 | B | PP |  | CO02, ST01, LO04 | HA09 |  | 0 | CO02, LO04 and HA09 apply only when this substance is carried in bulk or without packaging |
| 2071 | Ammonium nitrate fertilizers | 9 | M11 |  |  |  |  | B | PP |  | CO02, ST02 | HA09 |  | 0 | Dangerous only in bulk or without packaging. CO02, ST02 and HA09 apply only when this substance is carried in bulk or without packaging |
| 2073 | AMMONIA SOLUTION, relative density less than 0.880 at 15 °C in water, with more than 35% but not more than 50% ammonia | 2 | 4A |  | 2.2 | 532 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 2074 | ACRYLAMIDE | 6.1 | T2 | III | 6.1 | 802 | LQ9 | T | PP, EP |  |  |  |  | 0 |  |
| 2075 | CHLORAL, ANHYDROUS, STABILIZED | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2076 | CRESOLS, LIQUID | 6.1 | TC1 | II | 6.1+8 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2076 | CRESOLS, SOLID | 6.1 | TC2 | II | 6.1+8 | 802 | LQ18 | T | PP, EP |  |  |  |  | 2 |  |
| 2077 | alpha-NAPHTHYLAMINE | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2078 | TOLUENE DIISOCYANATE | 6.1 | T1 | II | 6.1 | 279 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2079 | DIETHYLENETRIAMINE | 8 | C7 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 2186 | HYDROGEN CHLORIDE, REFRIGERATED LIQUID | 2 | 3TC |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 2187 | CARBON DIOXIDE, REFRIGERATED LIQUID | 2 | 3A |  | 2.2 | 593 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 2188 | ARSINE | 2 | 2TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2189 | DICHLOROSILANE | 2 | 2TFC |  | 2.3+2.1+8 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2190 | OXYGEN DIFLUORIDE, COMPRESSED | 2 | 1TOC |  | 2.3+5.1+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2191 | SULPHURYL FLUORIDE | 2 | 2T |  | 2.3 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2192 | GERMANE | 2 | 2TF |  | 2.3+2.1 | 632 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 2193 | HEXAFLUOROETHANE, COMPRESSED (REFRIGERANT GAS R 116) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 2194 | SELENIUM HEXAFLUORIDE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2195 | TELLURIUM HEXAFLUORIDE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2196 | TUNGSTEN HEXAFLUORIDE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2197 | HYDROGEN IODIDE, ANHYDROUS | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2198 | PHOSPHORUS PENTAFLUORIDE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2199 | PHOSPHINE | 2 | 2TF |  | 2.3+2.1 | 632 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2200 | PROPADIENE, STABILIZED | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2201 | NITROUS OXIDE, REFRIGERATED LIQUID | 2 | 3O |  | 2.2+5.1 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2202 | HYDROGEN SELENIDE, ANHYDROUS | 2 | 2TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2203 | SILANE | 2 | 2F |  | 2.1 | 632 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2204 | CARBONYL SULPHIDE | 2 | 2TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2205 | ADIPONITRILE | 6.1 | T1 | III | 6.1 | 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2206 | ISOCYANATES, TOXIC, N.O.S. or ISOCYANATE SOLUTION, TOXIC, N.O.S. | 6.1 | T1 | II | 6.1 | 274 551 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2206 | ISOCYANATES, TOXIC, N.O.S. or ISOCYANATE SOLUTION, TOXIC, N.O.S. | 6.1 | T1 | III | 6.1 | 274 551 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2208 | CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 10% but not more than 39% available chlorine | 5.1 | O2 | III | 5.1 |  | LQ12 |  | PP |  |  |  |  | 0 |  |
| 2209 | FORMALDEHYDE SOLUTION with not less than 25% formaldehyde | 8 | C9 | III | 8 | 533 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2210 | MANEB or MANEB PREPARATION with not less than 60% maneb | 4.2 | SW | III | 4.2+4.3 | 273 | LQ0 | B | PP, EX, A | VE01, VE03 |  |  | IN01, IN03 | 0 | VE03, IN01 and IN03 apply only when this substance is carried in bulk or without packaging |
| 2211 | POLYMERIC BEADS, EXPANDABLE, evolving flammable vapour | 9 | M3 | III | none | 207 633 | LQ27 | B | PP, EX, EP, A | VE01, VE03 |  |  | IN01 | 0 | VE03 and IN01 apply only when this substance is carried in bulk or without packaging |
| 2212 | BLUE ASBESTOS (crocidolite) or BROWN ASBESTOS (amosite, mysorite) | 9 | M1 | II | 9 | 168 802 | LQ25 |  | PP |  |  |  |  | 0 |  |
| 2213 | PARAFORMALDEHYDE | 4.1 | F1 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2214 | PHTHALIC ANHYDRIDE with more than 0.05% of maleic anhydride | 8 | C4 | III | 8 | 169 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2215 | MALEIC ANHYDRIDE, MOLTEN | 8 | C3 | III | 8 |  | LQ0 | T | PP, EP |  |  |  |  | 0 |  |
| 2215 | MALEIC ANHYDRIDE | 8 | C4 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2216 | Fish meal (Fish scrap), stabilized | 9 | M11 |  |  |  |  | B | PP |  |  |  |  | 0 |  |
| 2217 | SEED CAKE with not more than 1.5% oil and not more than 11% moisture | 4.2 | S2 | III | 4.2 | 142 800 | LQ0 | B | PP |  |  |  | IN01 | 0 | IN01 applies only when this substance is carried in bulk or without packaging |
| 2218 | ACRYLIC ACID, STABILIZED | 8 | CF1 | II | 8+3 |  | LQ22 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2219 | ALLYL GLYCIDYL ETHER | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2222 | ANISOLE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2224 | BENZONITRILE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2225 | BENZENESULPHONYL CHLORIDE | 8 | C3 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2226 | BENZOTRICHLORIDE | 8 | C9 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2227 | n-BUTYL METHACRYLATE, STABILIZED | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2232 | 2-CHLOROETHANAL | 6.1 | T1 | I | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2233 | CHLOROANISIDINES | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2234 | CHLOROBENZOTRI- FLUORIDES | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2235 | CHLOROBENZYL CHLORIDES | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2236 | 3-CHLORO-4-METHYLPHENYL ISOCYANATE | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2237 | CHLORONITROANILINES | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2238 | CHLOROTOLUENES | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2239 | CHLOROTOLUIDINES, liquid | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2239 | CHLOROTOLUIDINES, solid | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2240 | CHROMOSULPHURIC ACID | 8 | C1 | I | 8 |  | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 2241 | CYCLOHEPTANE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2242 | CYCLOHEPTENE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2243 | CYCLOHEXYL ACETATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2244 | CYCLOPENTANOL | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2245 | CYCLOPENTANONE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2246 | CYCLOPENTENE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2247 | n-DECANE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2248 | DI-n-BUTYLAMINE | 8 | CF1 | II | 8+3 |  | LQ22 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2249 | DICHLORODIMETHYL ETHER, SYMMETRICAL | 6.1 | T1 |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 2250 | DICHLOROPHENYL ISOCYANATES | 6.1 | T2 | II | 6.1 | 802 | LQ17 |  | PP, EP |  |  |  |  | 2 |  |
| 2251 | BICYCLO[2.2.1]HEPTA-2,5-DIENE, STABILIZED (2,5-NORBORNADIENE, STABILIZED) | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2252 | 1,2-DIMETHOXYETHANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2253 | N,N-DIMETHYLANILINE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2254 | MATCHES, FUSEE | 4.1 | F1 | III | 4.1 | 293 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2256 | CYCLOHEXENE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2257 | POTASSIUM | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2258 | 1,2-PROPYLENEDIAMINE | 8 | CF1 | II | 8+3 |  | LQ22 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2259 | TRIETHYLENETETRAMINE | 8 | C7 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 2260 | TRIPROPYLAMINE | 3 | FC | III | 3+8 |  | LQ7 |  | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 2261 | XYLENOLS, liquid | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2261 | XYLENOLS, solid | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2262 | DIMETHYLCARBAMOYL CHLORIDE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2263 | DIMETHYLCYCLO- HEXANES | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2264 | N,N-DIMETHYLCYCLO- HEXYLAMINE | 8 | CF1 | II | 8+3 |  | LQ22 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2265 | N,N-DIMETHYL- FORMAMIDE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2266 | DIMETHYL-N-PROPYLAMINE | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2267 | DIMETHYL THIOPHOSPHORYL CHLORIDE | 6.1 | TC1 | II | 6.1+8 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2269 | 3,3'-IMINODIPROPYLAMINE | 8 | C7 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2270 | ETHYLAMINE, AQUEOUS SOLUTION with not less than 50% but not more than 70% ethylamine | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2271 | ETHYL AMYL KETONE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2272 | N-ETHYLANILINE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2273 | 2-ETHYLANILINE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2274 | N-ETHYL-N-BENZYLANILINE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2275 | 2-ETHYLBUTANOL | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2276 | 2-ETHYLHEXYLAMINE | 3 | FC | III | 3+8 |  | LQ7 | T | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 2277 | ETHYL METHACRYLATE, STABILIZED | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2278 | n-HEPTENE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2279 | HEXACHLOROBUTADIENE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2280 | HEXAMETHYLENE- DIAMINE, SOLID | 8 | C8 | III | 8 |  | LQ24 | T | PP, EP |  |  |  |  | 0 |  |
| 2281 | HEXAMETHYLENE DIISOCYANATE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2282 | HEXANOLS | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2283 | ISOBUTYL METHACRYLATE, STABILIZED | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2284 | ISOBUTYRONITRILE | 3 | FT1 | II | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2285 | ISOCYANATOBENZO-TRIFLUORIDES | 6.1 | TF1 | II | 6.1+3 | 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2286 | PENTAMETHYLHEPTANE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2287 | ISOHEPTENE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2288 | ISOHEXENE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2289 | ISOPHORONEDIAMINE | 8 | C7 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2290 | ISOPHORONE DIISOCYANATE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2291 | LEAD COMPOUND, SOLUBLE, N.O.S. | 6.1 | T5 | III | 6.1 | 199 274 535 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2293 | 4-METHOXY-4-METHYLPENTAN-2-ONE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2294 | N-METHYLANILINE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2295 | METHYL CHLOROACETATE | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2296 | METHYLCYCLOHEXANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2297 | METHYLCYCLOHEXANONE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2298 | METHYLCYCLOPENTANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2299 | METHYL DICHLOROACETATE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2300 | 2-METHYL-5-ETHYLPYRIDINE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2301 | 2-METHYLFURAN | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2302 | 5-METHYLHEXAN-2-ONE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2303 | ISOPROPENYLBENZENE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2304 | NAPHTHALENE, MOLTEN | 4.1 | F2 | III | 4.1 | 536 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2305 | NITROBENZENE- SULPHONIC ACID | 8 | C4 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 2306 | NITROBENZO- TRIFLUORIDES, liquid | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2306 | NITROBENZOTRI-FLUORIDES, solid | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2307 | 3-NITRO-4-CHLORO-BENZOTRIFLUORIDE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2308 | NITROSYLSULPHURIC ACID, LIQUID | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2308 | NITROSYLSULPHURIC ACID, SOLID | 8 | C2 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 2309 | OCTADIENE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2310 | PENTANE-2,4-DIONE | 3 | FT1 | III | 3+6.1 | 802 | LQ7 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 2311 | PHENETIDINES | 6.1 | T1 | III | 6.1 | 279 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2312 | PHENOL, MOLTEN | 6.1 | T1 | II | 6.1 | 802 | LQ0 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2313 | PICOLINES | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2315 | POLYCHLORINATED BIPHENYLS | 9 | M2 | II | 9 | 305 802 | LQ29 |  | PP, EP |  |  |  |  | 0 |  |
| 2316 | SODIUM CUPROCYANIDE, SOLID | 6.1 | T5 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2317 | SODIUM CUPROCYANIDE SOLUTION | 6.1 | T4 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2318 | SODIUM HYDROSULPHIDE with less than 25% water of crystallization | 4.2 | S4 | II | 4.2 | 504 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2319 | TERPENE HYDROCARBONS, N.O.S. | 3 | F1 | III | 3 | 274 | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2320 | TETRAETHYLENE- PENTAMINE | 8 | C7 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2321 | TRICHLOROBENZENES, LIQUID | 6.1 | T1 | III | 6.1 | 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2322 | TRICHLOROBUTENE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2323 | TRIETHYL PHOSPHITE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2324 | TRIISOBUTYLENE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2325 | 1,3,5-TRIMETHYLBENZENE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2326 | TRIMETHYLCYCLO- HEXYLAMINE | 8 | C7 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2327 | TRIMETHYLHEXA- METHYLENEDIAMINES | 8 | C7 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2328 | TRIMETHYLHEXAMETHYLENE DIISOCYANATE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2329 | TRIMETHYL PHOSPHITE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2330 | UNDECANE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2331 | ZINC CHLORIDE, ANHYDROUS | 8 | C2 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2332 | ACETALDEHYDE OXIME | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2333 | ALLYL ACETATE | 3 | FT1 | II | 3+6.1 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2334 | ALLYLAMINE | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2335 | ALLYL ETHYL ETHER | 3 | FT1 | II | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2336 | ALLYL FORMATE | 3 | FT1 | I | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2337 | PHENYL MERCAPTAN | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2338 | BENZOTRIFLUORIDE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2339 | 2-BROMOBUTANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2340 | 2-BROMOETHYL ETHYL ETHER | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2341 | 1-BROMO-3-METHYLBUTANE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2342 | BROMOMETHYLPROPANES | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2343 | 2-BROMOPENTANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2344 | BROMOPROPANES | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2344 | BROMOPROPANES | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2345 | 3-BROMOPROPYNE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2346 | BUTANEDIONE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2347 | BUTYL MERCAPTAN | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2348 | BUTYL ACRYLATES, STABILIZED | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2350 | BUTYL METHYL ETHER | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2351 | BUTYL NITRITES | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2351 | BUTYL NITRITES | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2352 | BUTYL VINYL ETHER, STABILIZED | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2353 | BUTYRYL CHLORIDE | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2354 | CHLOROMETHYL ETHYL ETHER | 3 | FT1 | II | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2356 | 2-CHLOROPROPANE | 3 | F1 | I | 3 |  | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2357 | CYCLOHEXYLAMINE | 8 | CF1 | II | 8+3 |  | LQ22 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2358 | CYCLOOCTATETRAENE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2359 | DIALLYLAMINE | 3 | FTC | II | 3+6.1+8 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2360 | DIALLYL ETHER | 3 | FT1 | II | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2361 | DIISOBUTYLAMINE | 3 | FC | III | 3+8 |  | LQ7 |  | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 2362 | 1,1-DICHLOROETHANE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2363 | ETHYL MERCAPTAN | 3 | F1 | I | 3 |  | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2364 | n-PROPYLBENZENE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2366 | DIETHYL CARBONATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2367 | alpha-METHYLVALERALDEHYDE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2368 | alpha-PINENE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2370 | 1-HEXENE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2371 | ISOPENTENES | 3 | F1 | I | 3 |  | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2372 | 1,2-DI-(DIMETHYLAMINO) ETHANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2373 | DIETHOXYMETHANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2374 | 3,3-DIETHOXYPROPENE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2375 | DIETHYL SULPHIDE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2376 | 2,3-DIHYDROPYRAN | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2377 | 1,1-DIMETHOXYETHANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2378 | 2-DIMETHYLAMINO-ACETONITRILE | 3 | FT1 | II | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2379 | 1,3-DIMETHYLBUTYLAMINE | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2380 | DIMETHYLDIETHOXY- SILANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2381 | DIMETHYL DISULPHIDE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2382 | DIMETHYLHYDRAZINE, SYMMETRICAL | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2383 | DIPROPYLAMINE | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2384 | DI-n-PROPYL ETHER | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2385 | ETHYL ISOBUTYRATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2386 | 1-ETHYLPIPERIDINE | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2387 | FLUOROBENZENE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2388 | FLUOROTOLUENES | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2389 | FURAN | 3 | F1 | I | 3 |  | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2390 | 2-IODOBUTANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2391 | IODOMETHYLPROPANES | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2392 | IODOPROPANES | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2393 | ISOBUTYL FORMATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2394 | ISOBUTYL PROPIONATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2395 | ISOBUTYRYL CHLORIDE | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2396 | METHACRYLALDEHYDE, STABILIZED | 3 | FT1 | II | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2397 | 3-METHYLBUTAN-2-ONE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2398 | METHYL tert-BUTYL ETHER | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2399 | 1-METHYLPIPERIDINE | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2400 | METHYL ISOVALERATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2401 | PIPERIDINE | 8 | CF1 | I | 8+3 |  | LQ20 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2402 | PROPANETHIOLS | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2403 | ISOPROPENYL ACETATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2404 | PROPIONITRILE | 3 | FT1 | II | 3+6.1 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2405 | ISOPROPYL BUTYRATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2406 | ISOPROPYL ISOBUTYRATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2407 | ISOPROPYL CHLOROFORMATE | 6.1 | TFC | I | 6.1+3+8 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2409 | ISOPROPYL PROPIONATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2410 | 1,2,3,6-TETRAHYDROPYRIDINE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2411 | BUTYRONITRILE | 3 | FT1 | II | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2412 | TETRAHYDROTHIOPHENE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2413 | TETRAPROPYL ORTHOTITANATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2414 | THIOPHENE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2416 | TRIMETHYL BORATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2417 | CARBONYL FLUORIDE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2418 | SULPHUR TETRAFLUORIDE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2419 | BROMOTRIFLUORO- ETHYLENE | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2420 | HEXAFLUOROACETONE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2421 | NITROGEN TRIOXIDE | 2 | 2TOC |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 2422 | OCTAFLUOROBUT-2-ENE (REFRIGERANT GAS R 1318) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 2424 | OCTAFLUOROPROPANE (REFRIGERANT GAS R 218) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 2426 | AMMONIUM NITRATE, LIQUID, hot concentrated solution, in a concentration of more than 80% but not more than 93% | 5.1 | O1 |  | 5.1 | 252 644 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2427 | POTASSIUM CHLORATE, AQUEOUS SOLUTION | 5.1 | O1 | II | 5.1 |  | LQ10 |  | PP |  |  |  |  | 0 |  |
| 2427 | POTASSIUM CHLORATE, AQUEOUS SOLUTION | 5.1 | O1 | III | 5.1 |  | LQ13 |  | PP |  |  |  |  | 0 |  |
| 2428 | SODIUM CHLORATE, AQUEOUS SOLUTION | 5.1 | O1 | II | 5.1 |  | LQ10 |  | PP |  |  |  |  | 0 |  |
| 2428 | SODIUM CHLORATE, AQUEOUS SOLUTION | 5.1 | O1 | III | 5.1 |  | LQ13 |  | PP |  |  |  |  | 0 |  |
| 2429 | CALCIUM CHLORATE, AQUEOUS SOLUTION | 5.1 | O1 | II | 5.1 |  | LQ10 |  | PP |  |  |  |  | 0 |  |
| 2429 | CALCIUM CHLORATE, AQUEOUS SOLUTION | 5.1 | O1 | III | 5.1 |  | LQ13 |  | PP |  |  |  |  | 0 |  |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 | C4 | I | 8 | 274 | LQ21 |  | PP, EP |  |  |  |  | 0 |  |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 | C4 | II | 8 | 274 | LQ23 | T | PP, EP |  |  |  |  | 0 |  |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 | C4 | III | 8 | 274 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2431 | ANISIDINES | 6.1 | T1 | III | 6.1 | 802 | LQ9 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2432 | N,N-DIETHYLANILINE | 6.1 | T1 | III | 6.1 | 279 802 | LQ9 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2433 | CHLORONITROTOLUENES, LIQUID | 6.1 | T1 | III | 6.1 | 802 | LQ9 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2433 | CHLORONITROTOLUENES, SOLID | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2434 | DIBENZYLDICHLORO- SILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2435 | ETHYLPHENYL- DICHLOROSILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2436 | THIOACETIC ACID | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2437 | METHYLPHENYL- DICHLOROSILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2438 | TRIMETHYLACETYL CHLORIDE | 6.1 | TFC | I | 6.1+3+8 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2439 | SODIUM HYDROGENDIFLUORIDE | 8 | C2 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 2440 | STANNIC CHLORIDE PENTAHYDRATE | 8 | C2 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2441 | TITANIUM TRICHLORIDE, PYROPHORIC or TITANIUM TRICHLORIDE MIXTURE, PYROPHORIC | 4.2 | SC4 | I | 4.2+8 | 537 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2442 | TRICHLOROACETYL CHLORIDE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2443 | VANADIUM OXYTRICHLORIDE | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2444 | VANADIUM TETRACHLORIDE | 8 | C1 | I | 8 |  | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 2445 | LITHIUM ALKYLS | 4.2 | SW | I | 4.2+4.3 | 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2446 | NITROCRESOLS, liquid | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2446 | NITROCRESOLS, solid | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2447 | PHOSPHORUS, WHITE, MOLTEN | 4.2 | ST3 | I | 4.2+6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2448 | SULPHUR, MOLTEN | 4.1 | F3 | III | 4.1 | 538 | LQ0 | T | PP |  |  |  |  | 0 |  |
| 2451 | NITROGEN TRIFLUORIDE | 2 | 2O |  | 2.2+5.1 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2452 | ETHYLACETYLENE, STABILIZED | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2453 | ETHYL FLUORIDE (REFRIGERANT GAS R 161) | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2454 | METHYL FLUORIDE (REFRIGERANT GAS R 41) | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2455 | METHYL NITRITE | 2 | 2A |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 2456 | 2-CHLOROPROPENE | 3 | F1 | I | 3 |  | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2457 | 2,3-DIMETHYLBUTANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2458 | HEXADIENES | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2459 | 2-METHYL-1-BUTENE | 3 | F1 | I | 3 |  | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2460 | 2-METHYL-2-BUTENE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2461 | METHYLPENTADIENE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2463 | ALUMINIUM HYDRIDE | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2464 | BERYLLIUM NITRATE | 5.1 | OT2 | II | 5.1+6.1 | 802 | LQ11 |  | PP |  |  |  |  | 2 |  |
| 2465 | DICHLOROISOCYANURIC ACID, DRY or DICHLOROISOCYANURIC ACID SALTS | 5.1 | O2 | II | 5.1 | 135 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 2466 | POTASSIUM SUPEROXIDE | 5.1 | O2 | I | 5.1 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2468 | TRICHLOROISOCYANURIC ACID, DRY | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 2469 | ZINC BROMATE | 5.1 | O2 | III | 5.1 |  | LQ12 |  | PP |  |  |  |  | 0 |  |
| 2470 | PHENYLACETONITRILE, LIQUID | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2471 | OSMIUM TETROXIDE | 6.1 | T5 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2473 | SODIUM ARSANILATE | 6.1 | T3 | III | 6.1 | 802 | LQ9 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2474 | THIOPHOSGENE | 6.1 | T1 | II | 6.1 | 279 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2475 | VANADIUM TRICHLORIDE | 8 | C2 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2477 | METHYL ISOTHIOCYANATE | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2478 | ISOCYANATES, FLAMMABLE, TOXIC, N.O.S. or ISOCYANATE SOLUTION, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | II | 3+6.1 | 274 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2478 | ISOCYANATES, FLAMMABLE, TOXIC, N.O.S. or ISOCYANATE SOLUTION, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | III | 3+6.1 | 274 802 | LQ7 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 2480 | METHYL ISOCYANATE | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2481 | ETHYL ISOCYANATE | 3 | FT1 | I | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2482 | n-PROPYL ISOCYANATE | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2483 | ISOPROPYL ISOCYANATE | 3 | FT1 | I | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2484 | tert-BUTYL ISOCYANATE | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2485 | n-BUTYL ISOCYANATE | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2486 | ISOBUTYL ISOCYANATE | 3 | FT1 | II | 3+6.1 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2487 | PHENYL ISOCYANATE | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2488 | CYCLOHEXYL ISOCYANATE | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2490 | DICHLOROISOPROPYL ETHER | 6.1 | T1 | II | 6.1 | 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2491 | ETHANOLAMINE or ETHANOLAMINE SOLUTION | 8 | C7 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2493 | HEXAMETHYLENEIMINE | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2495 | IODINE PENTAFLUORIDE | 5.1 | OTC | I | 5.1+6.1+8 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2496 | PROPIONIC ANHYDRIDE | 8 | C3 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2498 | 1,2,3,6-TETRAHYDRO- BENZALDEHYDE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2501 | TRIS-(1-AZIRIDINYL) PHOSPHINE OXIDE SOLUTION | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2501 | TRIS-(1-AZIRIDINYL) PHOSPHINE OXIDE SOLUTION | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2502 | VALERYL CHLORIDE | 8 | CF1 | II | 8+3 |  | LQ22 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2503 | ZIRCONIUM TETRACHLORIDE | 8 | C2 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2504 | TETRABROMOETHANE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2505 | AMMONIUM FLUORIDE | 6.1 | T5 | III | 6.1 | 802 | LQ9 | B | PP, EP |  |  |  |  | 0 |  |
| 2506 | AMMONIUM HYDROGEN SULPHATE | 8 | C2 | II | 8 |  | LQ23 | B | PP, EP |  | CO03 |  |  | 0 | CO03 applies only when this substance is carried in bulk or without packaging |
| 2507 | CHLOROPLATINIC ACID, SOLID | 8 | C2 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2508 | MOLYBDENUM PENTACHLORIDE | 8 | C2 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2509 | POTASSIUM HYDROGEN SULPHATE | 8 | C2 | II | 8 |  | LQ23 | B | PP, EP |  | CO03 |  |  | 0 | CO03 applies only when this substance is carried in bulk or without packaging |
| 2511 | 2-CHLOROPROPIONIC ACID, SOLUTION | 8 | C3 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2511 | 2-CHLOROPROPIONIC ACID, SOLID | 8 | C4 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2512 | AMINOPHENOLS (o-, m-, p-) | 6.1 | T2 | III | 6.1 | 279 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2513 | BROMOACETYL BROMIDE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2514 | BROMOBENZENE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2515 | BROMOFORM | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2516 | CARBON TETRABROMIDE | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2517 | 1-CHLORO-1,1-DIFLUOROETHANE (REFRIGERANT GAS R 142b) | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2518 | 1,5,9-CYCLODODECATRIENE | 6.1 | T1 | III | 6.1 | 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2520 | CYCLOOCTADIENES | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2521 | DIKETENE, STABILIZED | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2522 | 2-DIMETHYLAMINOETHYL METHACRYLATE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2524 | ETHYL ORTHOFORMATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2525 | ETHYL OXALATE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2526 | FURFURYLAMINE | 3 | FC | III | 3+8 |  | LQ7 |  | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 2527 | ISOBUTYL ACRYLATE, STABILIZED | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2528 | ISOBUTYL ISOBUTYRATE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2529 | ISOBUTYRIC ACID | 3 | FC | III | 3+8 |  | LQ7 |  | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 2531 | METHACRYLIC ACID, STABILIZED | 8 | C3 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 2533 | METHYL TRICHLOROACETATE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2534 | METHYLCHLOROSILANE | 2 | 2TFC |  | 2.3+2.1+8 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2535 | 4-METHYLMORPHOLINE (N-METHYLMORPHOLINE) | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2536 | METHYLTETRA-HYDROFURAN | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2538 | NITRONAPHTHALENE | 4.1 | F1 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2541 | TERPINOLENE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2542 | TRIBUTYLAMINE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2545 | HAFNIUM POWDER, DRY | 4.2 | S4 | I | 4.2 | 540 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2545 | HAFNIUM POWDER, DRY | 4.2 | S4 | II | 4.2 | 540 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2545 | HAFNIUM POWDER, DRY | 4.2 | S4 | III | 4.2 | 540 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2546 | TITANIUM POWDER, DRY | 4.2 | S4 | I | 4.2 | 540 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2546 | TITANIUM POWDER, DRY | 4.2 | S4 | II | 4.2 | 540 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2546 | TITANIUM POWDER, DRY | 4.2 | S4 | III | 4.2 | 540 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2547 | SODIUM SUPEROXIDE | 5.1 | O2 | I | 5.1 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2548 | CHLORINE PENTAFLUORIDE | 2 | 2TOC |  | 2.3+5.1+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2552 | HEXAFLUOROACETONE HYDRATE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2554 | METHYLALLYL CHLORIDE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2555 | NITROCELLULOSE WITH WATER (not less than 25% water, by mass) | 4.1 | D | II | 4.1 | 541 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2556 | NITROCELLULOSE WITH ALCOHOL (not less than 25% alcohol, by mass, and not more than 12.6% nitrogen, by dry mass) | 4.1 | D | II | 4.1 | 541 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2557 | NITROCELLULOSE, with not more than 12.6% nitrogen, by dry mass, MIXTURE WITH or WITHOUT PLASTICIZER, WITH or WITHOUT PIGMENT | 4.1 | D | II | 4.1 | 241 541 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2558 | EPIBROMOHYDRIN | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2560 | 2-METHYLPENTAN-2-OL | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2561 | 3-METHYL-1-BUTENE | 3 | F1 | I | 3 |  | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2564 | TRICHLOROACETIC ACID SOLUTION | 8 | C3 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 2564 | TRICHLOROACETIC ACID SOLUTION | 8 | C3 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2565 | DICYCLOHEXYLAMINE | 8 | C7 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2567 | SODIUM PENTACHLOROPHENATE | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2570 | CADMIUM COMPOUND | 6.1 | T5 | I | 6.1 | 274 596 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2570 | CADMIUM COMPOUND | 6.1 | T5 | II | 6.1 | 274 596 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2570 | CADMIUM COMPOUND | 6.1 | T5 | III | 6.1 | 274 596 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2571 | ALKYLSULPHURIC ACIDS | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2572 | PHENYLHYDRAZINE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2573 | THALLIUM CHLORATE | 5.1 | OT2 | II | 5.1+6.1 | 802 | LQ11 |  | PP |  |  |  |  | 2 |  |
| 2574 | TRICRESYL PHOSPHATE with more than 3% ortho isomer | 6.1 | T1 | II | 6.1 | 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2576 | PHOSPHORUS OXYBROMIDE, MOLTEN | 8 | C1 | II | 8 |  | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 2577 | PHENYLACETYL CHLORIDE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2578 | PHOSPHORUS TRIOXIDE | 8 | C2 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2579 | PIPERAZINE | 8 | C8 | III | 8 |  | LQ24 | T | PP, EP |  |  |  |  | 0 |  |
| 2580 | ALUMINIUM BROMIDE SOLUTION | 8 | C1 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2581 | ALUMINIUM CHLORIDE SOLUTION | 8 | C1 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2582 | FERRIC CHLORIDE SOLUTION | 8 | C1 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2583 | ALKYLSULPHONIC ACIDS, SOLID or ARYLSULPHONIC ACIDS, SOLID with more than 5% free sulphuric acid | 8 | C2 | II | 8 | 274 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 2584 | ALKYLSULPHONIC ACIDS, LIQUID or ARYLSULPHONIC ACIDS, LIQUID with more than 5% free sulphuric acid | 8 | C1 | II | 8 | 274 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2585 | ALKYLSULPHONIC ACIDS, SOLID or ARYLSULPHONIC ACIDS, SOLID with not more than 5% free sulphuric acid | 8 | C4 | III | 8 | 274 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2586 | ALKYLSULPHONIC ACIDS, LIQUID or ARYLSULPHONIC ACIDS, LIQUID with not more than 5% free sulphuric acid | 8 | C3 | III | 8 | 274 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2587 | BENZOQUINONE | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2589 | VINYL CHLOROACETATE | 6.1 | TF1 | II | 6.1+3 | 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2590 | WHITE ASBESTOS (chrysotile, actinolite, anthophyllite, tremolite) | 9 | M1 | III | 9 | 168 542 802 | LQ27 |  | PP |  |  |  |  | 0 |  |
| 2591 | XENON, REFRIGERATED LIQUID | 2 | 3A |  | 2.2 | 593 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 2599 | CHLOROTRIFLUORO- METHANE AND TRIFLUOROMETHANE AZEOTROPIC MIXTURE with approximately 60% chlorotrifluoromethane (REFRIGERANT GAS R 503) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 2600 | CARBON MONOXIDE AND HYDROGEN MIXTURE, COMPRESSED | 2 | 1TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2601 | CYCLOBUTANE | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2602 | DICHLORO- DIFLUOROMETHANE AND DIFLUOROETHANE AZEOTROPIC MIXTURE with approximately 74% dichlorodifluoromethane (REFRIGERANT GAS R 500) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 2603 | CYCLOHEPTATRIENE | 3 | FT1 | II | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2604 | BORON TRIFLUORIDE DIETHYL ETHERATE | 8 | CF1 | I | 8+3 |  | LQ20 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2605 | METHOXYMETHYL ISOCYANATE | 3 | FT1 | I | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2606 | METHYL ORTHOSILICATE | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2607 | ACROLEIN DIMER, STABILIZED | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2608 | NITROPROPANES | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2609 | TRIALLYL BORATE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2610 | TRIALLYLAMINE | 3 | FC | III | 3+8 |  | LQ7 |  | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 2611 | PROPYLENE CHLOROHYDRIN | 6.1 | TF1 | II | 6.1+3 | 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2612 | METHYL PROPYL ETHER | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2614 | METHALLYL ALCOHOL | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2615 | ETHYL PROPYL ETHER | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2616 | TRIISOPROPYL BORATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2616 | TRIISOPROPYL BORATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2617 | METHYLCYCLOHEXANOLS, flammable | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2618 | VINYLTOLUENES, STABILIZED | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2619 | BENZYLDIMETHYLAMINE | 8 | CF1 | II | 8+3 |  | LQ22 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2620 | AMYL BUTYRATES | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2621 | ACETYL METHYL CARBINOL | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2622 | GLYCIDALDEHYDE | 3 | FT1 | II | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2623 | FIRELIGHTERS, SOLID with flammable liquid | 4.1 | F1 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2624 | MAGNESIUM SILICIDE | 4.3 | W2 | II | 4.3 |  | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2626 | CHLORIC ACID, AQUEOUS SOLUTION with not more than 10% chloric acid | 5.1 | O1 | II | 5.1 | 613 | LQ10 |  | PP |  |  |  |  | 0 |  |
| 2627 | NITRITES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 103 274 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 2628 | POTASSIUM FLUOROACETATE | 6.1 | T2 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2629 | SODIUM FLUOROACETATE | 6.1 | T2 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2630 | SELENATES or SELENITES | 6.1 | T5 | I | 6.1 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2642 | FLUOROACETIC ACID | 6.1 | T2 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2643 | METHYL BROMOACETATE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2644 | METHYL IODIDE | 6.1 | T1 | I | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2645 | PHENACYL BROMIDE | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2646 | HEXACHLOROCYCLO- PENTADIENE | 6.1 | T1 | I | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2647 | MALONONITRILE | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2648 | 1,2-DIBROMOBUTAN-3-ONE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2649 | 1,3-DICHLOROACETONE | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2650 | 1,1-DICHLORO-1-NITROETHANE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2651 | 4,4'-DIAMINO- DIPHENYLMETHANE | 6.1 | T2 | III | 6.1 | 802 | LQ9 | T | PP, EP |  |  |  |  | 0 |  |
| 2653 | BENZYL IODIDE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2655 | POTASSIUM FLUOROSILICATE | 6.1 | T5 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2656 | QUINOLINE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2657 | SELENIUM DISULPHIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2659 | SODIUM CHLOROACETATE | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2660 | NITROTOLUIDINES (MONO) | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2661 | HEXACHLOROACETONE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2662 | HYDROQUINONE | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2664 | DIBROMOMETHANE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2667 | BUTYLTOLUENES | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2668 | CHLOROACETONITRILE | 6.1 | TF1 | II | 6.1+3 | 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2669 | CHLOROCRESOLS, liquid | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2669 | CHLOROCRESOLS, solid | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2670 | CYANURIC CHLORIDE | 8 | C4 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 2671 | AMINOPYRIDINES (o-, m-, p-) | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2672 | AMMONIA SOLUTION, relative density between 0.880 and 0.957 at 15 °C in water, with more than 10% but not more than 35% ammonia | 8 | C5 | III | 8 | 543 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2673 | 2-AMINO-4-CHLOROPHENOL | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2674 | SODIUM FLUOROSILICATE | 6.1 | T5 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2676 | STIBINE | 2 | 2TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2677 | RUBIDIUM HYDROXIDE SOLUTION | 8 | C5 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2677 | RUBIDIUM HYDROXIDE SOLUTION | 8 | C5 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2678 | RUBIDIUM HYDROXIDE | 8 | C6 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 2679 | LITHIUM HYDROXIDE SOLUTION | 8 | C5 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2679 | LITHIUM HYDROXIDE SOLUTION | 8 | C5 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2680 | LITHIUM HYDROXIDE | 8 | C6 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 2681 | CAESIUM HYDROXIDE SOLUTION | 8 | C5 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2681 | CAESIUM HYDROXIDE SOLUTION | 8 | C5 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2682 | CAESIUM HYDROXIDE | 8 | C6 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 2683 | AMMONIUM SULPHIDE SOLUTION | 8 | CFT | II | 8+3+6.1 | 802 | LQ22 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2684 | 3-DIETHYLAMINO- PROPYLAMINE | 3 | FC | III | 3+8 |  | LQ7 |  | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 2685 | N,N-DIETHYLETHYLENE- DIAMINE | 8 | CF1 | II | 8+3 |  | LQ22 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2686 | 2-DIETHYLAMINO- ETHANOL | 8 | CF1 | II | 8+3 |  | LQ22 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2687 | DICYCLOHEXYL- AMMONIUM NITRITE | 4.1 | F3 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2688 | 1-BROMO-3-CHLOROPROPANE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2689 | GLYCEROL alpha-MONOCHLOROHYDRIN | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2690 | N,n-BUTYLIMIDAZOLE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2691 | PHOSPHORUS PENTABROMIDE | 8 | C2 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 2692 | BORON TRIBROMIDE | 8 | C1 | I | 8 |  | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 2693 | BISULPHITES, AQUEOUS SOLUTION, N.O.S. | 8 | C1 | III | 8 | 274 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2698 | TETRAHYDROPHTHALIC ANHYDRIDES with more than 0.05% of maleic anhydride | 8 | C4 | III | 8 | 169 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2699 | TRIFLUOROACETIC ACID | 8 | C3 | I | 8 |  | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 2705 | 1-PENTOL | 8 | C9 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2707 | DIMETHYLDIOXANES | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2707 | DIMETHYLDIOXANES | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2709 | BUTYLBENZENES | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2710 | DIPROPYL KETONE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2713 | ACRIDINE | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2714 | ZINC RESINATE | 4.1 | F3 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2715 | ALUMINIUM RESINATE | 4.1 | F3 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2716 | 1,4-BUTYNEDIOL | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2717 | CAMPHOR, synthetic | 4.1 | F1 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2719 | BARIUM BROMATE | 5.1 | OT2 | II | 5.1+6.1 | 802 | LQ11 |  | PP |  |  |  |  | 2 |  |
| 2720 | CHROMIUM NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 2721 | COPPER CHLORATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 2722 | LITHIUM NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 2723 | MAGNESIUM CHLORATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 2724 | MANGANESE NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 2725 | NICKEL NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 2726 | NICKEL NITRITE | 5.1 | O2 | III | 5.1 |  | LQ12 |  | PP |  |  |  |  | 0 |  |
| 2727 | THALLIUM NITRATE | 6.1 | TO2 | II | 6.1+5.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2728 | ZIRCONIUM NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 2729 | HEXACHLOROBENZENE | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2730 | NITROANISOLES, LIQUID | 6.1 | T1 | III | 6.1 | 279 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2730 | NITROANISOLES, SOLID | 6.1 | T2 | III | 6.1 | 279 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2732 | NITROBROMOBENZENES, LIQUID | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2732 | NITROBROMOBENZENES, SOLID | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2733 | AMINES, FLAMMABLE, CORROSIVE, N.O.S. or POLYAMINES, FLAMMABLE, CORROSIVE, N.O.S. | 3 | FC | I | 3+8 | 274 544 | LQ3 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2733 | AMINES, FLAMMABLE, CORROSIVE, N.O.S. or POLYAMINES, FLAMMABLE, CORROSIVE, N.O.S. | 3 | FC | II | 3+8 | 274 544 | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2733 | AMINES, FLAMMABLE, CORROSIVE, N.O.S. or POLYAMINES, FLAMMABLE, CORROSIVE, N.O.S. | 3 | FC | III | 3+8 | 274 544 | LQ7 |  | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 2734 | AMINES, LIQUID, CORROSIVE, FLAMMABLE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, FLAMMABLE, N.O.S. | 8 | CF1 | I | 8+3 | 274 | LQ20 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2734 | AMINES, LIQUID, CORROSIVE, FLAMMABLE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, FLAMMABLE, N.O.S. | 8 | CF1 | II | 8+3 | 274 | LQ22 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2735 | AMINES, LIQUID, CORROSIVE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, N.O.S. | 8 | C7 | I | 8 | 274 | LQ20 | T | PP, EP |  |  |  |  | 0 |  |
| 2735 | AMINES, LIQUID, CORROSIVE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, N.O.S. | 8 | C7 | II | 8 | 274 | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 2735 | AMINES, LIQUID, CORROSIVE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, N.O.S. | 8 | C7 | III | 8 | 274 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2738 | N-BUTYLANILINE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2739 | BUTYRIC ANHYDRIDE | 8 | C3 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2740 | n-PROPYL CHLOROFORMATE | 6.1 | TFC | I | 6.1+3+8 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2741 | BARIUM HYPOCHLORITE with more than 22% available chlorine | 5.1 | OT2 | II | 5.1+6.1 | 802 | LQ11 |  | PP |  |  |  |  | 2 |  |
| 2742 | CHLOROFORMATES, TOXIC, CORROSIVE, FLAMMABLE, N.O.S. | 6.1 | TFC | II | 6.1+3+8 | 274 561 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2743 | n-BUTYL CHLOROFORMATE | 6.1 | TFC | II | 6.1+3+8 | 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2744 | CYCLOBUTYL CHLOROFORMATE | 6.1 | TFC | II | 6.1+3+8 | 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2745 | CHLOROMETHYL CHLOROFORMATE | 6.1 | TC1 | II | 6.1+8 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2746 | PHENYL CHLOROFORMATE | 6.1 | TC1 | II | 6.1+8 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2747 | tert-BUTYLCYCLOHEXYL CHLOROFORMATE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2748 | 2-ETHYLHEXYL CHLOROFORMATE | 6.1 | TC1 | II | 6.1+8 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2749 | TETRAMETHYLSILANE | 3 | F1 | I | 3 |  | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2750 | 1,3-DICHLOROPROPANOL-2 | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2751 | DIETHYLTHIO- PHOSPHORYL CHLORIDE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2752 | 1,2-EPOXY-3-ETHOXYPROPANE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2753 | N-ETHYLBENZYL-TOLUIDINES, LIQUID | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2753 | N-ETHYLBENZYL-TOLUIDINES, SOLID | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2754 | N-ETHYLTOLUIDINES | 6.1 | T1 | II | 6.1 | 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2758 | CARBAMATE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2758 | CARBAMATE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2760 | ARSENICAL PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2760 | ARSENICAL PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2762 | ORGANOCHLORINE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2762 | ORGANOCHLORINE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2764 | TRIAZINE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2764 | TRIAZINE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2772 | THIOCARBAMATE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2772 | THIOCARBAMATE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2776 | COPPER BASED PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2776 | COPPER BASED PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2778 | MERCURY BASED PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2778 | MERCURY BASED PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2780 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2780 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2782 | BIPYRIDILIUM PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2782 | BIPYRIDILIUM PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |