## UNITED

NATIONS

Distr.

Economic and Social		GENERAL

Council

TRANS/WP.29/2002/56

20 August 2002

ENGLISH

Original:	ENGLISH

and FRENCH

# ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

(One-hundred-and-twenty-eighth session,

12-15 November 2002, agenda item 5.2.11.)

PROPOSAL FOR DRAFT SUPPLEMENT 5 TO THE 02 SERIES
OF AMENDMENTS TO REGULATION No. 48

(Installation of lighting and light-signalling devices)

Transmitted by the Working Party on Lighting

and Light-Signalling (GRE)

Note:  The text reproduced below was adopted by GRE at its forty-eighth session and is transmitted for consideration to WP.29 and AC.1.  It is based on documents TRANS/WP.29/GRE/2002/8 and TRANS/WP.29/GRE/2002/14, as amended, complemented by a set of Transitional Provisions proposed by an expert from the Working Party "Brussels 1952" (TRANS/WP.29/GRE/48, paras. 19-22).

__________

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraph 6.3.4.2., amend to read:

"6.3.4.2.	In height:

minimum:	Not less than 250 mm above the ground.

maximum:	For M1 and N1 category vehicles not more than 800 mm above the ground;  For all other categories of vehicles no maximum height.

However, no point on the apparent surface in the direction of the reference axis must be higher than the highest point on the apparent surface in the direction of the reference axis of the dipped-beam headlamp."

Paragraphs 6.4. to 6.4.6., amend to read:

"6.4.	REVERSING LAMP

6.4.1.	Presence

Mandatory on motor vehicles and on trailers of categories O2, O3 and O4.  Optional on trailers of category O1.

6.4.2.	Number

6.4.2.1.	One device mandatory and a second device optional on motor vehicles of category M1 and on all other vehicles with a length not exceeding 6000 mm.

6.4.2.2.	Two devices mandatory and two devices optional on all vehicles with a length exceeding 6,000 mm, except vehicles of category M1.

6.4.3.		Arrangement

No special requirement.

6.4.4.	Position

6.4.4.1.	In width:	no special requirement.

6.4.4.2.	In height:	not less than 250 mm and not more than 1,200 mm above the ground.

6.4.4.3.	In length:	at the rear of the vehicle.

However, if installed, the two optional devices mentioned in paragraph 6.4.2.2. shall be fitted on the side or rear of the vehicle, in conformity with the requirements of paragraphs 6.4.5. and 6.4.6.

6.4.5.	Geometric visibility

Defined by angles α and β, as specified in paragraph 2.13.;

α =	15° upwards and 5° downwards,

β =	45° to right and to left if there is only one device,

45° outwards and 30° inwards if there are two.

The reference axis of the two optional devices mentioned in paragraph 6.4.2.2., if fitted on the side of the vehicle shall be orientated sideward horizontally with an inclination of 10°± 5° in relation to the median longitudinal plane of the vehicle.

6.4.6.	Orientation

Rearwards and sideward, as specified in paragraph 6.4.5. above.

All the reversing lamps fitted on the vehicle must not cause undue dazzle or discomfort to other road users."

Paragraph 6.4.7.2., amend to read:

"6.4.7.2.	Moreover, the electrical connections of the two optional devices mentioned in paragraph 6.4.2.2. shall be such that these devices cannot light up unless the lamps referred to in paragraph 5.11. are switched on."

Insert new paragraphs 12.9. to 12.12., to read:

"12.9.	As from the official date of entry into force of Supplement 5 to the 02 series of amendments no Contracting Party applying this Regulation shall refuse to grant approvals under this Regulation as amended by Supplement 5 to the 02 series of amendments.

12.10.	As from 36 months after the date of entry into force of Supplement 5 to the 02 series of amendments Contracting Parties applying this Regulation shall grant approvals only if the vehicle type to be approved meets the requirements of this Regulation as amended by Supplement 5 to the 02 series of amendments.

12.11.	Contracting Parties applying this Regulation shall not refuse to grant extensions of approvals to the preceding series of amendments to this Regulation, including Supplement 4 to the 02 series of amendments.

12.12.	Contracting Parties applying this Regulation shall continue to grant approvals to those vehicle types which comply with the requirements of this Regulation as amended by Supplement 4 to the 02 series of amendments during the 36 months period which follows the official date of entry into force of Supplement 5 to the 02 series of amendments."

__________

# Text boxes

E