Distr.

GENERAL

TRANS/WP.29/GRE/2002/9

25 January 2002

Original: ENGLISH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Lighting and Light-Signalling (GRE)

(Forty-eighth session, 9-12 April 2002,

agenda item 2.7.)

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 98

(Headlamps with gas-discharge light sources)

Transmitted by the Expert from the Working Party "Brussels 1952" (GTB)

Note:  The text reproduced below was prepared by the expert from GTB in order to clarify the measuring procedure in the Regulation, in the case when filament lamps of Regulation No. 37 are used for the driving beam in addition to Regulation No. 99 gas-discharge light source.

_________

Paragraph 6.3.2., amend to read:

"6.3.2.	It is possible to use several light sources for the driving beam, these light sources being listed in either Regulation No. 37 (in this case the filament lamps shall be operated at their reference flux) or Regulation No. 99.  The following provisions shall be met:"

__________

_____________

Note:  This document is distributed to the Experts on Lighting and Light-Signalling only.

GE.02-20379