Distr.

GENERAL

TRANS/WP.29/GRPE/2002/12

4 April 2002

ENGLISH ONLY

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Pollution and Energy (GRPE)

(Forty-fourth session, 10-14 June 2002,

agenda item 4.5.)

PROPOSAL FOR AMENDMENTS TO REGULATION No. 110

(Specific CNG components)

Transmitted by the expert from CLEPA

Note:	The text reproduced below was prepared by the expert from CLEPA in order to introduce some editorial changes to the text of the Regulation.

___________

_______________

Note:  This document is distributed to the Experts on Pollution and Energy only.

A. PROPOSAL

Annex 4B,

Paragraph 1.6.2.2., amend to read:

“1.6.2.2 	The sealing cone of swivel-nut type must be of the type with a half vertical angle of 45°.”

Insert new paragraphs 1.6.2.3. and 1.6.2.4., to read:

“1.6.2.3.	The couplings can be made as swivel-nut type or as quick-connector type.

1.6.2.4.	It shall be impossible to disconnect the quick-connector type without specific measures or the use of dedicated tools.”

Insert new paragraphs 2.6.4. and 2.6.5., to read:

“2.6.4.	The couplings can be made as swivel-nut type or as quick-connector type.

2.6.5.	It shall be impossible to disconnect the quick-connector type without specific measures or the use of dedicated tools.”

*    *    *

###### B.	JUSTIFICATION

The adoption of an alternative architecture of couplings, design as quick-connector type, makes easier the assembling operations and reduces the leakage problems in the manufacturer assembly plant as well during maintenance operations in work-shops.  The safety degree is increased.

______________