Informal document No.  19

(43rd GRPE, 15-18 January 2002,

agenda item 4.2.)

Italian proposal to amend Regulation No. 96, 01 series of amendments,

according to the Polish proposal TRANS/WP.29/GRPE/2001/9  and Add. 1.

Transmitted by the expert from Italy

# Proposal

Annex 1B paragraph 1.7: Amend to read

“0.1.	Fuel system:

pump - line - injector

rotary pump

in-line pump

single element

unit injector”

Annex 1B paragraph 1.9: add missing numbering

“1.9	exhaust after-treatment

oxidation catalyst

reduction catalyst

thermal reactor

particulates trap”

Annex 1B item 3: delete the whole item.

Insert new Annex 1B – Appendix A, to read:

“Annex 1B – Appendix A

ESSENTIAL CHARACTERISTICS OF THE ENGINE FAMILY

1.	COMMON PARAMETERS 1/

1.1.	Combustion cycle:

1.2.	Cooling medium:

1.3.	Method of air aspiration:

1.4.	Combustion chamber type/design:

1.5.	Valve and porting 3/4 configuration, size and number:

1.6.	Fuel system:

1.7.	Engine management systems

Proof of identity pursuant to drawing number(s):

1.7.1.	charge cooling system:

1.7.2.	exhaust gas recirculation 2/:

1.7.3.	water injection/emulsion 2/:

1.7.4.	air injection 2/:

1.8.	Exhaust after-treatment system 2/:

Proof of identical (or lowest for the parent engine) ratio: system capacity/fuel delivery per stroke, pursuant to diagram number(s):

2.	ENGINE FAMILY LISTING

2.1.	Engine family name:

2.2.	Specification of engines within this family:

| Engine Type | No. of cylinders | Rated Speed | Rated Net Power (kW) | Maximum Torque Speed | Maximum Torque | Low Idle Speed |
| --- | --- | --- | --- | --- | --- | --- |
| PARENT ENGINE (FOR FULL DETAILS SEE ANNEX 1A) |

2.3.	In addition, for each engine type within the family, the information required in appendix of this annex shall be submitted to the approval authority.

Re-name the old Annex 1B Appendix to read:

“Annex 1B – Appendix B”

*     *     *

# Justification

The whole proposal is in line with the one presented by the Polish expert in documents Trans/WP.29/GRPE/2001/9  and Add. 1, but it further aligns the text with the one of directive 97/68/EC.

It has been specifically discussed and approved by the Polish and EU Commission experts.

__________