Original:  ENGLISH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Construction of Vehicles

Meeting of Experts on Pollution and Energy (GRPE)

(Forty-fourth session GRPE – 10-14 June 2002, agenda item 4.5.)

PROPOSAL FOR AMENDMENTS TO REGULATION No.110

(Specific components CNG)

Transmitted by the Expert from the Italian delegation

Note: 	The text reproduced below was prepared by Italian Delegation in order to amend the text of Regulation No. 110.

A. PROPOSAL

Annex 3 - Appendix A

Paragraph A.24 ,  (Pressure relief device requirements), amend to read :

…………….

(a) 	One specimen shall be held at a controlled temperature of not less than 95°C and a pressure …………(instead of 100°C)

Annex 3 – Appendix A,

Add a new paragraph. A.28 to read:

“A.28	Manual valve device requirements

One specimen shall be submitted to a fatigue test at a pressure cycling rate not to exceed 4 cycles per minute as follows:

- held at 20 °C while pressured for 2000 cycles between 2 MPa and 26 MPa;

Annex 3 – Appendix D, amend to read:

………….

(d) serial and part number

Annex 4A,

Add a new paragraph 6 to read:

“6	Manual Valve

6.1	The manual valve device in Class 0 shall be designed to withstand a pressure of 1.5 times the working pressure.

  - The manual valve device in Class 0 shall be designed to operate at a temperature from –40°C to 85 °C.

****************

#### B. JUSTIFICATION

Re: Annex 3, Appendix A, A24

The maximum ambient temperature at normal conditions, without fire, is normally considered 90°C in automotive designing for the components on board. Moreover, since PRDs are designed to operate at the temperature of 110 +/- 10 °C, they could melt at 100 °C.

###### Re: Annex  4A, A28

See justification to the previous amendment

#### Re: Annex 3 Appendix D

This editorial amendment is required for consistency reason with Annex 3 – 11. Marking Par. 11.1 …..…

(iv) Cylinder identification (applicable part number and a serial number unique for every cylinder.]

##### Re: Annex 4A, paragraph 6

In the original text there was a lack of prescriptions and the experience revealed the need to provide for them.

-------------------------