Distr.

GENERAL

TRANS/WP.29/GRRF/2002/4

20 November 2001

ORIGINAL: ENGLISH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Brakes and Running Gear (GRRF)

(Fifty-first session, 4–8 February 2002,

agenda item 1.1.)

# PROPOSAL FOR DRAFT CORIGENDUM 1 TO SUPPLEMENT 6 TO THE 09 SERIES OF

# AMENDMENTS TO REGULATION No. 13

(Braking)

Transmitted by the Expert from the European Association

of Automobile Suppliers (CLEPA)

Note:	The text reproduced below was prepared by the expert from CLEPA in order to correct the text of the Regulation.  The text refers to the draft Supplement 6 to the 09 series of amendments to Regulation No. 13, contained in document TRANS/WP.29/793.

____________

_____________

Note:	This document is distributed to the Experts on Brakes and Running Gear only.

GE.01-

Annex 12,

Paragraphs 2.2.26. to 2.2.28., renumber as paragraphs 2.2.28. to 2.2.30.

Paragraph 2.3.6., amend to read:

“..... forward; i.e., Figure 6, graph M = f(P), ..."

Paragraph 2.3.9., amend to read:

“2.3.9.	r:	characteristic of the brake when ...”

Paragraph 5.4.4., amend to read:

"5.4.4.	surface area of the piston in master ...”

Paragraph 5.4.5., amend to read:

“5.4.5.	stroke of the master cylinder 	”

Paragraph 7.4.3.2., amend the symbol “rr'” to read “r’r”

## Annex 12, appendix 2,

Item 8.2., amend to read:

“8.2.	with hydraulic transmission device 1/

....

travel of master cylinder s"Hz  .................... mm

....”

Item 9.7.A., amend to read:

“9.7.A.	Pressure for M*

p*  = ........... N/cm²”

Items 9.10., 9.10.1. and 9.10.1.A., amend to read:

“9.10.	Service brake performance when reversing (see figures 6 and 7 of appendix 1 to this annex)

    - Maximum (figure 6) braking torque Mr = ....................... Nm

9.10.1.A.	Maximum (figure 6) braking torque Mr = ....................... Nm”

Item 9.12.2., amend to read:

“.......

.......

Hot performance = ............................................ %

(expressed as % of brake test Type-0 - see para. 9.12.1 above)

.........”

Annex 13,

Paragraph 4.1., the reference to footnote 12/, and footnote 12/ should read footnote 2/.

# Paragraph 4.1.1., the reference to footnote 15/ and footnote 15/ should read footnote 3/.

# Paragraph 5.2.5., the reference to footnote 16/ and footnote 16/ should read footnote 13/.

# Paragraph 5.3.7., the reference to footnote 16/ should read to footnote 13/.

____________