Informal Document n°  11

( 32nd GRSP, 10-13 Dec 2002

Agenda item B.2 )

CLEPA Proposal for revision to the specifications to the Child restraint system envelopes as specified in TRANS/WP.29/GRSP/2001/15/Rev.2 and the relevant cross references in TRANS/WP.29/GRSP/2001/16/Rev.2

TRANS/WP.29/GRSP/2001/15/Rev.2

- ISOFIX child restraint system size classes and fixtures

Insert new class B1- ISO/F3: Reduced-Height Forward Facing toddler CRS (modified)

A - ISO/F3: Full-Height Forward Facing toddler CRS

B - ISO/F2: Reduced-Height Forward Facing toddler CRS

B1- ISO/F3: Reduced-Height Forward Facing toddler CRS (modified)

C - ISO/R3: Full-Size Rearward Facing toddler CRS

D - ISO/R2: Reduced-Size Rearward Facing toddler CRS

E - ISO/R1: Rearward Facing infant CRS

F – ISO/L1: Left Lateral Facing position CRS (carry-cot)

G - ISO/L2: Right Lateral Facing position CRS (carry-cot)

| Mass group | ISOFIX size class | Fixture (CRF) |
| --- | --- | --- |
| 0 – up to 10 kg | F | ISO/L1 |
|  | G | ISO/L2 |
|  | E | ISO/R1 |
| 0+ - up to 13 kg | C | ISO/R3 |
|  | D | ISO/R2 |
|  | E | ISO/R1 |
| I – 9 to 18 kg | A | ISO/F3 |
|  | B | ISO/F2 |
|  | B1 | ISO/F3 |
|  | C | ISO/R3 |
|  | D | ISO/R2 |

Add new § 4.3 B1- ISO/F3: Reduced-Height Forward Facing toddler CRS (modified)

drawing for Class B1, and renumber existing drawings as 4.4, 4.5, 4.6, 4.7.

Modify all original drawings 4.1 to 4.5, by removing armrest recess, drawing for fixture B attached is typical.

Revise old drawing 4.6 (New 4.7) Lateral facing child restraint systems envelope by correcting dimension 915 to 815 mm.

New 4.3 Reduced height forward-facing toddler child restraint systems envelope

New 4.7 (old 4.6) Lateral facing child restraint systems envelope

VSF-ISOR3

VSF-ISOR2