| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | INF.5 Distr. GENERAL TRANS/WP.15/AC.1/2003/ January 2003 Original: ENGLISH |

### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the

Working Party on the Transport of Dangerous Goods

(Bern, 24-28 March 2003)

# PART 1 OF RID/ADR

Chapter 1.6, Transitional Measures for IBCs

Transmitted by the Expert of Germany

Introduction:

With the implementation of the 2001 revised edition of ADR/RID, IBC shall, in acc. with 6.5.2.1.1 be marked with letters, numerals and symbols at least 12 mm high. The previous edition of ADR/RID did not specify the height of the marking. Transitional provisions for existing design types and IBCs are not provided.

Proposal:

It is proposed to introduce a transitional clause in ADR/RID, Chapter 1.6 in order to clarify the situation. It is proposed, that the revised marking requirements shall apply only to IBC that are manufactured after 31 December 2002, as follows:

1.6.X.X	IBCs manufactured in accordance with the requirements of para. 1612 (1) RID / 3612 (1) ADR applicable up to 31 December 2002 and marked with letters, numerals and symbols less then 12 mm high may be used.

Justification:

The revision of the IBC marking requirements was a consequential alignment with the marking requirements for packages, which had been including provisions on the size of the marking in earlier editions of ADR/RID. This revision was deemed reasonable to achieve the same level of visibility of the marking.

On the other side, an obligation for existing IBCs to be re-marked in the required size would create tremendous difficulties. Millions of IBCs have been put on the market, crossing borders and changing owners and users.

Any re-marking would require that essential questions would need to be addressed, such as:

- Who is authorized to change the marking,

- How can re-marking be organised crossing borders,

- Which elements of the marking need to re-marked,

- Which technical means are allowed in case of embossed or similar markings,

- Is a double marking allowed,

- And others.

# Footnotes

The numbering may require the introduction of a new division for packagings, including IBCs and large packagings, because it is the first clause for this category.