2003-05-11

## Basis for discussion. Comparison between regulations

Working group meeting on RID/ADR, paragraph 1.1.4.2.2, concerning the relationship between all modes of transport with regard to the transport document (Consignment Note)

The information in the table below shows the details that have to be entered in the transport document. The table also consider cases when additional documents must accompany the  transport. These documents often relates to approval, certification etc.. This is the case for all modes of transport. Other circumstances such as different consignor definitions in the regulations have also been highlighted.

State and Operator variations of the ICAO-Ti and IATA-DGR have not been considered in the table. Some of them do require additional text to be added in the document such as emergency response tel. No.

Changes discussed during the current biennium have not been considered.

Comparison between the UN recommendations, 12th Edition, ADR/RID 2003, IMDG Code amdt 31-02, ICAO-TI, 2003-2004 Edition, CFR 49 (parts 100 to 185, revised as of Oct. 1, 2001) and the IATA-DGR, 44th Edition.

| Information in the document | UN Rec. | ADR | RID | IMDG Code | ICAO-TI | CFR 49 | IATA-DGR | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Generally for particulars related to the required sequence with no information interspersed According to the UN Rec., ADR, IMDG Code and ICAO.TI a recommended dangerous goods form is set out. For the IATA-DGR, the form is specified and defined in the IATA-DGR regulations. The language used must be English for the IMDG Code, ICAO-TI And IATA-DGR. For the air mode, the wording in English may be supplemented by an accurate printed translation in any other language. For ADR, in an official language of the forwarding country, and also, if that language is not English, French, or German, in English, French or German. See also para. 5.4.1.4.1 of the ADR. |
| Basic sequence | 2 alternatives are defined (5.4.1.4.2) | Same as UN (5.4.1.1.1) | Same as UN (5.4.1.1.1) | Same as UN (5.4.1.4.2) | Same as UN + a third option which is intended to be deleted from 31 Dec. 2004 (5; 4.1.4.2.1/4.1.4.2.2) |  | Same as ICAO-TI but only one sequence (UNNo. first) from 1 Jan. 2005 as proposed by IATA (8.1.6.9.1) |  |
| UNNo. | Yes, preceded by “UN” (5.4.1.4.1) | Yes, preceded by “UN” (5.4.1.1.1) | Yes, preceded by “UN” (5.4.1.1.1) | Yes, preceded by “UN” (5.4.1.4.1) | Yes, preceded by “UN” (5; 4.1.4.1/3; 2.1.1) |  | Yes, preceded by “UN” (8.1.6.9.1) | 1) |
| PSN (basic) | According to substance list (5.4.1.4.1/3.1.2) | According to substance list (5.4.1.1.1/3.1.2) | According to substance list (5.4.1.1.1/3.1.2) | According to substance list (5.4.1.4.1/3.1.2) | According to substance list (5; 4.1.4.1/3; 1.2) |  | According to substance list (8.1.3/4.1) | 2) |
| Technical names for generic and n.o.s entries | When SP 274 is assigned (3.1.2.8) | When SP 274 is assigned (3.1.2.8) | When SP 274 is assigned (3.1.2.8) | When SP 274 is assigned (5.4.1.4.3/3.1.2.8) | Indicated with a “*” in the substance list (5; 4.1.4.2.2/3; 1.2.7) |  | Indicated with a “(” in the substance list (8.1.3.1/4.1.2.1) | 3) |
| Class | Yes (5.4.1.4.1) | Yes (5.4.1.1.1) | Yes (5.4.1.1.1) | Yes (5.4.1.4.1) | Yes (5; 4.1.4.1/3; 2.1.1) |  | Yes (8.1.6.9.1) | 4) |
| Sub-risk | Yes (5.4.1.4.1) | Yes (5.4.1.1.1) | Yes (5.4.1.1.1) | Yes (5.4.1.4.1) | Yes (5; 4.1.4.1/3; 2.1.1) |  | Yes (8.1.6.9.1) | 5) |
| Packing Group | Yes (5.4.1.4.1) | Yes (5.4.1.1.1) | Yes (5.4.1.1.1) | Yes (5.4.1.4.1) | Yes (5; 4.1.4.1/3; 2.1.1) |  | Yes (8.1.6.9.1) |  |
| Additional “general” information in the transport document |
| Consignor’s name and address | Yes (5.4.1.3) | Yes (5.4.1.1.1) | Not required | Yes (5.4.1.3) | Yes (5; 4.1.3) |  | Yes (8.1.6.1) | 6) |
| Consignee’s name and address | Yes (5.4.1.3) | Yes (5.4.1.1.1) | Not required | Yes (5.4.1.3) | Yes (5; 4.1.3) |  | Yes (8.1.6.2) | 7) |

| Information in the document | UN Rec. | ADR | RID | IMDG Code | ICAO-TI | CFR 49 | IATA-DGR | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Additional “general” information in the transport document (cont.) |
| Date when document prepared | Yes (5.4.1.3) | Not required | Not required | Yes (5.4.1.3) | Yes (5; 4.1.3) |  | Not required | 8) |
| Shipper’s certification | Yes (5.4.1.6) | Not required | Not required | Yes (5.4.1.6) | Yes (5; 4.1.6) |  | Yes (8.1.4.1) |  |
| Number and type of packages | Yes (5.4.1.5.1) ) see also appendix 1 | Yes (5.4.1.1.1) see also appendix 1 | Not required | Yes (5.4.1.5.1) ) see also appendix 1 | Yes (5; 4.1.5.1) ) see also appendix 1 |  | Yes (8.1.6.9.2) ) see also appendix 1 |  |
| Total quantity of dangerous goods | Yes (5.4.1.5.1) | Yes (5.4.1.1.1) | Not required | Yes (5.4.1.5.1) | Yes (5; 4.1.5.1) |  | Yes (8.1.6.9.2) | 9) |
| Airport of Departure | Not required | Not relevant | Not relevant | Not relevant | Not required |  | Yes (8.1.5/8.1.6.6) |  |
| Airport of Destination | Not required | Not relevant | Not relevant | Not relevant | Not required |  | Yes (8.1.5/8.1.6.7) |  |
| Relation to Air Waybill Number | Not required | Not relevant | Not relevant | Not relevant | Not required |  | Yes (8.1.5/8.1.6.3) |  |
| Page of pages | Yes (5.4.1.2.3) | Not required | Not required | Yes (5.4.1.2.3) | Yes (5; 4.1.2.3) |  | Yes (8.1.6.4) |  |
| Flashpoint | Not required | Not required | Not required | Yes, Class 3 (5.4.1.4.3) | Not required |  | Not required |  |
| Empty uncleaned packagings (and tanks) | Yes (5.4.1.4.3) | Yes (5.4.1.1.6) | Yes (5.4.1.1.6) | Yes (5.4.1.4.3) | Yes (5; 4.1.4.3) |  | Yes (8.1.3.10) | 10) |
| “Waste” | Yes (5.4.1.4.3) | Yes (5.4.1.1.3) | Yes (5.4.1.1.3) | Yes (5.4.1.4.3) | Yes (5; 4.1.4.3) |  | Yes (8.1.3.10) | 11) |
| Marine Pollutant | Not required | Not relevant | Not relevant | Yes (5.4.1.4.3) | Not relevant |  | Not relevant |  |
| Elevated temperature subst. | Yes (5.4.1.4.3) | Yes (5.4.1.1.14) | Yes (5.4.1.1.14) | Yes (5.4.1.4.3) | Forbidden |  | Forbidden | 12) |
| Salvage package | Yes (5.4.1.5.3) | Yes (5.4.1.1..5) | Yes (5.4.1.1..5) | Yes (5.4.1.5.3) | Yes (5; 4.1.5.3) |  | Yes (8.1.3.8) |  |
| Limited quantities | Yes (5.4.1.5.2) | Not relevant | Not relevant | Yes (5.4.1.5.2) | Yes (5; 4.1.5.2) |  | Yes (8.1.6.9.4) | 13) |
| Packing instruction No. | Not required | Not required | Not required | Not required | Yes (5; 4.1.5.8.1) |  | Yes (8.1.6.9.3) |  |
| Substances stabilized by temp. control (not 4.1 / 5.2) | Yes (5.4.1.5.4) | Yes (5.4.1.1.15) | Not relevant, forbidden | Yes (5.4.1.5.4) | Forbidden |  | Forbidden |  |
| Cargo or passenger aircraft | Not required | Not relevant | Not relevant | Not relevant | Not required |  | Yes (8.1.6.5) |  |
| Continuous road/rail transport (ADR/RID) after sea or air transport | Not required | Yes (5.4.1.1.7/1.1.4.2) | Yes (5.4.1.1.7/1.1.4.2) | Not relevant | Not relevant |  | Not relevant |  |

| Information in the document | UN Rec. | ADR | RID | IMDG Code | ICAO-TI | CFR 49 | IATA-DGR | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Additional “general” information in the transport document (cont.) |
| Overpack is used | Not required | Not required | Not required | Not required | Yes (4.1.5.8.1) |  | Yes (8.1.6.9.3) |  |
| Emergency response information | Yes (5.4.3) or additional document | Additional document (5.4.3) | Not required | Yes (5.4.3.2) but in practice EmS Guide on Ships | Additional document (7; 4.8) on board the aircraft |  | Additional document (9.5.1.2) on board the aircraft |  |
| When IMO tanks are used (ADR/RID) | Not relevant | Yes (5.4.1.1.8) | Yes (5.4.1.1.8) | Not relevant | Not relevant |  | Not relevant |  |
| Combi-traffic (ADR/RID) | Not considered | See RID | Yes (5.4.1.1.9) | Not considered | Not considered |  | Not considered |  |
| Additions such as “liquid/solid”, “mixture/solution”, “molten”, “stabilized” when missing in the PSN | Yes (3.1.2.3-6) | Yes (3.1.2.3-6) | Yes (3.1.2.3-6) | Yes (3.1.2.4-6) | Yes (3; 1.2.3-5) |  | Yes (78.1.3.6, 8.1.3.2, 8.1.3.3, 8.1.3.9) |  |
| Additional or special information required for Class 1, Class 2, Self-reactive Substances of Class 4.1, Organic Peroxides of Class 5.2, Class 6.2 and Class 7 |
| Class 1 |
| Net explosive mass | Yes (5.4.1.5.1) | Yes (5.4.1.2.1) | Yes (5.4.1.2.1) | Yes (5.4.1.5.1) | Not required |  | Not required | 14) |
| Additional commercial name allowed | Yes (3.1.2.8.1) | Yes (5.4.1.2.1) | Yes (5.4.1.2.1) | Yes (3.1.2.3) | Yes (5; 4.1.4.2.2) |  | Yes (8.1.3) |  |
| Approval for n.o.s.-entries or samples and use of P101 | Yes, SP 16 and 178 and (4.1.4 / P101) | Additional document (5.4.1.2.1) and statement for P101 | Additional document (5.4.1.2.1) and statement for P101 | Yes, 5.4.1.5.9/4.1.5.18) | Yes, for P101 (5; 4.1.5.8.2) |  | Yes, for P101 (8.1.6.9.4)) |  |
| Protective container | Not considered | Additional document (5.4.1.2.1) | Additional document (5.4.1.2.1) | Not considered | Not considered |  | Not considered |  |
| Fireworks of UN Nos. 0333, 0334, 0335, 0336 and 0337 | Not required | Yes (5.4.1.2.1) | Yes (5.4.1.2.1) | Not required | Not required |  | Not required |  |

| Information in the document | UN Rec. | ADR | RID | IMDG Code | ICAO-TI | CFR 49 | IATA-DGR | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Additional or special information required for Class 1, Class 2, Self-reactive Substances of Class 4.1, Organic Peroxides of Class 5.2, Class 6.2 and Class 7 (cont.) |
| Class 1 (cont.) |
| Explosive substances for which a minimum water or phlegmatizer content is specified in the individual entry is prohibited when containing less water or phlematizer than the specified minimum | Not required | Not required | Not required | Yes (5.4.1.5.9) | Not required |  | Not required |  |
| Class 2 |
| Aerosols above 1000 ml | Not required | Not required | Not required | Yes (5.4.1.5.8) | Not required |  | Not required | 16) |
| Composition of mixtures as percentage of the volume (not receptacles) | Not required | Yes (5.4.1.2.2) | Yes (5.4.1.2.2) | Not required | Not required |  | Not required |  |
| Transport of receptacles for testing | Not required | Yes (5.4.1.2.2) | Yes (5.4.1.2.2) | Not required | Not required |  | Not required |  |
| Transport of cryogenic gases in tanks | Not required | Not required | Yes (5.4.1.2.2) | Not required | Not required |  | Not required |  |
| Class 4.1 |
| control temp /emergency temp. | Yes (5.4.1.5.5) | Yes (5.4.1.2.3.1) | Not relevant, forbidden | Yes (5.4.1.5.5) | Not relevant, forbidden |  | Not relevant, forbidden | 15) |
| label conforming to model No. 1 is not required | Yes (5.4.1.5.5.1) | Yes (5.4.1.2.3.2) | Yes (5.4.1.2.3.2) | Yes (5.4.1.5.5.1) | Not considered |  | Not considered |  |

| Information in the document | UN Rec. | ADR | RID | IMDG Code | ICAO-TI | CFR 49 | IATA-DGR | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Additional or special information required for Class 1, Class 2, Self-reactive Substances of Class 4.1, Organic Peroxides of Class 5.2, Class 6.2 and Class 7 (cont.) |
| Class 4.1 (cont.) |
| Self-reactive substances- Protected from direct sun light etc.. | Not required | Not required | Not required | Not required | Yes (4.1.5.8.3) |  | Yes (8.1.6.11) |  |
| When approval is required | Yes (5.4.1.5.5.2) + additional document | Yes (5.4.1.2.3.3) + additional document | Yes (5.4.1.2.3.3) + additional document | Yes (5.4.1.5.5.2) + additional document | Yes (5; 4.1.5.5.1) + additional document |  | Yes (8.1.6.9.4) + additional document |  |
| Transport of sample | Yes (5.4.1.5.5.3) | Yes (5.4.1.2.3.4) | Yes (5.4.1.2.3.4) | Yes (5.4.1.5.5.3) | Yes (5; 4.1.5.5.2) |  | Yes (8.1.6.11.2) |  |
| Not a self-reactive substance (type G) | Not required | Yes (5.4.1.2.3.5) (optional) | Yes (5.4.1.2.3.5) (optional) | Not required | Not required |  | Not required |  |
| Class 5.2 |
| control temp /emergency temp. | Yes (5.4.1.5.5) | Yes (5.4.1.2.3.1) | Not relevant, forbidden | Yes (5.4.1.5.5) | Not relevant, forbidden |  | Not relevant, forbidden | 15) |
| Self-reactive substances- Protected from direct sun light etc.. | Not required | Not required | Not required | Not required | Yes (4.1.5.8.3) |  | Yes (8.1.6.11) |  |
| When approval is required | Yes (5.4.1.5.5.2) + additional document | Yes (5.4.1.2.3.3) + additional document | Yes (5.4.1.2.3.3) + additional document | Yes (5.4.1.5.5.2) + additional document | Yes (5; 4.1.5.5.1) + additional document |  | Yes (8.1.6.9.4) + additional document |  |
| Transport of sample | Yes (5.4.1.5.5.3) | Yes (5.4.1.2.3.4) | Yes (5.4.1.2.3.4) | Yes (5.4.1.5.5.3) | Yes (5; 4.1.5.5.2) |  | Yes (8.1.6.11.2) |  |
| Not an organic peroxide (type G) | Not required | Yes (5.4.1.2.3.5) (optional) | Yes (5.4.1.2.3.5) (optional) | Not required | Not required |  | Not required |  |
| Class 6.2 |
| Full address of consignee and name and Phone No. of a responsible person | Yes (5.4.1.5.6) | Not required | Not required | Yes (5.4.1.5.6) | Yes (5; 4.1.5.6) |  | Yes (8.1.6.2) |  |
| Advanced arrangements with the consignee | Not required | Not required | Not required | Not required | Not required |  | Yes (8.1.6.11.3/1.3.3.1) |  |

| Information in the document | UN Rec. | ADR | RID | IMDG Code | ICAO-TI | CFR 49 | IATA-DGR | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Additional or special information required for Class 1, Class 2, Self-reactive Substances of Class 4.1, Organic Peroxides of Class 5.2, Class 6.2 and Class 7 (cont.) |
| Class 6.2 (cont.) |
| Genetically modified substance | Not required | Yes (5.4.1.2.4) | Yes (5.4.1.2.4) | Not required | Not required |  | Not required |  |
| Easily perishable substance | Not required | Yes (5.4.1.2.4) | Not required | Not required | Not required |  | Not required |  |
| Class 7 |
| Name or symbol of each radionuclide or, for mixtures, a general description or a list | Yes (5.4.1.5.7.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.5.7.1) | Yes (5; 4.1.5.7.1) |  | Yes (10.8.3.9.2) |  |
| Description of the physical and chemical form or a notation with regards to special form or low dispersible material | Yes (5.4.1.5.7.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.5.7.1) | Yes (5; 4.1.5.7.1) |  | Yes (10.8.3.9.2) |  |
| Maximum activity of the radioactive content | Yes (5.4.1.5.7.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.5.7.1) | Yes (5; 4.1.5.7.1) |  | Yes (10.8.3.9.2) |  |
| Activity of each radionuclide in the same package | Not required | Not required | Not required | Not required | Not required |  | Yes (10.8.3.9.2) |  |
| Category of the package | Yes (5.4.1.5.7.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.5.7.1) | Yes (5; 4.1.5.7.1) |  | Yes (10.8.3.9.3) |  |
| Transport index | Yes (5.4.1.5.7.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.5.7.1) | Yes (5; 4.1.5.7.1) |  | Yes (10.8.3.9.3) |  |
| The criticality safety index (incl. fissile material) | Yes (5.4.1.5.7.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.5.7.1) | Yes (5; 4.1.5.7.1) |  | Yes (10.8.3.9.3) |  |
| Identification mark if applicable | Yes (5.4.1.5.7.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.5.7.1) | Yes (5; 4.1.5.7.1) |  | Yes (10.8.3.9.4) |  |
| “All packed in one” | Not required | Not required | Not required | Not required | Not required |  | Yes (10.8.3.9.2) |  |

| Information in the document | UN Rec. | ADR | RID | IMDG Code | ICAO-TI | CFR 49 | IATA-DGR | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Additional or special information required for Class 1, Class 2, Self-reactive Substances of Class 4.1, Organic Peroxides of Class 5.2, Class 6.2 and Class 7 (cont.) |
| Class 7 (cont.) |
| For consignments in overpacks or freight containers | Yes (5.4.1.5.7.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.5.7.1) | Yes (5; 4.1.5.7.1) |  | Yes (10.8.3.9.2) |  |
| Shipped under exclusive use | Yes (5.4.1.5.7.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.5.7.1) | Yes (5; 4.1.5.7.1) |  |  |  |
| For LSA-II, LSA-III, SCO-I, SCO-II, Total activity | Yes (5.4.1.5.7.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.5.7.1) | Yes (5; 4.1.5.7.1) |  | Yes (10.8.3.9.2) |  |
| Statement regarding actions by the carrier | Yes (5.4.1.5.7.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.2.5.1) | Yes (5.4.1.5.7.1) | Yes (5; 4.1.5.7.2) |  | Not required |  |

| Miscellaneous | UN Rec. | ADR | RID | IMDG Code | ICAO-TI | CFR 49 | IATA-DGR | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Various differences |
| Container/vehicle packing certificate | Yes (only for sea transport) (5.4.2.1) | Yes (only for container prior to sea transport (5.4.2) | Yes (only for container prior to sea transport (5.4.2) | Yes (5.4.2.1) | Not required |  | Not required | 17) |
| Viscous <23C substances to be placed in PG III | Yes (2.3.2.2/2.3.2.3) | Yes (2.2.3.1.4) | Yes (2.2.3.1.4) | Yes (2.3.2.2/2.3.2.3)) | Yes (2; 3.2.2/3.2.3) |  | Yes (3.3.3/3.3.3.1) |  |
| Viscous substances not dangerous goods if less than 450 l | Yes (2.3.2.5) | Yes (2.2.3.1.5) | Yes (2.2.3.1.5) | No, see (2.3.2.5). Valid for max. 30 l and a statement in the declaration | No |  | No |  |
| According to SP 640 | Not required | Yes (5.4.1.1.16) |  | Not required | Not required |  | Not required |  |
| Consignor definition | Any person, organization or government which prepares a consignment for transport (1.2.1) | See Note | See Note | Any person, organization or government which prepares a consignment for transport (1.2.1) | Not defined |  | Not defined | 18) |

# Explanation of the figures in the column “Notes”

1)	ICAO-TI and IATA-DGR uses ID 8000 “Consumer commodities” in addition to the UNNos.

2)	The use of upper case or lower case is optional. In the ADR/RID this is specifically expressed.

3)	Has not been checked if the “*” and “(” exactly correspond to SP 274. However, see tables below.

4)	The ADR relate to label model numbers due to the differences with regards to class 2. The ADR does not indicate division 2.1, 2.2 and 2.3

while other modes do. The result in the transport document is the same.

5)	Enclosed in brackets – all modes of transport

6)	It has been recognised in the IATA-DGR that the name and address of the consignor, which appears on the Declaration form may differ from

that on the Air Waybill (8.1.6.1). Compare with CIM Waybill and the CMR Waybill.

7)	It has been recognised in the IATA-DGR that the name and address of the consignee, which appears on the Declaration form may differ from

that on the Air Waybill (8.1.6.2). Compare with CIM Waybill and the CMR Waybill.

8)	IATA-DGR, not to be mixed up with the signing of the Shipper’s certification (where the date appears)

9)	See Annex 1 for the very detailed requirements of the IATA-DGR regarding quantity of dangerous goods being carried by air.

10)	Dangerous goods of classes other than class 7.

11)	Other than radioactive wastes.

12)	According to the UN rec., ADR and the IMDG Code the word “HOT” shall be added if the PSN does not cover the elevated state of the

substance. Transport by air of elevated temperature substances is forbidden. The ICAO-TI and the IATA-DGR cover only molten substances.

13)	Transport by air: The quantities of different dangerous goods contained in one outer packaging must be such that “Q” does not exceed the value

of 1 where “Q” is calculated using the formula:

Q=

where: n1, n2 etc. are the net quantities per package of the dangerous goods and M1, M2, etc. are the maximum net quantities per package

permitted for these excepted quantity dangerous goods permitted for the appropriate packing group by 2.7.5.2.

The following dangerous goods do not need to be taken into account in the calculation of the Q-value:

(a)  carbon dioxide, solid (dry ice), UN 1845; and

(b)  those with the same UN number, packing group and physical state (i.e. solid or liquid), providing they are the only dangerous goods in the

package and the total net quantity does not exceed the maximum net quantity according to 2.7.5.2.

14)	For air transport the “net quantity of explosives” per package must be added (IATA-DGR para. 7.1.5.1). According to the ADR, the transport

document shall indicate, in addition to the requirements in 5.4.1.1.1 (g): - the total net mass, in kg, of explosive contents for each substance or

article bearing a different UN number; - the total net mass, in kg, of explosive contents for all substances and articles covered by the transport document. For sea transport the total quantity of the net explosive mass shall be added.

15)	Only to be transported by air under special permission.

16)	IMDG Code: The information in the transport document for aerosols below 1000 ml shall be classified as Class 2 only (3.4.6.2).

17)	The Container/Vehicle Packing Certificate is integrated into the recommended multi-modal form.

18)	the enterprise which consigns dangerous goods either on its own behalf or for a third party. If the transport operation is carried out under a contract for carriage, consignor means the consignor according to the contract for carriage;

###### Annex 1

### QUANTITY OF DANGEROUS GOODS

IATA-DGR, 44th Edition, Para. 8.1.6.9.2

8.1.6.9.2	Second Sequence—Quantity and Type of Packing

Step 6. Number of packages (of same type and content), their type of packaging (either in full or by the use of the UN Packaging Specification Code, for example: “Fibreboard box”, “Box, fibreboard”, “4G”), and:

(a)  except for empty uncleaned packagings, where a maximum quantity per package is shown in Columns H, J or L of Subsection 4.2 -- List of Dangerous Goods, the net quantity (including the unit of measurement as shown in Columns H, J or L abbreviated or in full, or multiples thereof) in each package in weight or volume, or the gross weight if applicable, of each item of dangerous goods bearing a different Proper Shipping Name, UN/ID number or packing group must be shown;

(b)  where the maximum quantity per package is shown as “No Limit” or has a packing instruction reference in Columns H, J or L of the List of Dangerous Goods, the net quantity of the hazard contained in each package or the gross weight of each article or package must be shown;

(c)  for chemical kits or first aid kits, the total net quantity (including the unit of measure) of dangerous goods must be shown. The net weight of liquids within the kits are to be calculated on a 1 to 1 basis of their volume, i.e. 1 L equal to 1 kg;

(d)  for “Dangerous goods in machinery or apparatus” the individual total quantities of dangerous goods in solid, liquid or gaseous state, contained in the article must be shown;

(e)  when two or more different items of dangerous goods are packed in the same outer packaging, the words “All Packed in One (description of package type)” must immediately follow the relevant entries. If the shipment contains more than one package, each containing the same assortment and quantities of compatible commodities, then the statement immediately following the relevant entries must read:

“All Packed in One (insert description of package type) x ....”. (insert the actual number of packages.)

(f)  when two or more different items of dangerous goods are packed in the same outer packaging in accordance with 5.0.2.11 or 5.0.3.2, the “Q” value rounded up to the first decimal place;

(g)  for dangerous goods transported in Salvage Packagings, an estimate of the remaining quantity must be entered and the words “SALVAGE PACKAGE” must be included.

Note: 	For shipments of explosives to/from Europe, in addition to the net quantity of explosives, it is recommended that the “Net Explosive Quantity” in kilograms (kg) per package be shown. The net explosive quantity refers only to the quantity of explosive substances.

Step 7. When an overpack is used, the wording “Overpack Used” must be inserted on the declaration form immediately after all the relevant entries relating to the packages within each overpack. In such cases, packages within overpacks must be listed first.

(	multiple overpacks with identical contents shall be identified as follows: “Overpack

Used x (number of identical overpacks)”.

Note:	See Figure 8.1.M, (Example 9).

- multiple overpacks with different contents shall be identified by listing them separately.

Note:	See Figure 8.1.N, (Example 10) for operator requirements when offering multi-

overpacks containing different quantities of dangerous goods.

ADR version 2003

Paragraph	5.4.1.1.1

(f) the total quantity of each item of dangerous goods bearing a different UN number, proper shipping name or, when applicable, packing group (as a volume or as a gross mass, or as a net mass as appropriate);

NOTE: In the case of intended application of 1.1.3.6, the total quantity of dangerous

goods for each transport category shall be indicated in the transport document in

accordance with 1.1.3.6.3.

UN Recommendations 12th Edition, para. 5.4.1.5.1

ICAO-TI 2003-2004 Edition, para. 5; 4.1.5.1

IMDG Code, Amdt 31-02, para. 5.4.1.5.1

Total quantity of dangerous goods

Except for empty uncleaned packagings, the total quantity of dangerous goods covered by the description (by volume or mass as appropriate) of each item of dangerous goods bearing a different Proper Shipping Name, UN Number or packing group shall be included. For Class 1 dangerous goods, the quantity shall be the net explosive mass. For dangerous goods transported in salvage packagings, an estimate of the quantity of dangerous goods shall be given. The number and kind  (e.g. drum, box, etc) of packagings shall also be indicated. Abbreviations may be used to specify the unit of measurement for the total quantity.

Annex 2

## Hamburg RID/ADR Working Group – 10-1 June 2003

# The purpose with this document is to highlight differences between the regulations having an impact on harmonized documentation. Please note that these entries are only a few examples and that there are many entries in the various regulations that differ in a similar way. Consideration has not been taken to current work during the present biennium except for UN Nos. 1268, 2319 and 3295 of the ADR/RID where SP 274 will be deleted

# SOME DIFFERENCES WITH REGARD TO PROPER SHIPPING NAMES, including text in lower case and P Groups.

| UN No. | UN 12 Edition | ADR 2003 | IMDG CODE 31-02 | ICAO-TI 2003-2004 | IATA-DGR 44 |
| --- | --- | --- | --- | --- | --- |
| 0209 | TNT, WETTED; dry or wetted with less than 30% water, by mass | TNT, WETTED; dry or wetted with less than 30% water, by mass | TNT, WETTED; dry or wetted with less than 30% water, by mass | TNT, WETTED; dry or wetted with less than 30% water, by mass (Forbidden) | TNT (Forbidden) |
| 3366 | TNT, WETTED; with not less than 10% water, by mass (PG I) | TNT; wetted with not less than 10% water, by mass (PG I) | TNT, WETTED; with not less than 10% water, by mass (PG I) | TNT; not less than 10% water, by mass (PG II) | TNT, WETTED; with more than 10% but less than 30% water, by weight (PG I) |
| 1354 | TRINITROBENZENE, WETTED; with not less than 30% water, by mass (PG I) | TRINITROBENZENE, WETTED; with not less than 30% water, by mass (PG I) | TRINITROBENZENE, WETTED; with not less than 30% water, by mass (PG I) | TRINITROBENZENE, WETTED; with not less than 30% water, by mass (PG I) | TRINITROBENZENE, WETTED; with 30% or more water, by weight (PG I) |
| 3367 | TRINITROBENZENE, WETTED; with not less than 10% water, by mass (PG I) | TRINITROBENZENE, WETTED; with not less than 10% water, by mass (PG I) | TRINITROBENZENE, WETTED; with not less than 10% water, by mass (PG I) | TRINITROBENZENE, WETTED; with not less than 10% water, by mass (PG II) | TRINITROBENZENE, WETTED; with more than 10% but less than 30% water, by weight (PG I) |
| 3368 | TRINITROBENZOIC ACID, WETTED; with not less than 10% water, by mass (PG I) | TRINITROBENZOIC ACID, WETTED; with not less than 10% water, by mass (PG I) | TRINITROBENZOIC ACID, WETTED; with not less than 10% water, by mass (PG I) | TRINITROBENZOIC ACID, WETTED; with not less than 10% water, by mass (PG II) | TRINITROBENZOIC ACID, WETTED; with more than 10% but less than 30% water, by weight (PG I) |

| UN No. | UN 12 Edition | ADR 2003 | IMDG CODE 31-02 | ICAO-TI 2003-2004 | IATA-DGR 44 |
| --- | --- | --- | --- | --- | --- |
| 3369 | SODIUM DINITRO-o-CRESOLATE WETTED; with not less than 10% water, by mass (PG I) | SODIUM DINITRO-o-CRESOLATE WETTED; with not less than 10% water, by mass (PG I) | SODIUM DINITRO-o-CRESOLATE WETTED; with not less than 10% water, by mass (PG I) | SODIUM DINITRO-o-CRESOLATE WETTED; with not less than 10% water, by mass (PG II) | SODIUM DINITRO-o-CRESOLATE, WETTED; with more than 10% but less than 15% water, by mass (PG I) |
| 3370 | UREA NITRATE, WETTED; with not less than 10% water, by mass (PG I) | UREA NITRATE, WETTED; with not less than 10% water, by mass (PG I) | UREA NITRATE, WETTED; with not less than 10% water, by mass (PG I) | UREA NITRATE, WETTED; with not less than 10% water, by mass (PG II) | UREA NITRATE, WETTED; with more than 10% but less than 20% water, by weight (PG I) |
| 1788 | HYDROBROMIC ACID (PG II/III) | HYDROBROMIC ACID (PG II/III) | HYDROBROMIC ACID (PG II/III) | HYDROBROMIC ACID; not more than 49% strength (PG II/III) | HYDROBROMIC ACID; 49% or less strength (PG II/III) |
| 1790 | HYDROFLUORIC ACID; solution, with more than 60% hydrofluoric acid (PG I) | - | HYDROFLUORIC ACID; solution, with more than 60% hydrofluoric acid (PG I) | HYDROFLUORIC ACID; more than 60% strenght (PG I) | HYDROFLUORIC ACID; more than 60% strenght (PG I) |
| 1790 | - | HYDROFLUORIC ACID; with more than 60% but not more than 85% hydrofluoric acid; more than 60% (PG I) | - | - | - |
| 1790 | - | HYDROFLUORIC ACID; with more than 85% hydrofluoric acid (PG I) | - | - | - |
| 1265 | PENTANES; liquid (PG II) | PENTANES; liquid (PG II) | PENTANES, LIQUID (PG II) | PENTANES; liquid (PG II) | PENTANES; liquid (PG II) |
| 1278 | 1-CHLOROPROPANE (PG II) | 1-CHLOROPROPANE (PG II) | 1-CHLOROPROPANE (PG II) | 1-CHLOROPROPANE (PG II) | PROPYL CHLORIDE (PG II) |

| UN No. | UN 12 Edition | ADR 2003 | IMDG CODE 31-02 | ICAO-TI 2003-2004 | IATA-DGR 44 |
| --- | --- | --- | --- | --- | --- |
| 2014 | HYDROGEN PEROXIDE, AQUEOUS SOLUTION; with not less than 20% but not more than 60% hydrogen peroxide (stabilized as necessary) (PG II) | HYDROGEN PEROXIDE, AQUEOUS SOLUTION; with not less than 20% but not more than 60% hydrogen peroxide (stabilized as necessary) (PG II) | HYDROGEN PEROXIDE, AQUEOUS SOLUTION; with not less than 20% but not more than 60% hydrogen peroxide (stabilized as necessary) (PG II) | HYDROGEN PEROXIDE, AQUEOUS SOLUTION; with not less than 20% but not more than 40% hydrogen peroxide (stabilized as necessary) (PG II) | HYDROGEN PEROXIDE, AQUEOUS SOLUTION; with not less than 20% but not more than 40% hydrogen peroxide (stabilized as necessary) (PG II) |
| 2431 | ANISIDINES (PG III) | ANISIDINES (PG III) | ortho-ANISIDINE (PG III) | ANISIDINES LIQUID/SOLID(PG III) | ANISIDINES LIQUID/SOLID(PG III) |
| 2669 | CHLOROCRESOLS (PG II) | CHLOROCRESOLS; liquid/solid (PG II) | CHLOROCRESOLS SOLUTION/SOLID(PG II) | CHLOROCRESOLS LIQUID/SOLID (PG II) | CHLOROCRESOLS LIQUID/SOLID (PG II) |

### TABLE SHOWING DIFFERENCES WITH REGARD TO PSN and TECHNICAL NAMES

The ADR/RID column show the UN Nos. requiring technical names not required by UN Recommendations, 12th Edition.

| ADR/RID version 2003 | IATA_DGR 44th Version | IMDG Code Amdt 31-02 | Comments |
| --- | --- | --- | --- |
| CLASS 1 | UN Nos. | CLASS 1 | UN Nos. | CLASS 1 | UN Nos. | * No technical name required - in line with UN Recommendations 12th Edition |
| Division 1.3 | 0132 | Division 1.3 | 0132* | Division 1.3 | 0132* |  |
| CLASS 2 | 1075 | CLASS 2 | 1075* | CLASS 2 | 1075* |  |
|  | 3167 |  | 3167* |  | 3167* |  |
|  | 3168 |  | 3168* |  | 3168* |  |
|  | 3169 |  | 3169* |  | 3169* |  |
| CLASS 3 | 1268 | CLASS 3 | 1268* | CLASS 3 | 1268* |  |
|  | 2319 |  | 2319* |  | 2319* |  |
|  | 2985 |  | 2985* |  | 2985* |  |
|  | 3248 |  | 3248* |  | 3248* |  |
|  | 3256 |  | 3256* |  | 3256* |  |
|  | 3295 |  | 3295* |  | 3295* |  |
| CLASS 4 |  | CLASS 4 |  | CLASS 4 |  |  |
| Division 4.1 | 1353 | Division 4.1 | 1353* | Division 4.1 | 1353* |  |
| Division 4.1 | 1373 | Division 4.1 | 1373* | Division 4.1 | 1373* |  |

| ADR/RID version 2003 | IATA_DGR 44th Version | IMDG Code Amdt 31-02 | Comments |
| --- | --- | --- | --- |
| CLASS 4 | UN Nos. | CLASS 4 | UN Nos. | CLASS 4 | UN Nos. | * No technical name required - in line with UN Recommendations 12th Edition |
| Division 4.3 | 1389 | Division 4.3 | 1389* | Division 4.3 | 1389* |  |
|  | 1390 |  | 1390* |  | 1390* |  |
|  | 1391 |  | 1391* |  | 1391* |  |
|  | 1392 |  | 1392* |  | 1392* |  |
|  | 1393 |  | 1393* |  | 1393* |  |
|  | 1421 |  | 1421* |  | 1421* |  |
|  | 2988 |  | 2988* |  | 2988* |  |
| CLASS 5 |  | CLASS 5 |  | CLASS 5 |  |  |
| Division 5.1 | 1450 | Division 5.1 | 1450* | Division 5.1 | 1450* |  |
|  | 1461 |  | 1461* |  | 1461* |  |
|  | 1462 |  | 1462* |  | 1462* |  |
|  | 1477 |  | 1477* |  | 1477* |  |
|  | 1481 |  | 1481* |  | 1481* |  |
|  | 1482 |  | 1482* |  | 1482* |  |
|  | 1483 |  | 1483* |  | 1483* |  |
|  | 2627 |  | 2627* |  | 2627* |  |
|  | 3210 |  | 3210* |  | 3210* |  |
|  | 3211 |  | 3211* |  | 3211* |  |
|  | 3212 |  | 3212* |  | 3212* |  |
|  | 3213 |  | 3213* |  | 3213* |  |

| ADR/RID version 2003 | IATA_DGR 44th Version | IMDG Code Amdt 31-02 | Comments |
| --- | --- | --- | --- |
| CLASS 5 | UN Nos. | CLASS 5 | UN Nos. | CLASS 5 | UN Nos. | * No technical name required - in line with UN Recommendations 12th Edition |
| Division 5.1 | 3214 | Division 5.1 | 3214* | Division 5.1 | 3214* |  |
|  | 3215 |  | 3215* |  | 3215* |  |
|  | 3216 |  | 3216* |  | 3216* |  |
|  | 3218 |  | 3218* |  | 3218* |  |
|  | 3219 |  | 3219* |  | 3219* |  |
| CLASS 6 |  | CLASS 6 |  | CLASS 6 |  |  |
| Division 6.1 | 1549 | Division 6.1 | 1549* | Division 6.1 | 1549* |  |
|  | 1556 |  | 1556* |  | 1556* |  |
|  | 1557 |  | 1557* |  | 1557* |  |
|  | 1564 |  | 1564* |  | 1564* |  |
|  | 1566 |  | 1566* |  | 1566* |  |
|  | 1583 |  | 1583* |  | 1583* |  |
|  | 1655 |  | 1655* |  | 1655* |  |
|  | 1707 |  | 1707* |  | 1707* |  |
|  | 1851 |  | 1851* |  | 1851* |  |
|  | 1935 |  | 1935* |  | 1935* |  |
|  | 2024 |  | 2024* |  | 2024* |  |
|  | 2025 |  | 2025* |  | 2025* |  |
|  | 2026 |  | 2026* |  | 2026* |  |
|  | 2291 |  | 2291* |  | 2291* |  |
|  | 2570 |  | 2570* |  | 2570* |  |
|  | 2630 |  | 2630* |  | 2630* |  |
|  | 2742 |  | 2742* |  | 2742* |  |

| ADR/RID version 2003 | IATA_DGR 44th Version | IMDG Code Amdt 31-02 | Comments |
| --- | --- | --- | --- |
| CLASS 6 | UN Nos. | CLASS 6 | UN Nos. | CLASS 6 | UN Nos. | No technical name required - in line with UN Recommendations 12th Edition "2788, 3146 / IATA-DGR" No technical name required - Required in UN Recommendations 12th Edition. |
| Division 6.1 | ---- | Division 6.1 | 2788 | Division 6.1 | ---- |  |
|  | 2856 |  | 2856* |  | 2856* |  |
|  | 3048 |  | 3048* |  | 3048* |  |
|  | 3141 |  | 3141* |  | 3141* |  |
|  | 3144 |  | 3144* |  | 3144* |  |
|  | ---- |  | 3146 |  | ---- |  |
|  | 3249 |  | 3249* |  | 3249* |  |
|  | 3283 |  | 3283* |  | 3283* |  |
|  | 3284 |  | 3284* |  | 3284* |  |
|  | 3285 |  | 3285* |  | 3285* |  |
|  | 3361 |  | 3361* |  | 3361* |  |
|  | 3362 |  | 3362* |  | 3362* |  |
| CLASS 8 | 1740 | CLASS 8 | 1740* | CLASS 8 | 1740* | No technical name required - in line with UN Recommendations 12th Edition "2693 / IATA-DGR" No technical name - Required in UN Recommendations 12th Edition. "2571 / ADR" No technical name required - Required in UN Recommendations 12th Edition. |
|  | 2430 |  | 2430* |  | 2430* |  |
|  | 2571 |  | ---- |  | ---- |  |
|  | 2583 |  | 2583* |  | 2583* |  |
|  | 2584 |  | 2584* |  | 2584* |  |
|  | 2585 |  | 2585* |  | 2585* |  |
|  | 2586 |  | 2586* |  | 2586* |  |
|  | ---- |  | 2693 |  | ---- |  |
|  | 2837 |  | 2837* |  | 2837* |  |
|  | 2986 |  | 2986* |  | 2986* |  |
|  | 2987 |  | 2987* |  | 2987* |  |
|  | 3145 |  | 3145* |  | 3145* |  |
| CLASS 9 | 3257 | CLASS 9 | 3257* | CLASS 9 | 3257* | No technical name required - in line with UN Recommendations 12th Edition |
|  | 3258 |  | 3258* |  | 3258* |  |