INF.30/Add.3 E/Rev.1

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the

Working Party on the Transport of Dangerous Goods

(Bern, 24-28 March 2003)

HARMONIZATION WITH THE UNITED NATIONS

MODEL REGULATIONS ON THE TRANSPORT OF DANGEROUS GOODS

Draft proposal of amendments to Part 3 of RID/ADR/ADN

Prepared by the UNECE secretariat

NOTE:	The proposal is based on ST/SG/AC.10/29/Add.1.

Stricken out text means that the amendment does not seem relevant for RID/ADR/ADN.

Text underlined means alternative wording proposed by the secretariat.

Text in square brackets means that the relevance of the text for RID/ADR/ADN should be discussed by the Working Group of the Joint Meeting.

PART 3

#### Chapter 3.1

3.1.2.2 (b)	Replace the existing text with the following:

"UN 2793 FERROUS METAL BORINGS, SHAVINGS, TURNINGS or CUTTINGS in a form liable to self-heating. The proper shipping name is the most appropriate of the following combinations:

FERROUS METAL BORINGS

FERROUS METAL SHAVINGS

FERROUS METAL TURNINGS

FERROUS METAL CUTTINGS"

3.1.2.4	Replace the existing paragraph with the following text:

"3.1.2.4		Many substances have an entry for both the liquid and solid state (see definitions for liquid and solid in 1.2.1), or for the solid and solution. These are allocated separate UN numbers which are not necessarily adjacent to each other. Details are provided in the alphabetical index, e.g.:

NITROXYLENES, LIQUID	6.1	1665

NITROXYLENES, SOLID	6.1	3447"

3.1.2.7	Replace "included" with "transported carried".

3.1.2.8.1	Replace "their technical" with "the technical" in the first sentence.

3.1.2.8.1.3	Replace "UN 2003 METAL ALKYL, WATER-REACTIVE, N.O.S (trimethylgallium)" with "UN 3394 ORGANOMETALLIC SUBSTANCE, LIQUID, PYROPHORIC, WATER-REACTIVE  (trimethylgallium)".

### Chapter 3.2

3.2.1	Column (2)	Add the following sentence at the end of the existing text:

"Unless otherwise indicated for an entry in the dangerous goods list, the word "solution" in a proper shipping name means one or more named dangerous goods dissolved in a liquid that is not otherwise subject to these Regulations.".

Column (10)	Add the following sentence at the end of the existing text first paragraph:

"Bulk container code - a code including the letters "BK" refers to types of [bulk containers] used for the transport carriage of [bulk goods] described in Chapter 6.8 11."

Dangerous Goods List Table A

Amend the heading applicable to columns (10) and (11) to read: "UN Portable tanks and bulk containers". Amend the heading of column (10), to read "Instructions" and the heading of column (11) to read "Special provisions".

UN Nos. 2014, 2427, 2428, 2429, 2626, 2984, 3098, 3099, 3139, 3149, 3210, 3211, 3213, 3214, 3216, 3218 , and 3219, replace "kg" with "L" in column 7.

Delete “TP13” in column (11) everywhere it appears (RID/ADR).

Delete “TE1” in column (11) everywhere it appears (RID/ADR).

For UN Nos. No. 1611, 1704, 2936 replace "500 g" with "100 ml" in column 7, "P002 IBC08" with "P001 IBC02" in column (8), delete "B2, B4" in column (9a) and add "T7" and "TP2" in columns (10) and (11) respectively.

For UN Nos 1611 and 1704, add “T7” and “TP24” in column (10) and (11) respectively.

For UN Nos. 1003, 1038, 1073, 1913, 1951, 1961, 1963, 1966, 1970, 1972, 1977, 2187, 2201, 2591, 3136, 3138, 3158, 3311 and 3312, replace "P200" with "P203" in column (8).

In the Dangerous Goods List, assign "TP5" in column (11) to each refrigerated liquid gas that is assigned "T75" in column (10). (Apply to UN Nos. 1003, 1038, 1073, 1913, 1951, 1961, 1963, 1966, 1970, 1972, 1977, 2187, 2201, 2591, 3136, 3138, 3158, 3311 and 3312).

For UN Nos 0331, 0332 and 3375, insert "T1" in column (10) and "TP1", "TP17" and "TP32" in column (11).

For UN Nos 1334, 1350, 1438, 1454, 1474, 1486, 1495, 1498, 1499, 1942, 2067, 2213, 2969, 3170 (PG II and III), 3175, 3243 and 3244, insert "BK1, BK2" in column (10) and for UN Nos. 1376, 1408 and 2950, insert "BK2" in the same column.

For the liquid, packing group I entries of UN Nos. 1583, 2810, 2927, 2929, 3122, 3123, 3275, 3276, 3278, 3279, 3280, 3281, 3287 and 3289, insert "315" in column (6).

For all the UN Nos. containing the words "fissile-excepted" in lower case in column (2), insert "317" in column (6). (Apply to UN Nos.: 2912, 2913, 2915, 2916, 2917, 2919, 2978, 3321, 3322, 3323 and 3332).

For UN Nos. 1366, 1370, 2005, 2445, 3051, 3052, 3053 and 3076, add "320" in column (6).

UN No. 1010	Add the following text at the end of the existing name in column (2) Replace the text in lower case at the end of the description in column (2) with:

"or BUTADIENES AND HYDROCARBON MIXTURE, STABILIZED, containing more than 40% butadienes".

UN No. 1057	Replace "P003 P205" with "P002" in column (8) and add "PP84" in column (9a).

UN No. 1203	The amendment does not apply to the English version.

UN No. 1389	Add ", LIQUID" in column (2), replace “W2” with “W1” in column (3b) and (for RID/ADR) delete "P403 IBC04" in column (8). Delete “B1” in column (9a).

UN No. 1392	Add ", LIQUID" in column (2), replace “W2” with “W1” in column (3b) and (for RID/ADR) delete "P403, IBC04" in column (8) and delete "B1" in column (9a).

UN No. 1408	(for RID/ADR) Insert "B6" in column (9a).

UN No. 1420	Add ", LIQUID" in column (2), replace “W2” with “W1” in column (3b) and (for RID/ADR) replace "P403, IBC04" with "P402" in column (8) and delete "B1" in column (9a).

UN No. 1422	Add ", LIQUID" in column (2), replace “W2” with “W1” in column (3b) and (for RID/ADR) replace "P403, IBC04" with "P402" in column (8) and delete "B1" in column (9a).

UN No. 1445	Add ", SOLID" in column (2).

UN No. 1447	Add ", SOLID" in column (2).

UN No. 1459	Add ", SOLID" in column (2).

UN No. 1470	Add ", SOLID" in column (2).

UN No. 1578	Add Change case of ", SOLID solid" in column (2).

UN No. 1579	Add ", SOLID" in column (2).

UN No. 1605	(for RID/ADR) Replace "P601" with "P602" in column (8).

UN No. 1650	Add ", SOLID" in column (2).

UN No. 1680	Add ", SOLID" in column (2).

UN No. 1689	Add ", SOLID" in column (2) and delete "B1" in column 9.

UN No. 1690	Add ", SOLID" in column (2).

UN No. 1697	Add ", SOLID" in column (2), replace “T1” with “T2“ in column (3b). “LQ17” with “LQ18” in column (7), (RID/ADR) “L4BN” with “SGAN” in column (12), (RID only) “CE5” with “CE9” in column (19).

UN No. 1701	Add ", LIQUID" in column (2).

UN No. 1709	Add ", SOLID" in column (2).

UN No. 1729	Replace “C3” with “C4” in column (4) and “LQ22” with “LQ23” in column (7). (for RID/ADR) Replace "L" with "kg" in column 7 and  "P001 IBC02" with "P002 IBC08" in column (8), insert "B2, B4" in column (9a), replace “MP152 with “MP10” in column (9b), and replace "T7" with "T3" and "TP2" with "TP33" in columns (10) and (11), respectively and Insert “SGAN” before “L4BN” in column (12). (RID only) Replace “CE6” with “CE10” in column (19).

UN No. 1742	Add ", LIQUID" in column (2).

UN No. 1743	Add ", LIQUID" in column (2).

UN No. 1744		Add "PP82" in column (9a).

UN No. 1748	(PGIII)	Add "PP85" in column (9a).

UN No. 1793 	(for RID/ADR) Replace "kg" with "L" and "P002 [IBC08] [IBC03] LP02" with "P001 IBC02 LP01" in columns 7 and 8 respectively and delete "B3" in column 9.

UN No. 1805	In column (2), replace "LIQUID" with "SOLUTION" and add "223" in column (6).

UN No. 1811	Amend the name in column (2) to read "POTASSIUM HYDROGENDIFLUORIDE SOLID".

UN No. 1812	Add ", SOLID" in column (2).

UN No. 1843	Add ", SOLID" in column (2) and (for RID/ADR) delete "T7" and "TP2" in columns (10) and (11) respectively.

UN 1931	Replace "NONE" with "5 kg" in column 7.

UN No. 1963	(for RID/ADR) Add "TP34" in column (11).

UN No. 1966	(for RID/ADR) Add "TP34" in column (11).

UN No. 2003	Delete.

UN No. 2014	Add "PP10" and delete "PP29" in column (9a).

UN No. 2074	Add ", SOLID" in column (2).

UN No. 2077	(for RID/ADR) Replace "T3" and "TP1" with "T1" and "TP33" in columns (10) and (11) respectively.

UN 2186	Insert "P099" in column (8).

UN No. 2208	Insert "313" and "314" in column (6) and (for RID/ADR) "PP85" and "B13" in column 9.

UN 2211	Replace "NONE" with "5 kg" in column 7.

UN No. 2235	Add ", LIQUID" in column (2) and replace “T2” with “T1” in column (3b) and “LQ9” with “LQ19” in column (7). (RID/ADR) Replace “MP10” with “MP15” in column (9b), delete “SGAN” in column (12) and “VW9/VV9” in column (17). (RID only) Replace “CE11” with “CE8”.

UN No. 2236	Add ", LIQUID" in column (2) and replace “T2” with “T1” in column (3b) and “LQ18” with “LQ17” in column (7). (RID/ADR) Replace “MP10” with “MP15” in column (9b) and delete “SGAN” in column (12). (RID only) Replace “CE9” with “CE5”.

UN No. 2239	Add Change case of ", SOLID solid" in column (2). Delete the “liquid” entry.

UN No. 2261	Add Change case of ", SOLID solid" in column (2). Delete the “liquid” entry.

UN No. 2305	(for RID/ADR) Replace "L" with "kg" in column 7, "P001 IBC02" with "P002 IBC08" in column (8) and add "B2, B4" in column 9a and Add "T3", "TP33" in columns (10) and (11) respectively.

UN No. 2306	Add Change case of ", LIQUID liquid" in column (2). Delete the “solid” entry.

UN No. 2315	Add ", LIQUID" in column (2).

UN 2439 	 Replace "L" with "kg" in column 7.

UN No. 2445	Add ", LIQUID" in column (2).

UN No. 2446	Add Change case of ", SOLID" in column (2).

UN No. 2511 first entry	Delete ", SOLUTION" in column (2) and insert "223" in column (6).

Delete the entry for "2-CHLOROPROPIONIC ACID, SOLID".

UN No. 2552	Add ", LIQUID" in column (2).

UN No. 2662	Add ", SOLID" in column (2).

UN No. 2669	Delete the solid entry.

UN No. 2729	(for RID/ADR) Replace "L" with "kg" in column 7, "P001 IBC03 LP01" with "P002 IBC08 LP02" in column (8), and add "B3", "T1" and "TP33" in columns 9, 10 and (11) respectively.

UN 2751	Replace "kg" with "L" in column 7, "P002 IBC08" with "P001 IBC02" in column (8) and delete "B2 B4" in column 9.

UN No. 2813	(for RID/ADR) For packing groups I, II and III, add "PP83" in column (9a).

UN No. 2814	Delete "274" and add "318" in column (6).

UN No. 2823	(for RID/ADR) Replace "L" with "kg" in column 7 and "P001 IBC03 LP01" with "P002 IBC08 LP02" in column (8).

UN 2851	Replace "kg" with "L" in column 7 and "P002 IBC08" with "P001 IBC02" in column (8) and delete "B2 B4" in column 9.

UN No. 2857	Amend the name in column (2) to read as follows:  "REFRIGERATING MACHINES containing non-flammable, non-toxic gases or ammonia solutions (UN 2672)".

UN No. 2880 (PGIII)	Add "PP85" in column (9).

UN No. 2900	Delete "274" and add "318" in column (6) and add "BK1 BK2" in column (10).

UN No. 2937	Add ", LIQUID" in column (2).

UN No. 2956	Delete "181" in column (6).

UN No. 3049	Delete.

UN No. 3050	Delete.

UN No. 3052	(for the “LIQUID” entry of RID/ADR) Add "TP9" in column (11).

UN 3082	Replace "kg" with "L" in column 7.

UN 3125	(Packing group II) Replace "P001" with "P002" in column (8).

UN No. 3149	(for RID/ADR) Add "PP10" in column (9a).

UN 3166	Add "312" in column (6).

UN No. 3176	(for RID/ADR) Delete "TP9" in column (11) ([2 entries]).

UN No. 3203	Delete ([2 entries]).

UN No. 3207	Delete ([3 entries]).

UN No. 3276	Amend the name in column (2) to read as follows: "NITRILES, TOXIC, LIQUID, N.O.S". (3 entries)

UN No. 3278	For the liquid entry entries, amend the name in column (2) to read as follows: "ORGANOPHOSPHORUS COMPOUND, TOXIC, LIQUID, N.O.S"(3 entries). Delete the solid entries.

UN No. 3280	For the liquid entries, amend the name in column (2) to read as follows: "ORGANOARSENIC COMPOUND, LIQUID, N.O.S" (3 entries). Delete the solid entries.

UN No. 3281	For the liquid entries, amend the name in column (2) to read as follows: "METAL CARBONYLS, LIQUID, N.O.S" (3 entries). Delete the solid entries.

UN No. 3282	For the liquid entries, amend the name in column (2) to read as follows: "ORGANOMETALLIC COMPOUND, TOXIC, LIQUID, N.O.S" (3 entries). Delete the solid entries.

UN No. 3283	Amend the name in column (2) to read as follows: "SELENIUM COMPOUND, SOLID, N.O.S" (3 entries).

UN 3314	Replace "NONE" with "5 kg" in column 7.

UN No. 3315	In column (2), delete ", liquid or solid".

UN No. 3372	Delete (3 entries).

UN No. 3373	In the name in column (2), insert "or CLINICAL" before "SPECIMENS" and add "319" in column (6).

UN No. 3375	Delete "306" in column (6).

UN 3378 (PGIII)	Delete "PP84" and ", B13" in column (9) and add "BK1 BK2" in column (10).

Assign TP9 to all N.O.S entries of Classes 4.2, 6.1 and 8, packing group I to which a T code has been assigned in column (10).

Amend the following entries to read as follows:

| UN No. | Name and description | Class | Classification Code | Packing group | Labels | Special provisions | Limited quantities | Packagings | UN Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special packing provisions | Mixed packing provisions | Portable tank instruction | Portable tank special provisions |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) |
| 1597 | DINITROBENZENES LIQUID | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 |
| 1597 | DINITROBENZENES LIQUID | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T7 | TP2 |
| 1656 | NICOTINE HYDROCHLORIDE, LIQUID or SOLUTION | 6.1 | T1 | II | 6.1 | 43 | LQ17 | P001 IBC02 |  | MP15 |  |  |
| 1656 | NICOTINE HYDROCHLORIDE, LIQUID or SOLUTION | 6.1 | T1 | III | 6.1 | 43 | LQ19 | P001 IBC03 LP01 R001 |  | MP15 |  |  |
| 1658 | NICOTINE SULPHATE SOLUTION | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 |
| 1658 | NICOTINE SULPHATE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T7 | TP2 |
| 1748 | CALCIUM HYPOCHLORITE, DRY or CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 39% available chlorine (8.8% available oxygen) | 5.1 | O2 | II | 5.1 | 313 314 589 | LQ11 | P002 IBC08 | PP85 B4, B13 | MP10 |  |  |
| 1748 | CALCIUM HYPOCHLORITE, DRY or CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 39% available chlorine (8.8% available oxygen) | 5.1 | O2 | III | 5.1 | 316 589 | LQ12 | P002 IBC08 | B4 | MP10 |  |  |
| 1835 | TETRAMETHYL-AMMONIUM HYDROXIDE SOLUTION | 8 | C7 | II | 8 |  | LQ22 | P001 IBC02 |  | MP15 | T7 | TP2 |
| 1835 | TETRAMETHYL-AMMONIUM HYDROXIDE SOLUTION | 8 | C7 | III | 8 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T7 | TP2 |
| 1938 | BROMOACETIC ACID SOLUTION | 8 | C3 | II | 8 |  | LQ22 | P001 IBC02 |  | MP15 | T7 | TP2 |
| 1938 | BROMOACETIC ACID SOLUTION | 8 | C3 | III | 8 |  | LQ19 | P001 IBC02 LP01 R001 |  | MP15 | T7 | TP2 |
| 2669 | CHLOROCRESOLS SOLUTION | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 |
| 2669 | CHLOROCRESOLS SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T7 | TP2 |
| 2880 | CALCIUM HYPOCHLORITE, HYDRATED or CALCIUM HYPOCHLORITE HYDRATED MIXTURE, with not less than 5.5% but not more than 16% water | 5.1 | O2 | II | 5.1 | 313 314 | LQ11 | P002 IBC08 | PP85 B4, B13 | MP10 |  |  |
| 2880 | CALCIUM HYPOCHLORITE, HYDRATED or CALCIUM HYPOCHLORITE HYDRATED MIXTURE, with not less than 5.5% but not more than 16% water | 5.1 | O2 | III | 5.1 | 316 | LQ12 | P002 IBC08 | B4 | MP10 |  |  |

Add the following new entries:

(Note: When two UN numbers appear in column (1) of the table below, the number in italics corresponds to a current entry in the Dangerous Goods List Table A for the same substance in solid, liquid or solution state and is given only for reference.).

| UN No. | Name and description | Class | Classification Code | Packing group | Labels | Special provisions | Limited quantities | Packagings and IBCs | UN Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special provisions | Mixed packing provisions | Instructions | Special provisions |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) |
| 3377 | SODIUM PERBORATE MONOHYDRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | P002 IBC08 LP02 R001 | B3 | [MP2] [MP10] | T1 BK1 BK2 | TP33 |
| 3378 | SODIUM CARBONATE PEROXYHYDRATE | 5.1 | O2 | II | 5.1 |  | LQ11 | P002 IBC08 | B4 | [MP2] [MP10] | T3 BK1 BK2 | TP33 |
| 3378 | SODIUM CARBONATE PEROXYHYDRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | P002 IBC08 LP02 | B3 BK1 BK2 | [MP2] [MP10] | T1 BK1 BK2 | TP33 |
| 3379 | DESENSITIZED EXPLOSIVE, LIQUID, N.O.S. | 3 | D | I | 3 | 274 311 | [LQ0] [LQ3] | P099 |  | MP2 |  |  |
| 3380 | DESENSITIZED EXPLOSIVE, SOLID, N.O.S. | 4.1 | D | I | 4.1 | 274 311 | LQ0 | P099 |  | MP2 |  |  |
| 3381 | TOXIC BY INHALATION LIQUID, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | 6.1 | [T1] [T4] | I | 6.1 | 274 | LQ0 | P601 |  | [MP8] [MP17] | T22 | TP2 TP9 TP13 |
| 3382 | TOXIC BY INHALATION LIQUID, N.O.S. with an inhalation toxicity toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | 6.1 | [T1] [T4] | I | 6.1 | 274 | LQ0 | P602 |  | [MP8] [MP17] | T20 | TP2 TP9 TP13 |
| 3383 | TOXIC BY INHALATION LIQUID, FLAMMABLE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | 6.1 | TF1 | I | 6.1 +3 | 274 | LQ0 | P601 |  | [MP8] [MP17] | T22 | TP2 TP9 TP13 |
| 3384 | TOXIC BY INHALATION LIQUID, FLAMMABLE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | 6.1 | TF1 | I | 6.1 +3 | 274 | LQ0 | P602 |  | MP8 MP17 | T20 | TP2 TP9 TP13 |

| ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identification No. | UN No. | Name and description |
| --- | --- | --- | --- | --- | --- | --- |
| Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |  |  |
| (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) | (1) | (2) |
| [SGAN] [SGAV] | TU3 | AT | 3 |  | [VV8] | CV24 |  | 50 | 3377 | SODIUM PERBORATE MONOHYDRATE |
| [SGAN] [SGAV] | TU3 | AT | 2 | V11 | [VV8] | CV24 |  | 50 | 3378 | SODIUM CARBONATE PEROXYHYDRATE |
| [SGAN] [SGAV] | TU3 | AT | 3 |  | [VV8] | CV24 |  | 50 | 3378 | SODIUM CARBONATE PEROXYHYDRATE |
|  |  |  | 1 |  |  |  | S2 S20 | (RID 33) | 3379 | DESENSITIZED EXPLOSIVE, LIQUID, N.O.S. |
|  |  |  | 1 |  |  |  | S17 | (RID ?) | 3380 | DESENSITIZED EXPLOSIVE, SOLID, N.O.S. |
| L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 | 3381 | TOXIC BY INHALATION LIQUID, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 |
| L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 | 3382 | TOXIC BY INHALATION LIQUID, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 |
| [L10CH] [L15CH] [L15DH(+)] | TU14 TU15 TE1 TE19 TE21 | FL | [0] [1] |  |  | CV1 CV13 CV28 | S2 S9 S17 | 663 | 3383 | TOXIC BY INHALATION LIQUID, FLAMMABLE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 |
| [L10CH] [L15CH] [L15DH(+)] | TU14 TU15 TE1 TE19 TE21 | FL | [0] [1] |  |  | CV1 CV13 CV28 | S2 S9 S17 | 663 | 3384 | TOXIC BY INHALATION LIQUID, FLAMMABLE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 |

| UN No. | Name and description | Class | Classification Code | Packing group | Labels | Special provisions | Limited quantities | Packagings and IBCs | UN Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special provisions | Mixed packing provisions | Instructions | Special provisions |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) |
| 3385 | TOXIC BY INHALATION LIQUID, WATER-REACTIVE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | 6.1 | TW1 | I | 6.1 +4.3 | 274 | LQ0 | P601 |  | MP8 MP17 | T22 | TP2 TP9 TP13 |
| 3386 | TOXIC BY INHALATION LIQUID, WATER-REACTIVE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | 6.1 | TW1 | I | 6.1 +4.3 | 274 | LQ0 | P602 |  | MP8 MP17 | T20 | TP2 TP9 TP13 |
| 3387 | TOXIC BY INHALATION LIQUID, OXIDIZING, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | 6.1 | TO1 | I | 6.1 +5.1 | 274 | LQ0 | P601 |  | MP8 MP17 | T22 | TP2 TP9 TP13 |
| 3388 | TOXIC BY INHALATION LIQUID, OXIDIZING, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | 6.1 | TO1 | I | 6.1 +5.1 | 274 | LQ0 | P602 |  | MP8 MP17 | T20 | TP2 TP9 TP13 |
| 3389 | TOXIC BY INHALATION LIQUID, CORROSIVE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | 6.1 | [TC1] [TC3] | I | 6.1 +8 | 274 | LQ0 | P601 |  | MP8 MP17 | T22 | TP2 TP9 TP13 |
| 3390 | TOXIC BY INHALATION LIQUID, CORROSIVE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | 6.1 | [TC1] [TC3] | I | 6.1 +8 | 274 | LQ0 | P602 |  | MP8 MP17 | T20 | TP2 TP9 TP13 |
| 3391 | ORGANOMETALLIC SUBSTANCE, SOLID, PYROPHORIC | 4.2 | [S5] | I | 4.2 | 274 | LQ0 | P404 | PP86 | MP2 | T21 | TP7 TP33 |

| ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identification No. | UN No. | Name and description |
| --- | --- | --- | --- | --- | --- | --- |
| Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |  |  |
| (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) | (1) | (2) |
| L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 623 | 3385 | TOXIC BY INHALATION LIQUID, WATER-REACTIVE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 |
| L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 623 | 3386 | TOXIC BY INHALATION LIQUID, WATER-REACTIVE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 |
| L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 665 | 3387 | TOXIC BY INHALATION LIQUID, OXIDIZING, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 |
| L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 665 | 3388 | TOXIC BY INHALATION LIQUID, OXIDIZING, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 |
| L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 668 | 3389 | TOXIC BY INHALATION LIQUID, CORROSIVE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 |
| L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 668 | 3390 | TOXIC BY INHALATION LIQUID, CORROSIVE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 |
| [L21DH] | [TU4 TU14 TU22 TC1 TE1 TE21 TM1] | [AT] | 0 | V1 |  |  | S20 | 333 | 3391 | ORGANOMETALLIC SUBSTANCE, SOLID, PYROPHORIC |

| UN No. | Name and description | Class | Classification Code | Packing group | Labels | Special provisions | Limited quantities | Packagings and IBCs | UN Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special provisions | Mixed packing provisions | Instructions | Special provisions |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) |
| 3392 | ORGANOMETALLIC SUBSTANCE, LIQUID, PYROPHORIC | 4.2 | [S5] | I | 4.2 | 274 | LQ0 | P400 | PP86 | MP2 | T21 | TP2 TP7 |
| 3393 | ORGANOMETALLIC SUBSTANCE, SOLID, PYROPHORIC, WATER REACTIVE | 4.2 | SW | I | 4.2 +4.3 | 274 | LQ0 | P404 | PP86 | MP2 | T21 | TP7 TP33 |
| 3394 | ORGANOMETALLIC SUBSTANCE, LIQUID, PYROPHORIC, WATER REACTIVE | 4.2 | SW | I | 4.2 +4.3 | 274 | LQ0 | P400 | PP86 | MP2 | T21 | TP2 TP7 |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE | 4.3 | W2 | I | 4.3 | 274 | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE | 4.3 | W2 | II | 4.3 | 274 | LQ11 | P410 IBC04 |  | MP14 | T3 | TP33 |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE | 4.3 | W2 | III | 4.3 | 274 | LQ12 | P410 IBC06 |  | MP14 | T1 | TP33 |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, FLAMMABLE | 4.3 | WF2 | I | 4.3 +4.1 | 274 | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, FLAMMABLE | 4.3 | WF2 | II | 4.3 +4.1 | 274 | LQ11 | P410 IBC04 |  | MP14 | T3 | TP33 |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, FLAMMABLE | 4.3 | WF2 | III | 4.3 +4.1 | 274 | LQ12 | P410 IBC06 |  | MP14 | T1 | TP33 |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, SELF-HEATING | 4.3 | WS | I | 4.3 +4.2 | 274 | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, SELF-HEATING | 4.3 | WS | II | 4.3 +4.2 | 274 | LQ11 | P410 IBC04 |  | MP14 | T3 | TP33 |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, SELF-HEATING | 4.3 | WS | III | 4.3 +4.2 | 274 | LQ12 | P410 IBC06 |  | MP14 | T1 | TP33 |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE | 4.3 | W1 | I | 4.3 | 274 | LQ0 | P402 |  | MP2 | T13 | TP2 TP7 |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE | 4.3 | W1 | II | 4.3 | 274 | LQ10 | P001 IBC01 |  | MP15 | T7 | TP2 TP7 |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE | 4.3 | W1 | III | 4.3 | 274 | LQ13 | P001 IBC02 |  | MP15 | T7 | TP2 TP7 |
| 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE, FLAMMABLE | 4.3 | WF1 | I | 4.3 +3 | 274 | LQ0 | P402 |  | MP2 | T13 | TP2 TP7 |

| ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identification No. | UN No. | Name and description |
| --- | --- | --- | --- | --- | --- | --- |
| Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |  |  |
| (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) | (1) | (2) |
| L21DH | [TU4] TU14 [TU22] TC1 TE1 TE21 TM1 | AT | 0 | V1 |  |  | S20 | 333 | 3392 | ORGANOMETALLIC SUBSTANCE, LIQUID, PYROPHORIC |
| L21DH | TU4 TU14 TU22 TC1 TE1 TE21 TM1 | AT | 0 | V1 |  |  | S20 | X333 | 3393 | ORGANOMETALLIC SUBSTANCE, SOLID, PYROPHORIC, WATER REACTIVE |
| L21DH | TU4 TU14 TU22 TC1 TE1 TE21 TM1 | AT | 0 | V1 |  |  | S20 | X333 | 3394 | ORGANOMETALLIC SUBSTANCE, LIQUID, PYROPHORIC, WATER REACTIVE |
| [?] | [?] | AT | [0] [1] | V1 |  | CV23 | S20 | X423 | 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE |
| SGAN |  | AT | [0] [2] | V1 [V12] | [VV3] [VV5] [VV7] | CV23 |  | 423 | 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE |
| SGAN |  | AT | [0] [3] | V1 | [VV1] [VV5] [VV7] | CV23 |  | 423 | 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE |
| [?] | [?] | FL | 0 | V1 |  | CV23 |  | X423 | 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, FLAMMABLE |
| [?] | [?] | FL | 0 | V1 |  | CV23 |  | 423 | 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, FLAMMABLE |
| [?] | [?] | FL | 0 | V1 V12 |  | CV23 |  | 423 | 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, FLAMMABLE |
| [?] | [?] | AT | 1 | V1 |  | CV23 | S20 | X423 | 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, SELF-HEATING |
| SGAN |  | AT | 2 | V1 |  | CV23 |  | 423 | 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, SELF-HEATING |
| SGAN |  | AT | 3 | V1 | VV5 | CV23 |  | 423 | 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, SELF-HEATING |
| L10DH | TU14 TE1 TE21 TM2 | AT | 0 | V1 |  | CV23 | S20 | X323 | 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE |
| L4DH | TU14 TE1 TE21 TM2 | AT | 0 | V1 |  | CV23 |  | 323 | 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE |
| L4DH | TU14 TE1 TE21 TM2 | AT | 0 | V1 |  | CV23 |  | 323 | 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE |
| L10DH | TU4 TU14 TU22 TE1 TE21 TM2 | FL | 0 | V1 |  | CV23 | S2 S20 | X323 | 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE, FLAMMABLE |

| UN No. | Name and description | Class | Classification Code | Packing group | Labels | Special provisions | Limited quantities | Packagings and IBCs | UN Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special provisions | Mixed packing provisions | Instructions | Special provisions |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) |
| 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE, FLAMMABLE | 4.3 | WF1 | II | 4.3 +3 | 274 | LQ10 | P001 IBC01 |  | MP15 | T7 | TP2 TP7 |
| 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE, FLAMMABLE | 4.3 | WF1 | III | 4.3 +3 | 274 | LQ13 | P001 IBC02 R001 |  | MP15 | T7 | TP2 TP7 |
| 3400 | ORGANOMETALLIC SUBSTANCE, SOLID, SELF-HEATING | 4.2 | [S5] | II | 4.2 | 274 | LQ18 | P410 IBC06 |  | MP14 | T3 | TP33 |
| 3400 | ORGANOMETALLIC SUBSTANCE, SOLID, SELF-HEATING | 4.2 | [S5] | III | 4.2 | 274 | LQ11 | P002 IBC08 |  | MP14 | T1 | TP33 |
| 3401 1389 | ALKALI METAL AMALGAM, SOLID | 4.3 | W2 | I | 4.3 | 182 | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 |
| 3402 1392 | ALKALINE EARTH METAL AMALGAM, SOLID | 4.3 | W2 | I | 4.3 | 183 | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 |
| 3403 1420 | POTASSIUM METAL ALLOYS, SOLID | 4.3 | W2 | I | 4.3 |  | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 |
| 3404 1422 | Potassium sodium alloys, SOLID | 4.3 | W2 | I | 4.3 |  | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 |
| 3405 1445 | BARIUM CHLORATE SOLUTION | 5.1 | OT1 | II | 5.1 +6.1 |  | LQ10 | P504 IBC02 |  | MP2 | T4 | TP1 |
| 3405 1445 | BARIUM CHLORATE SOLUTION | 5.1 | OT1 | III | 5.1 +6.1 |  | LQ13 | P001 IBC02 |  | MP2 | T4 | TP1 |
| 3406 1447 | BARIUM PERCHLORATE SOLUTION | 5.1 | OT1 | II | 5.1 +6.1 |  | LQ10 | P504 IBC02 |  | MP2 | T4 | TP1 |
| 3406 1447 | BARIUM PERCHLORATE SOLUTION | 5.1 | OT1 | III | 5.1 +6.1 |  | LQ13 | P001 IBC02 |  | MP2 | T4 | TP1 |
| 3407 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE SOLUTION | 5.1 | O1 | II | 5.1 |  | LQ10 | P504 IBC02 |  | MP2 | T4 | TP1 |
| 3407 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE SOLUTION | 5.1 | O1 | III | 5.1 |  | LQ13 | P504 IBC02 |  | MP2 | T4 | TP1 |
| 3408 1470 | LEAD PERCHLORATE SOLUTION | 5.1 | OT1 | II | 5.1 +6.1 |  | LQ10 | P504 IBC02 |  | MP2 | T4 | TP1 |
| 3408 1470 | LEAD PERCHLORATE SOLUTION | 5.1 | OT1 | III | 5.1 +6.1 |  | LQ13 | P001 IBC02 |  | MP2 | T4 | TP1 |
| 3409 1578 | CHLORONITRO-BENZENES, LIQUID | 6.1 | T1 | II | 6.1 | 279 | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 |
| 3410 1579 | 4-CHLORO-o-TOLUIDINE HYDROCHLORIDE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 R001 |  | MP15 | T4 | TP1 |
| 3411 1650 | beta-NAPHTHYLAMINE SOLUTION | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 |
| 3411 1650 | beta-NAPHTHYLAMINE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC02 |  | MP15 | T7 | TP2 |

| ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identification No. | UN No. | Name and description |
| --- | --- | --- | --- | --- | --- | --- |
| Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |  |  |
| (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) | (1) | (2) |
| L4DH | TU4 TU14 TU22 TE1 TE21 TM2 | FL | 0 | V1 |  | CV23 | S2 | 323 | 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE, FLAMMABLE |
| L4DH | TU14 TE1 TE21 TM2 | FL | 0 | V1 |  | CV23 | S2 | 323 | 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE, FLAMMABLE |
| [SGAV] [SGAN] |  | AT | 2 | V1 V12 |  |  |  | 40 | 3400 | ORGANOMETALLIC SUBSTANCE, SOLID, SELF-HEATING |
| [SGAV] [SGAN] |  | AT | 3 | V1 | [VV4] |  |  | 40 | 3400 | ORGANOMETALLIC SUBSTANCE, SOLID, SELF-HEATING |
| L10BN(+) | TU1 TE5 TT3 TM2 | AT | 1 | V1 |  | CV23 | S20 | X423 | 3401 1389 | ALKALI METAL AMALGAM, SOLID |
| L10BN(+) | TU1 TE5 TT3 TM2 | AT | 1 | V1 |  | CV23 | S20 | X423 | 3402 1392 | ALKALINE EARTH METAL AMALGAM, SOLID |
| L10BN(+) | TU1 TE5 TT3 TM2 | AT | 1 | V1 |  | CV23 | S20 | X423 | 3403 1420 | POTASSIUM METAL ALLOYS, SOLID |
| L10BN(+) | TU1 TE5 TT3 TM2 | AT | 1 | V1 |  | CV23 | S20 | X423 | 3404 1422 | Potassium sodium alloys, SOLID |
| L4BN | TU3 | AT | 2 |  |  | CV24 CV28 |  | 56 | 3405 1445 | BARIUM CHLORATE SOLUTION |
| LGBV | TU3 | AT | 3 |  |  | CV24 CV28 |  | 56 | 3405 1445 | BARIUM CHLORATE SOLUTION |
| L4BN | TU3 | AT | 2 |  |  | CV24 CV28 |  | 56 | 3406 1447 | BARIUM PERCHLORATE SOLUTION |
| LGBV | TU3 | AT | 3 |  |  | CV24 CV28 |  | 56 | 3406 1447 | BARIUM PERCHLORATE SOLUTION |
| L4BN | TU3 | AT | 2 |  |  | CV24 |  | 50 | 3407 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE SOLUTION |
| LGBV | TU3 | AT | 3 |  |  | CV24 |  | 50 | 3407 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE SOLUTION |
| L4BN | TU3 | AT | 2 |  |  | CV24 CV28 |  | 56 | 3408 1470 | LEAD PERCHLORATE SOLUTION |
| LGBV | TU3 | AT | 3 |  |  | CV24 CV28 |  | 56 | 3408 1470 | LEAD PERCHLORATE SOLUTION |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 | 3409 1578 | CHLORONITRO-BENZENES, LIQUID |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3410 1579 | 4-CHLORO-o-TOLUIDINE HYDROCHLORIDE SOLUTION |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 | 3411 1650 | beta-NAPHTHYLAMINE SOLUTION |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3411 1650 | beta-NAPHTHYLAMINE SOLUTION |

| UN No. | Name and description | Class | Classification Code | Packing group | Labels | Special provisions | Limited quantities | Packagings and IBCs | UN Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special provisions | Mixed packing provisions | Instructions | Special provisions |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) |
| 3413 1680 | POTASSIUM CYANIDE SOLUTION | 6.1 | T4 | I | 6.1 |  | LQ0 | P001 |  | MP8 MP17 | T14 | TP2 TP13 |
| 3413 1680 | POTASSIUM CYANIDE SOLUTION | 6.1 | T4 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T11 | TP2 TP13 TP27 |
| 3413 1680 | POTASSIUM CYANIDE SOLUTION | 6.1 | T4 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T7 | TP2 TP13 TP28 |
| 3414 1689 | SODIUM CYANIDE SOLUTION | 6.1 | T4 | I | 6.1 |  | LQ0 | P001 |  | MP8 MP17 | T14 | TP2 TP13 |
| 3414 1689 | SODIUM CYANIDE SOLUTION | 6.1 | T4 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T11 | TP2 TP13 TP27 |
| 3414 1689 | SODIUM CYANIDE SOLUTION | 6.1 | T4 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T7 | TP2 TP13 TP28 |
| 3415 1690 | SODIUM FLUORIDE SOLUTION | 6.1 | T4 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 |
| 3416 1697 | CHLOROACETO-PHENONE, LIQUID | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 TP13 |
| 3417 1701 | XYLYL BROMIDE, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3418 1709 | 2,4-TOLUYLENE-DIAMINE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 |
| 3419 1742 | BORON TRIFLUORIDE ACETIC ACID COMPLEX, SOLID | 8 | C4 | II | 8 |  | LQ23 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3420 1743 | BORON TRIFLUORIDE PROPIONIC ACID COMPLEX, SOLID | 8 | C4 | II | 8 |  | LQ23 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3421 1811 | POTASSIUM HYDROGENDI-FLUORIDE SOLUTION | 8 | CT1 | II | 8 +6.1 |  | LQ22 | P001 IBC02 |  | MP15 | T7 | TP2 |
| 3421 1811 | POTASSIUM HYDROGENDI-FLUORIDE SOLUTION | 8 | CT1 | III | 8 +6.1 |  | LQ19 | P001 IBC03 |  | MP15 | T4 | TP1 |
| 3422 1812 | POTASSIUM FLUORIDE SOLUTION | 6.1 | T4 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 |
| 3423 1835 | TETRAMETHYL-AMMONIUM HYDROXIDE, SOLID | 8 | C8 | II | 8 |  | LQ24 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3424 1843 | AMMONIUM DINITRO-o-CRESOLATE SOLUTION | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 |
| 3424 1843 | AMMONIUM DINITRO-o-CRESOLATE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC02 |  | MP15 | T7 | TP2 |
| 3425 1938 | BROMOACETIC ACID, SOLID | 8 | C4 | II | 8 |  | LQ23 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3426 2074 | ACRYLAMIDE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 |
| 3427 2235 | CHLOROBENZYL CHLORIDES, SOLID | 6.1 | T2 | III | 6.1 |  | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 |
| ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identification No. | UN No. | Name and description |
| Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |  |  |
| (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) | (1) | (2) |
| L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 | 3413 1680 | POTASSIUM CYANIDE SOLUTION |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 | 3413 1680 | POTASSIUM CYANIDE SOLUTION |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3413 1680 | POTASSIUM CYANIDE SOLUTION |
| L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 | 3414 1689 | SODIUM CYANIDE SOLUTION |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 | 3414 1689 | SODIUM CYANIDE SOLUTION |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3414 1689 | SODIUM CYANIDE SOLUTION |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3415 1690 | SODIUM FLUORIDE SOLUTION |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 | 3416 1697 | CHLOROACETO-PHENONE, LIQUID |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3417 1701 | XYLYL BROMIDE, SOLID |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3418 1709 | 2,4-TOLUYLENE-DIAMINE SOLUTION |
| SGAN L4BN |  | AT | 2 | V11 |  |  |  | 80 | 3419 1742 | BORON TRIFLUORIDE ACETIC ACID COMPLEX, SOLID |
| SGAN L4BN |  | AT | 2 | V11 |  |  |  | 80 | 3420 1743 | BORON TRIFLUORIDE PROPIONIC ACID COMPLEX, SOLID |
| L4DH | TU14 TE21 | AT | 2 |  |  | CV13 CV28 |  | 86 | 3421 1811 | POTASSIUM HYDROGENDI-FLUORIDE SOLUTION |
| L4DH | TU14 TE21 | AT | 3 |  |  | CV13 CV28 |  | 86 | 3421 1811 | POTASSIUM HYDROGENDI-FLUORIDE SOLUTION |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3422 1812 | POTASSIUM FLUORIDE SOLUTION |
| SGAN L4BN |  | AT | 2 | V11 |  |  |  | 80 | 3423 1835 | TETRAMETHYL-AMMONIUM HYDROXIDE, SOLID |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 | 3424 1843 | AMMONIUM DINITRO-o-CRESOLATE SOLUTION |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3424 1843 | AMMONIUM DINITRO-o-CRESOLATE SOLUTION |
| SGAN |  | AT | 2 | V11 |  |  |  | 80 | 3425 1938 | BROMOACETIC ACID, SOLID |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3426 2074 | ACRYLAMIDE SOLUTION |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 | 3427 2235 | CHLOROBENZYL CHLORIDES, SOLID |

| UN No. | Name and description | Class | Classification Code | Packing group | Labels | Special provisions | Limited quantities | Packagings and IBCs | UN Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special provisions | Mixed packing provisions | Instructions | Special provisions |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) |
| 3428 2236 | 3-CHLORO-4-METHYLPHENYL ISOCYANATE, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3429 2239 | CHLORO-TOLUIDINES, LIQUID | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 |
| 3430 2261 | XYLENOLS, LIQUID | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 |
| 3431 2306 | NITROBENZO-TRIFLUORIDES, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3432 2315 | POLYCHLORINATED BIPHENYLS, SOLID | 9 | M2 | II | 9 | 305 | LQ25 | P906 IBC08 | [B4] | MP10 | T3 | TP33 |
| 3433 2445 | LITHIUM ALKYLS, SOLID | 4.2 | SW | I | 4.2 +4.3 | 320 | LQ0 | P400 |  | MP2 | T21 | TP7 TP33 |
| 3434 2446 | NITROCRESOLS, LIQUID | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 |
| 3435 2662 | HYDROQUINONE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 |
| 3436 2552 | HEXAFLUORO-ACETONE HYDRATE, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3437 2669 | CHLOROCRESOLS, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3438 2937 | alpha-METHYLBENZYL ALCOHOL, SOLID | 6.1 | T2 | III | 6.1 |  | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 |
| 3439 3276 | NITRILES, TOXIC, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 274 | LQ0 | P002 IBC07 |  | MP18 | T6 | TP9 TP33 |
| 3439 3276 | NITRILES, TOXIC, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 274 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3439 3276 | NITRILES, TOXIC, SOLID, N.O.S. | 6.1 | T2 | III | 6.1 | 274 | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 |
| 3440 3283 | SELENIUM COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | I | 6.1 |  | LQ0 | P001 |  | MP8 MP17 | T14 | TP2 TP9 TP27 |
| 3440 3283 | SELENIUM COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T11 | TP2 TP27 |
| 3440 3283 | SELENIUM COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | III | 6.1 |  | LQ19 | P001 IBC03 |  | MP15 | T7 | TP1 TP28 |
| 3468 | HYDROGEN IN A METAL HYDRIDE STORAGE SYSTEM | 2 | 2F |  | 2.1 | 321 | LQ0 | P099 |  | MP9 |  |  |

| ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identification No. | UN No. | Name and description |
| --- | --- | --- | --- | --- | --- | --- |
| Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |  |  |
| (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) | (1) | (2) |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3428 2236 | 3-CHLORO-4-METHYLPHENYL ISOCYANATE, SOLID |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3429 2239 | CHLORO-TOLUIDINES, LIQUID |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 | 3430 2261 | XYLENOLS, LIQUID |
| SGAH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3431 2306 | NITROBENZO-TRIFLUORIDES, SOLID |
| S4AH L4BH | TU15 TE1 TE15 | AT | 0 | V1 |  | CV1 CV13 CV28 | S19 | 90 | 3432 2315 | POLYCHLORINATED BIPHENYLS, SOLID |
| L21DH | TU4 TU14 TU22 TC1 TE1 TE21 TM1 | AT | 0 | V1 |  |  | S20 | X333 | 3433 2445 | LITHIUM ALKYLS, SOLID |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3434 2446 | NITROCRESOLS, LIQUID |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3435 2662 | HYDROQUINONE SOLUTION |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3436 2552 | HEXAFLUORO-ACETONE HYDRATE, SOLID |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 | 3437 2669 | CHLOROCRESOLS, SOLID |
| SGAH [L4BH] | TU15 TE1 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 | 3438 2937 | alpha-METHYLBENZYL ALCOHOL, SOLID |
| S10AH [L10CH] | [TU14] TU15 TE1 TE19 [TE21] | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 | 3439 3276 | NITRILES, TOXIC, SOLID, N.O.S. |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 | 3439 3276 | NITRILES, TOXIC, SOLID, N.O.S. |
| SGAH [L4BH] | TU15 TE1 TE15 TE19 | AT | 2 | V11 | VV9b | CV13 CV28 | S9 | 60 | 3439 3276 | NITRILES, TOXIC, SOLID, N.O.S. |
| L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 | 3440 3283 | SELENIUM COMPOUND, LIQUID, N.O.S. |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 | 3440 3283 | SELENIUM COMPOUND, LIQUID, N.O.S. |
| L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 | 3440 3283 | SELENIUM COMPOUND, LIQUID, N.O.S. |
|  |  |  | 2 | V7 |  | CV9 CV10 | S2 S20 | 23[9] | 3468 | HYDROGEN IN A METAL HYDRIDE STORAGE SYSTEM |

Add the following new entries for the solid form of substances previously covered by the UN number indicated in italics in column (1):

| UN No. | Name and description | Class | Classification Code | UN packing group | Labels | Special provisions | Limited quantities | Packagings and IBCs | UN Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special provisions | Mixed packing provisions | Portable tank instruction | Portable tank special provisions |
| (1) | (3a) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) |
| 3441 1577 | CHLORODINITRO-BENZENES, SOLID | 6.1 | T2 | II | 6.1 | 279 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3442 1590 | DICHLOROANILINES, SOLID | 6.1 | T2 | II | 6.1 | 279 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3443 1597 | DINITROBENZENES, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3444 1656 | NICOTINE HYDROCHLORIDE, SOLID | 6.1 | T2 | II | 6.1 | 43 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3445 1658 | NICOTINE SULPHATE, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3446 1664 | NITROTOLUENES, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3447 1665 | NITROXYLENES, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3448 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 274 | LQ0 | P002 |  | MP18 | T6 | TP9 TP33 |
| 3448 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 274 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3449 1694 | Bromobenzyl cyanides, solid | 6.1 | T2 | I | 6.1 | 138 | LQ0 | P002 |  | MP18 | T6 | TP33 |
| 3450 1699 | DIPHENYL-CHLOROARSINE, SOLID | 6.1 | T3 | I | 6.1 |  | LQ0 | P002 IBC07 | B1 | MP18 | T6 | TP33 |
| 3451 1708 | Toluidines, SOLID | 6.1 | T2 | II | 6.1 | 279 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3452 1711 | XYLIDINES, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3453 1805 | PHOSPHORIC ACID SOLID | 8 | C2 | III | 8 |  | LQ24 | P002 IBC08 LP02 | B3 | MP10 | T1 | TP33 |
| 3454 2038 | DINITROTOLUENES, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3455 2076 | CRESOLS, SOLID | 6.1 | TC2 | II | 6.1 +8 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3456 2308 | NITROSYL-SULPHURIC ACID, SOLID | 8 | C2 | II | 8 |  | LQ23 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3457 2433 | CHLORONITRO-TOLUENES, SOLID | 6.1 | T2 | III | 6.1 |  | LQ9 | P002 IBC08 LP02 | B3 | MP10 | T1 | TP33 |
| 3458 2730 | NITROANISOLES, SOLID | 6.1 | T2 | III | 6.1 | 279 | LQ9 | P002 IBC08 LP02 | B3 | MP10 | T1 | TP33 |
| 3459 2732 | NITROBROMO-BENZENES, SOLID | 6.1 | T2 | III | 6.1 |  | LQ9 | P002 IBC08 LP02 | B3 | MP10 | T1 | TP33 |
| 3460 2753 | N-ETHYLBENZYL-TOLUIDINES, SOLID | 6.1 | T2 | III | 6.1 |  | LQ9 | P002 IBC08 LP02 | B3 | MP10 | T1 | TP33 |
| 3461 3052 | ALUMINIUM ALKYL HALIDES, SOLID | 4.2 | SW | I | 4.2 +4.3 | [274] [320] | LQ0 | P404 |  | MP2 | T21 | TP7 TP33 |

| ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identification No. | UN No. | Name and description |
| --- | --- | --- | --- | --- | --- | --- |
| Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |  |  |
| (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) | (1) | (2) |
| SGAH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3441 1577 | CHLORODINITRO-BENZENES, SOLID |
| SGAH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3442 1590 | DICHLOROANILINES, SOLID |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3443 1597 | DINITROBENZENES, SOLID |
| SGAH | TU15 TE1 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 | 3444 1656 | NICOTINE HYDROCHLORIDE, SOLID |
| SGAH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3445 1658 | NICOTINE SULPHATE, SOLID |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3446 1664 | NITROTOLUENES, SOLID |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3447 1665 | NITROXYLENES, SOLID |
| S10AH L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 | 3448 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3448 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. |
| S10AH | TU15 TE1 TE19 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 | 3449 1694 | Bromobenzyl cyanides, solid |
| S10AH | TU15 TE1 TE19 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 | 3450 1699 | DIPHENYL-CHLOROARSINE, SOLID |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3451 1708 | Toluidines, SOLID |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3452 1711 | XYLIDINES, SOLID |
| SGAN |  | AT | 3 |  | VV9b | CV28 |  | 80 | 3453 1805 | PHOSPHORIC ACID, SOLID |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3454 2038 | DINITROTOLUENES, SOLID |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 68 | 3455 2076 | CRESOLS, SOLID |
| SGAN |  | AT | 2 | V11 |  |  |  | X80 | 3456 2308 | NITROSYL-SULPHURIC ACID, SOLID |
| SGAH | TU15 TE1 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 | 3457 2433 | CHLORONITRO-TOLUENES, SOLID |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 | 3458 2730 | NITROANISOLES, SOLID |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 | 3459 2732 | NITROBROMO-BENZENES, SOLID |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 | 3460 2753 | N-ETHYLBENZYL-TOLUIDINES, SOLID |
| L21DH | TU4 TU14 TU22 TC1 TE1 TE21 TM1 | AT | 0 | V1 |  |  | S20 | X333 | 3461 3052 | ALUMINIUM ALKYL HALIDES, SOLID |

| UN No. | Name and description | Class | Classification Code | UN packing group | Labels | Special provisions | Limited quantities | Packagings and IBCs | UN Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special provisions | Mixed packing provisions | Portable tank instruction | Portable tank special provisions |
| (1) | (3a) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) |
| 3462 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 210 274 | LQ0 | P002 IBC07 |  | MP18 | T6 | TP9 TP33 |
| 3462 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 210 274 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3462 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | T2 | III | 6.1 | 210 274 | LQ9 | P002 IBC08 R001 | B3 | MP10 | T1 | TP33 |
| 3464 3278 | ORGANOPHOS-PHORUS COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 43 274 | LQ0 | P002 IBC07 |  | MP18 | T6 | TP9 TP33 |
| 3464 3278 | ORGANOPHOS-PHORUS COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 43 274 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3464 3278 | ORGANOPHOS-PHORUS COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | T2 | III | 6.1 | 43 274 | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 |
| 3465 3280 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. | 6.1 | T3 | I | 6.1 | 274 | LQ0 | P002 IBC07 |  | MP18 | T6 | TP9 TP33 |
| 3465 3280 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. | 6.1 | T3 | II | 6.1 | 274 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3465 3280 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. | 6.1 | T3 | III | 6.1 | 274 | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 |
| 3466 3281 | METAL CARBONYLS, SOLID, N.O.S. | 6.1 | T3 | I | 6.1 | 274 562 | LQ0 | P002 IBC07 |  | MP18 | T6 | TP9 TP33 |
| 3466 3281 | METAL CARBONYLS, SOLID, N.O.S. | 6.1 | T3 | II | 6.1 | 274 562 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3466 3281 | METAL CARBONYLS, SOLID, N.O.S. | 6.1 | T3 | III | 6.1 | 274 562 | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 |
| 3467 3282 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | T3 | I | 6.1 | 274 562 | LQ0 | P002 IBC07 |  | MP18 | T6 | TP9 TP33 |
| 3467 3282 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | T3 | II | 6.1 | 274 562 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 |
| 3467 3282 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | T3 | III | 6.1 | 274 562 | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 |

| ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identification No. | UN No. | Name and description |
| --- | --- | --- | --- | --- | --- | --- |
| Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |  |  |
| (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) | (1) | (2) |
| S10AH L10CH | TU15 TE1 TE19 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 | 3462 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3462 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 | 3462 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. |
| S10AH L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 | 3464 3278 | ORGANOPHOS-PHORUS COMPOUND, TOXIC, SOLID, N.O.S. |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3464 3278 | ORGANOPHOS-PHORUS COMPOUND, TOXIC, SOLID, N.O.S. |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 | 3464 3278 | ORGANOPHOS-PHORUS COMPOUND, TOXIC, SOLID, N.O.S. |
| S10AH L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 | 3465 3280 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3465 3280 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 | 3465 3280 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. |
| S10AH L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 | 3466 3281 | METAL CARBONYLS, SOLID, N.O.S. |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3466 3281 | METAL CARBONYLS, SOLID, N.O.S. |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 | 3466 3281 | METAL CARBONYLS, SOLID, N.O.S. |
| S10AH L10CH | TU14 TU15 TE1 TE19 TE21 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 | 3467 3282 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 | 3467 3282 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. |
| SGAH L4BH | TU15 TE1 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 | 3467 3282 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. |

Rationalized approach for assignment of tank instructions for solids:

| Class | Labels | PG | Tank Instruction | Tank prov. | Apply to |
| --- | --- | --- | --- | --- | --- |
| 4.1 | 4.1 | I | Not Authorized |  | All UN Nos. in this group |
|  |  | II | T3 | TP33 | 1309, 1323, 1325 (replace "TP1" with "TP33"), 1326, 1339, 1341, 1343, 1345, 1352, 1358, 1437, 1868, 1871, 2925, 2926, 2989, 3089, 3175, 3178, 3179, 3180, 3181, 3182, 3242 |
|  |  | III | T1 | TP33 | 1309,1312, 1313, 1314, 1318, 1325 (replace "TP1" with "TP33"), 1328, 1330, 1332, 1334, 1338, 1346, 1350 (replace "TP1" with "TP33"), 1869, 2001, 2213, 2538, 2687, 2714, 2715, 2717, 2878, 2925, 2926, 2989, 3089, 3097, 3178, 3179, 3180, 3181, 3182 |
| 4.2 | 4.2 | I | T21 | TP7 TP33 | 1383, 1854, 2005, 2008, 2870, 2881, 3200, 3254 |
|  |  | II | T3 | TP33 | 1361, 1369, 1374, 1378, 1382, 1384, 1385, 1431, 1923, 1929, 2004, 2008, 2318, 2545, 2546, 2881, 2940, 3088, 3126, 3127, 3128, 3189, 3190, 3191, 3192, 3205, 3206, 3313, 3341, 3342 |
|  |  | III | T1 | TP33 | 1361, 1362, 1373, 1376, 1932, 2008, 2210, 2545, 2546, 2881, 3088, 3126, 3127, 3128, 3174, 3189, 3190, 3191, 3192, 3205, 3206, 3313, 3341, 3342 |
| 4.3 | 4.3 +6.1 | I | Not Authorized |  | All UN Nos. in this group |
|  |  | I | T9 | TP7 TP33 | 1402, 1428 (replace "TP3 TP31" with "TP33") and 2257 (replace "TP3 TP31" with "TP33") |
|  |  | II | T3 | TP33 | 1340, 1390, 1393, 1394, 1395, 1396, 1400, 1401, 1402, 1405, 1409, 1417, 1418, 1436, 2624, 2805, 2813, 2830, 2835, 3078, 3131, 3132, 3134, 3135, 3170, 3208, 3209, 3372 |
|  |  | III | T1 | TP33 | 1396, 1398, 1403, 1405, 1408, 1418, 1435, 1436, 2813, 2844, 2950, 2968, 3131, 3132, 3134, 3135, 3170, 3208, 3209, 3372 |
| 5.1 | 5.1 | I | Not Authorized |  | All UN Nos. in this group |
|  |  | II | T3 | TP33 | 1439, 1442, 1445 (replace "T4" with "T3" and "TP1" with "TP33"), 1446, 1447 (replace "T4" with "T3" and "TP1" with "TP33"), 1448, 1449, 1450, 1452, 1453, 1455, 1456, 1457, 1458, 1459 (replace "T4" with "T3" and "TP1" with "TP33", 1461, 1462, 1463, 1469, 1470 (replace "T4" with "T3" and "TP1" with "TP33"), 1472, 1473, 1475, 1476, 1477, 1479, 1481, 1482, 1483, 1484, 1485, 1487, 1488, 1489, 1490, 1493, 1494, 1495, 1496, 1502, 1503, 1506, 1508, 1509, 1512, 1513, 1514, 1515, 1516, 2464, 2465, 2468, 2573, 2626, 2627, 2719, 2721, 2723, 2741, 3085, 3087, 3212, 3247, 3377, 3378 |
|  |  | III | T1 | TP33 | 1438, 1444, 1451, 1454, 1458, 1459 (replace "T4" with "T1" and "TP1" with "TP33"), 1465, 1466, 1467, 1474, 1477, 1479, 1481, 1482, 1483, 1486, 1492, 1498, 1499, 1500, 1505, 1507, 1511, 1872, 1942, 2067, 2469, 2720, 2722, 2724, 2725, 2726, 2728, 3085, 3087, 3215, 3378 |
| 5.2 | 5.2 |  | T23 | TP33 | 3110, 3120 |
| 6.1 | 6.1 | I | T6 | TP33 | 1544, 1557, 1565, 1570, 1575, 1588, 1601, 1626, 1655, 1680 (replace "T14" with "T6" and "TP2 TP13" with "TP33"), 1689 (replace "T14" with "T6" and "TP2 TP13" with "TP33"), 1692, 1698, 1713, 1889, 2025, 2026, 2316, 2471, 2570, 2588, 2628, 2629, 2630, 2642, 2757, 2759, 2761, 2763, 2771, 2775, 2777, 2779, 2781, 2783, 2786, 2811, 2928, 2930, 3027, 3048, 3086, 3124, 3125, 3143, 3146, 3283 (replace "T14" with "T6" and "TP2 TP27" with "TP33"), 3284 (replace "T14" with "T6" and "TP2 TP27" with "TP33"), 3285 (replace "T14" with "T6" and "TP2 TP27" with "TP33"), 3288, 3290, 3345, 3349 |
|  |  | II | T3 | TP33 | 1544, 1546, 1554, 1555, 1557, 1558, 1559, 1561, 1562, 1564, 1566, 1567, 1569 (replace "T10" with "T3" and "TP2 TP13" with "TP33"), 1572, 1573, 1574, 1578 (replace "T7" with "T3" and "TP2" with "TP33"), 1585, 1586, 1587, 1588, 1596 (replace "T7" with "T3" and "TP2" with "TP33"), 1598 (replace "T7" with "T3" and "TP2" with "TP33"), 1601, 1606, 1607, 1608, 1617, 1618, 1620, 1621, 1622, 1623, 1624, 1625, 1627, 1629, 1630, 1631, 1634, 1636, 1637, 1638, 1639, 1640, 1641, 1642, 1643, 1644, 1645, 1646, 1650 (replace "T7" with "T3" and "TP2" with "TP33"), 1651, 1652, 1653, 1655, 1657, 1659, 1661 (replace "T7" with "T3" and "TP2" with "TP33"), 1671 (replace "T6" with "T3" and "TP2" with "TP33"), 1674, 1677, 1678, 1679, 1683, 1684, 1685, 1688, 1691, 1697 (replace "T7" with "T3" and "TP2 TP13" with "TP33"), 1707, 1712, 1751, 1843, 1885, 1894, 1895, 2018 (replace "T7" with "T3" and "TP2" with "TP33"), 2025, 2026, 2027, 2250 (replace "T7" with "T3" and "TP2" with "TP33"), 2261 (replace "T7" with "T3" and "TP2" with "TP33"), 2567, 2570, 2587, 2588, 2645, 2647, 2649, 2657, 2671, 2673, 2727, 2757, 2759, 2761, 2763, 2771, 2775, 2777, 2779, 2781, 2783, 2786, 2811, 2859, 2861, 2863, 2864, 2928, 2930, 2931, 3027, 3086, 3124, 3125, 3143, 3146, 3155, 3243, 3249, 3283 (replace "T11" with "T3" and "TP2 TP27" with "TP33"), 3284(replace "T11" with "T3" and "TP2 TP27" with "TP33"), 3285 (replace "T11" with "T3" and "TP2 TP27" with "TP33"), 3288, 3290, 3345, 3349 |
| 6.1 | 6.1 | III | T1 | TP33 | 1544, 1548, 1549, 1550, 1551, 1557, 1564, 1566, 1579 (replace "T4" with "T1" and "TP1" with "TP33"), 1588, 1601, 1616, 1655, 1663 (replace "T4" with "T1" and "TP3" with "TP33"), 1673 (replace "T7" with "T1" and "TP1" with "TP33"), 1690 (replace "T4" with "T1" and "TP1" with "TP33"), 1709 (replace "T4" with "T1" and "TP1" with "TP33"), 1812 (replace "T4" with "T1" and "TP1" with "TP33"), 1884, 2020, 2025, 2026, 2074 (replace "T4" with "T1" and "TP1" with "TP33"), 2233, 2237, 2239 (replace "T4" with "T1" and "TP1" with "TP33"), 2291, 2446, 2473, 2505, 2512, 2516, 2570, 2588, 2651 (replace "T4" with "T1" and "TP1" with "TP33"), 2655, 2659, 2660, 2662 (replace "T4" with "T1" and "TP1" with "TP33"), 2674, 2713, 2716, 2729, 2757, 2759, 2761, 2763, 2771, 2775, 2777, 2779, 2781, 2783, 2786, 2811, 2853, 2854, 2855, 2856, 2862, 2871, 2875, 2876, 3027, 3143, 3146, 3249, 3283 (replace "T7" with "T1"and "TP1 TP28" with "TP33"), 3284 (replace "T7" with "T1" and "TP1 TP28" with "TP33"), 3285 (replace "T7" with "T1" and "TP1 TP28" with "TP33"), 3288, 3345, 3349 |
| 8 | 8 | I | T6 | TP33 | 1759, 1905, 2430 (replace "T10" with "T1" and "TP2 TP28" with "TP33"), 2921, 2923, 3084, 3095, 3096, 3147, 3259, 3260, 3261, 3262, 3263 |
|  |  | II | T3 | TP33 | 1725, 1726, 1727, 1740, 1756, 1759, 1770, 1794, 1806, 1807, 1811 (replace "T7" with "T3" and "TP2" with "TP33"), 1813, 1823, 1825, 1839, 1847, 1849 (replace "T7" with "T3" and "TP2" with "TP33"), 1939 (replace "T7" with "T3" and "TP2" with "TP33"), 2033, 2430 (replace "TP2" with "TP33"), 2439, 2506, 2509, 2583, 2670, 2678, 2680, 2682, 2691, 2869, 2921, 2923, 3084, 3095, 3096, 3147, 3244, 3259, 3260, 3261, 3262, 3263 |
|  |  | III | T1 | TP33 | 1740, 1759, 1773, 1907, 1910, 2214 (replace "T4" with "T1" and "TP3" with "TP33"), 2215 (replace "T4" with "T1" and "TP1" with "TP33"), 2280 (replace "T4" with "T1" and "TP3" with "TP33"), 2331, 2430 (replace "T3" with "T1" and "TP1" with "TP33"), 2440, 2475, 2503, 2507, 2508, 2578, 2579 (replace "T4" with "T1" and "TP1 TP30" with "TP33"), 2585, 2698, 2802, 2803, 2812, 2823 (replace "T4" with "T1" and "TP1" with "TP33"), 2834 (replace "T3" with "T1" and "TP1" with "TP33"), 2865, 2869, 2905, 2923, 2967, 3147, 3253, 3259, 3260, 3261, 3262, 3263 |
| 9 | 9 | II | T3 | TP33 | 2212, 2969, 3152 |
|  |  | III | T1 | TP33 | 1841, 1931, 2211, 2216, 2590, 3077 |

Chapter 3.3

SP63		Amend as follows:

Replace (a) and (b) with the following:

2.2.2.1.3 (c)	Amend to read:

"(a)	Division 2.1 applies   “Assignment to group F shall apply if the contents include 85% by mass or more flammable components and the chemical heat of combustion is 30 kJ/g or more;

(b)	Division 2.2 applies   It shall not apply if the contents contain 1% by mass or less flammable components and the heat of combustion is less than 20 kJ/g."

Insert a new (c) as follows:

"(c)	Otherwise the aerosol the product shall be classified as tested for flammability in accordance with by the tests described in the Manual of Tests and Criteria, Part III, section 31. Extremely flammable and flammable aerosols shall be assigned to group F. classified in Division 2.1; non-flammable in Division 2.2;

The existing subparagraphs (c), (d), (e) and (f) become (d), (e), (f) and (g) respectively.

Add at the end a new paragraph to read as follows:

NOTE: Flammable components are flammable liquids, flammable solids or flammable gases and gas mixtures as defined in Notes 1 to 3 of sub-section 31.1.3 of Part III of the Manual of Tests and Criteria. This designation does not cover pyrophoric, self-heating or water-reactive substances. The chemical heat of combustion shall be determined by one of the following methods ASTM D 240, ISO/FDIS 13943: 1999 (E/F) 86.1 to 86.3 or NFPA 30B."

SP 133	Amend to read:

"If over-confined in packagings, this substance may exhibit explosive behaviour. Packagings authorized under packing instruction P409 are intended to prevent over-confinement. When a packaging other than those prescribed under packing instruction P409 is authorized by the competent authority of the country of origin in accordance with 4.1.3.7, the package shall bear an "EXPLOSIVE" subsidiary risk label unless the competent authority of the country of origin has permitted this label to be dispensed with for the specific packaging employed because test data have proved that the substance in this packaging does not exhibit explosive behaviour (see 5.4.1.5.5.1). The provisions of 7.1.3.1 shall also be then considered.".

SP 179		Amend to read: [or assign as a new special provision applicable to UN Nos 3077 and 3082]

"This designation shall be used for substances and mixtures which are dangerous to the aquatic environment or which are marine pollutants that do not meet the classification criteria of any other class or another substance within Class 9.  This designation may also be used for wastes not otherwise subject to these Regulations but which are covered under the Basel Convention on the Control of Transboundary Movements of Hazardous Wastes and their Disposal and for substances designated to be environmentally hazardous substances by the competent authority of the country of origin, transit or destination which do not meet the criteria for an environmentally hazardous substance according to these Regulations or for any other hazard Class.".

SP 215	Add the following text at the end:

"Homogeneous mixtures containing not more than 35 % by mass of azocarbonamide and at least 65 % of inert substance are not subject to RID/ADR/ADN these Regulations unless criteria of other classes or divisions are met.".

SP219		Amend to read as follows:

"Genetically modified micro-organisms and genetically modified organisms which meet the definition of an infectious substance and the criteria for inclusion in Division Class 6.2 in accordance with Chapter 2.6 section 2.2.62 shall be transported carried as UN No. 2814, UN No. 2900 or UN No. 3373, as appropriate.".

SP240	Add the following at the end of the existing special provision 240:

"Hybrid electric vehicles powered by both an internal combustion engine and wet batteries, sodium batteries or lithium batteries, transported with the battery(ies) installed shall be consigned under the entries UN 3166 VEHICLE, FLAMMABLE GAS POWERED or UN 3166 VEHICLE, FLAMMABLE LIQUID POWERED, as appropriate."

SP243	Amend to read as follows: [or assign as a new special provision applicable to UN No. 1203]

"Gasoline, motor spirit and petrol for use in spark-ignition engines (e.g. in automobiles, stationary engines and other engines) shall be assigned to this entry regardless of variations in volatility.".

SP296	Replace the existing text with the following:

"These entries apply for life-saving appliances such as life rafts, personal flotation devices and self-inflating slides. UN No. 2990 applies for self-inflating appliances and UN No. 3072 applies for life-saving appliances that are not self-inflating.  Life-saving appliances may contain:

(a) 	Signal devices (Class 1) which may include smoke and illumination signal flares packed in packagings that prevent them from being inadvertently activated;

(b) 	For UN No. 2990 only, cartridges, power device of Division 1.4, compatibility group S, may be contained for purposes of the self-inflating mechanism and provided that the quantity of explosives per appliance does not exceed 3.2 g;

(c) 	Division 2.2 Class 2 compressed gases, group A or O, according to 2.2.2.1.3;

(d) 	Electric storage batteries (Class 8) and lithium batteries (Class 9);

(e) 	First aid kits or repair kits containing small quantities of dangerous goods (e.g.: Classes 3, Division 4.1, Division 5.2, Class 8 or Class 9 substances); or

(f) 	"Strike anywhere" matches packed in packagings that prevent them from being inadvertently activated.".

SP 309 	Amend the last sentence to read as follows:

"Substances shall satisfactorily pass Test Series 8 of the Manual of Tests and Criteria, Part I, Section 18."

Add the following new special provisions:

"311	Substances shall not be transported carried under this entry unless approved by the competent authority on the basis of the results of appropriate tests according to Part I of the Manual of Tests and Criteria. Packaging shall ensure that the percentage of diluent does not fall below that stated in the competent authority approval, at any time during transport carriage.

312	Vehicles which contain an internal combustion engine shall be consigned under the entries UN No. 3166 VEHICLE, FLAMMABLE GAS POWERED or UN No. 3166 VEHICLE, FLAMMABLE LIQUID POWERED, as appropriate. These entries include hybrid electric vehicles powered by both an internal combustion engine and wet batteries, sodium batteries or lithium batteries, transported carried with the battery(ies) installed.

313	Substances and mixtures meeting the criteria for Class 8 shall be labelled with a "CORROSIVE" subsidiary risk label bear a subsidiary risk label conforming to mode No. 8 (see 5.2.2.2.2).

314	a) 	These substances are liable to exothermic decomposition at elevated temperatures. Decomposition can be initiated by heat or by impurities (e.g. powdered metals (iron, manganese, cobalt, magnesium) and their compounds);

b)	During the course of transport carriage, these substances shall be shaded from direct sunlight and all sources of heat and be placed in adequately ventilated areas.

315	This entry shall not be used for Division Class 6.1 substances which meet the inhalation toxicity criteria for packing group I described in 2.6.2.2.4.3 2.2.61.1.8.

316	This entry applies only to calcium hypochlorite, dry or hydrated, when transported carried in non friable tablet form.

317	"Fissile-excepted" applies only to those packages complying with 6.4.11.2.

318	For the purposes of documentation, the proper shipping name shall be supplemented with the technical name (see 3.1.2.8). Technical names need not be shown on the package. When the infectious substances to be transported carried are unknown, but suspected of meeting the criteria for inclusion in category A and assignment to UN No. 2814 or UN 2900, the words "suspected category A infectious substance" shall be shown, in parentheses, following the proper shipping name on the transport document, but not on the outer packagings.

319	This entry applies to human or animal material including, but not limited to, excreta, secreta, blood and its components, tissue and tissue fluids, and body parts being transported carried for purposes such as research, diagnosis, investigational activities, disease treatment or prevention.  Substances packed and marked in accordance with packing instruction P650 are not subject to any other requirements in these Regulations of RID/ADR/ADN.

320	It is intended that this entry will be deleted from modal requirements effective RID/ADR/ADN on 1 January 2007. Irrespective of 2.0.2.2 2.1.2, in the interim period, this entry or the appropriate generic entry may be used.

321	These storage systems shall always be considered as containing hydrogen.".