INF.30

Decisions made by the informal Working Group on Harmonisation with the UN Recommendations for information of the Joint Meeting (3 September 2003)

Document 2003/56/Add.3

1.	For UN 1793 IBC 03 is changed into IBC 02 to be in line with the UN Recommendations (see also par. 30 of 2003/56).

Document 2003/56/Add.4

2.	The modifications concerning 4.1.6.2 to 4.1.6.10 have been deleted. EIGA will submit an informal paper for the October meeting reviewing the whole Section 4.1.6 of RID/ADR.

3.	It has been pointed out that P 200 is not totally in line with the UN Recommendations. This should be kept in mind for future work.

4.	The representative of EIGA proposed to delete the existing texts in (7) and (8) of P 203. He was invited to submit a written proposal. 6.2.1.6.3 has to be kept for the moment (delete the modification in document 2003/56/Add.6).

5.	In P 404 the two first modifications should read as follows:

"Replace ", 2881, 3052, 3200 and 3203)." with ", 2881, 3052, 3200, 3391, 3393 and 3461)"."

6.	The square brackets around "2984" in PP 10 of P 504 are deleted. This should be reported to the UN Committee of Experts.

7.	In P 620 c) "in accordance with the requirements of P 200" should be deleted to be in line with the UN Recommendations.

8.	P 650 (8) a) should read at the end as follows: "… and the package (the outer packaging or the overpack) shall be marked "Carbon dioxide, solid" or "Dry ice"."

Document 2003/56/Add.5

9.	The modification for 5.2.2.2.1.1 should read as follows: "Add the following sentence at the end: "For receptacles intended for the transport of refrigerated liquefied gases the standard format of A7 (74 X 105 mm) may also be used.""

10.	The square brackets in 5.2.2.2.2 are deleted.

Document 2003/56/Add.7

11.	In 7.5.11 CW/CV33 (3.3) (c) the reference to "(3.5)" should read:

"(3.5) (b) and (c)".

12.	In 7.5.11 CW/CV 34 delete the square brackets around "of pressure receptacles".

13.	The Parts 8 and 9 have to be treated in the WP.15.

Questions that need further discussion in the plenary

1.	The special provision 201 depends on the discussion of document 2003/9 from Norway and will stay in square brackets for the moment.

2.	PP 84 and P 205 should be treated together with the document 2003/9 from Norway.

3.	Carriage of UN 3373 in tanks (see hand written proposal from the lunch working group).

_____