| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRSP/2003/3/Rev.1 19 September 2003 Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Passive Safety (GRSP)

(Thirty-fourth session, 8-12 December 2003,

agenda item B.1.2.)

## PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 17

(Strength of seats)

Revision 1

# Transmitted by the expert from the Czech Republic

Note:  The text reproduced below was prepared by the expert from the Czech Republic in order to update the proposal for the figure of annex 5 to the Regulation (TRANS/WP.29/GRSP/33, para. 21).

____________

_______________

Note: This document is distributed to the Experts on Passive Safety only.

Annex 5, the figure, amend to read:

1.	Original unloaded position.

2a. 	Displaced position by applying to the manikin’s back a moment of 373 Nm

about the R point, defining the position of the displaced reference line r1.

2b. 	Displaced position by applying to the 165 mm sphere a force F producing a moment

of 373 Nm about the R point, keeping the displaced reference line r1 in place.

3.	Position after displacement by the force F increased to 890N.

.

_________________