# UN/SCEGHS/8/INF.27

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

##### Sub-Committee of Experts on the Globally

##### Harmonized System of Classification

##### and Labelling of Chemicals

Eighth session, 7-9 December 2004

Item 2 (a) of the provisional agenda

UPDATING OF THE GLOBALLY HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS (GHS)

Physical hazards

Comments on ST/SG/AC.10/C.4/2004/2 and UN/SCEGHS/8/INF.2

Transmitted by the Expert from France

At the 26th session on the SCETDG, a decision was accepted (subject to final adoption of the report) regarding a modification to the criteria for self-reactive substances having both oxidizing and self-properties. The decision takes account of proposals ST/SG/AC.10/C.4/2004/2 (by France) and of ST/SG/AC.10/C.3/2004/107 (by USA ; reproduced in UN/SCEGHS/8/INF.2) and of the debates in the SCETDG 26th session. Corresponding amendments that are proposed to be brought into the GHS are presented on next page.

###### Text proposed for inclusion in the GHS document

Chapter 2.8 :

“2.8.2.1	Any self-reactive substance or mixture should be considered for classification in this class unless:

(a)	They are explosives, according to the GHS criteria of Chapter 2.1;

(b)	They are oxidizing liquids or solids, according to the GHS criteria of Chapters 2.13 or 2.14, except that mixtures of oxidizing substances which contain 5.0% or more of combustible organic substances shall be classified as self-reactive substances according to the procedure defined in NOTE 1 ;

(c)	They are organic peroxides, according to the GHS criteria of Chapter 2.15;

(d)	Their heat of decomposition is less than 300 J/g; or

(e)	Their self-accelerating decomposition temperature (SADT) (see 2.4.2.3.4) is greater than 75 °C for a 50 kg package.

NOTE 1 : Mixtures of oxidizing substances, meeting the criteria for classification as oxidizing substances, which contain 5.0% or more of combustible organic substances and which do not meet the criteria mentioned in (a), (c), (d) or (e) above, shall be subjected to the self-reactive substance classification procedure;

A mixture showing the properties of a self-reactive substance type B to F shall be classified as a self-reactive substance.

________________