| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/2004/34 1 April 2004 Original: ENGLISH |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

(One-hundred-and-thirty-third session, 22-25 June 2004,
agenda item 4.2.11.)

DRAFT CORRIGENDUM 3 TO THE 05 SERIES OF AMENDMENTS

TO REGULATION No. 83

(Emissions of M1 and N1 categories of vehicles)

Transmitted by the Working Party on Pollution and Energy (GRPE)

Note:	The text reproduced below was adopted by GRPE at its forty-seventh session, and is transmitted for consideration to WP.29 and to AC.1.  It is based on document TRANS/WP.29/GRPE/2004/5, as amended by annex 2 to the report (TRANS/WP.29/GRPE/47, paras. 23 and 24).

___________

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraph 2.19.2., correct to read:

"2.19.2.	Limitation of emissions of gaseous and particulate pollutants, durability of pollution control devices and on-board diagnostics of vehicles fuelled with diesel fuel (Approval C)".

Paragraph 3.1., correct to read:

"3.1.	The application for approval of a vehicle type with regard to exhaust emissions, crankcase emissions, evaporative emissions and durability of pollution control devices, as well as to its on-board diagnostic (OBD) system shall be submitted by the vehicle manufacturer or by his authorized representative."

Insert a new paragraph 5.3.8., to read:

"5.3.8.	OBD - test

This test shall be carried out on all vehicles referred to in paragraph 1.  The test procedure described in annex 11, paragraph 3. shall be followed."

Annex 1, paragraphs 4.2.13.2. and 4.2.13.3.1, correct the figure "LPG" to read "NG".

Annex 4,

Appendix 1, the note 1 to table 1.3, correct to read:

"(1)		PM = gearbox on neutral, clutch engaged

K1 , K5 = first or fifth gear engaged, clutch disengaged"

Appendix 5, paragraph 1.1., correct to read:

"….

The devices described in paragraphs 3.1. and 3.2. shall be deemed ….."

Appendix 5, paragraph 2.3.4.1.4., should be deleted.

Appendix 5, paragraphs 3.1.4. and 3.2.4., correct to read:

"…..

S3	is a hydrocarbon sampling point

..…"

Annex 11, paragraph 4.2., correct to read:

"4.2.	……

…… effective in complying with the requirements of this Regulation and that the manufacturer has ……"

Annex 11, appendix 1, paragraph 1., correct to read:

"1.	INTRODUCTION

This appendix describes the procedure of the test according to paragraph 3. of annex 11. The procedure ……

……"

___________