UNITED

# NATIONS

Distr.

GENERAL

TRANS/WP.29/2004/40

25 March 2004

# Original: ENGLISH

### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

(One-hundred-and-thirty-third session, 22-25 June 2004,

agenda item 4.2.4.)

# PROPOSAL FOR DRAFT SUPPLEMENT 3 TO REGULATION No. 13-H

(Harmonized braking)

Transmitted by the Working Party on Brakes and Running Gear (GRRF)

Note:	The text reproduced below was adopted by GRRF at its fifty-fifth session and is transmitted for consideration to WP.29 and to AC.1.  It is based on document TRANS/WP.29/GRRF/2004/7, not amended (TRANS/WP.29/GRRF/55, para. 11).

____________

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Insert new paragraphs 5.2.22. to 5.2.22.4. and the corresponding footnotes, to read:

"5.2.22.	Generation of a signal to illuminate stop lamps.

5.2.22.1.	Activation of the service braking system by the driver shall generate a signal that will be used to illuminate the stop lamps.

5.2.22.2.	Activation of the service braking system by "automatically commanded braking" shall generate the signal mentioned above. However, when the retardation generated is less than 0.7 m/s2 at a vehicle speed greater than 50 km/h the signal may be suppressed. */

      - Activation of part of the service braking system by "selective braking" shall not generate the signal mentioned above. **/

5.2.22.4.	Electric regenerative braking systems, which produce a retarding force upon release of the throttle pedal, shall not generate a signal mentioned above".

_________________

*/	At the time of type approval, compliance with this requirement shall be confirmed by the vehicle manufacturer.

**/	During a "selective braking" event, the function may change to "automatically commanded braking".

___________________

# Text boxes

E

Economic and Social

Council