| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRSG/2004/16 13 July 2004 ENGLISH Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on General Safety Provisions (GRSG)

(Eighty-seventh session, 12-15 October 2004,

agenda item 10.1.)

AMENDMENT PROPOSAL TO DRAFT GLOBAL TECHNICAL REGULATION ON

HAND CONTROLS, TELL-TALES AND INDICATORS

PRESENT ON CATEGORY 1 AND 2 VEHICLES

(TRANS/WP.29/2000/8/Rev.3)

Transmitted by the expert from the India

Note:  The text reproduced below is based on the text of informal document No. GRSG-86-27

(TRANS/WP.29/GRSG/65, para. 30.).

____________

_______________

Note: This document is distributed to the Experts on General Safety Provisions only.

- PROPOSAL

Table 1, the following symbols should be included:

"

| No | Column 1 | Column 2 | Column 3 | Column 4 | Column 5 |
| --- | --- | --- | --- | --- | --- |
|  | ITEM | SYMBOL | FUNCTION | ILLUMINATION | COLOUR |
| 41. | Fuel selector switch In case of Bi-fuel 12/ vehicles: For vehicles fitted with electronic fuel injection (Two position switch) a1.) Vehicles running on CNG a2.) Vehicles running on LPG |  | Control | Yes |  |

|  | For all other vehicles (Three position switch) b1.) Vehicles running on CNG b2.) Vehicles running on LPG |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 42 | CNG Fuel level |  | Tell-tale | Yes | Yellow |
|  |  |  | Indicator */(Example of indicator is given below) | Yes |  |

|  | LPG Fuel level |  | Tell-tale | Yes | Yellow |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Indicator */(Example of indicator is given below) | Yes |  |

"

Add the following footnote 12/:

"12/  Bi-fuel system is defined as a system equipped to operate either on CNG / LPG or some other fuel e.g. petrol."

Table 2,

Symbols for controls, tell-tales and indicators required in electric or hybrid electric road vehicles should be included in other symbols.

*          *          *

B.	JUSTIFICATION

India is one of the largest operators of automotive vehicles running on Bi-fuel i.e. on CNG / LPG or petrol.

Re. Table 1

In Bi-fuel vehicles, a fuel selector switch (control) is required for the selection of fuel to be used from the available fuels (e.g. CNG / LPG and petrol ).  Identification of this switch (control) is necessary hence a symbol is suggested.

In case of Bi-fuel vehicles fitted with electronic fuel injection systems, a two-position switch (control) is required for selection of fuel.

In the case of other Bi-fuel vehicles (e.g. carburettor fitted), a three-position switch (control) is required, particularly when switching over from petrol to CNG mode to empty the petrol from the carburettor bowl.

Symbols No. 7 of Table 1 used for fuel level tell-tale and indicator are normally used for fuel petrol/diesel.  A separate symbol as given above is available in ISO:2575:2000 for CNG / LPG fuel and suggested to be used in the case of CNG / LPG fuel level tell-tale and indicators.

*/  Example of indicator for fuel level.

F

E

Reference for symbols:

| 1. |  | ISO 2575:2000 ( E) Road Vehicles- Symbols for controls, indicators and tell-tales AnA Annex G- Fuel System G-0 G-01 |
| --- | --- | --- |
| 2. |  | ISO 2575:2000 ( E) /Amd. 1:2001(E) Annex Z-Special Signs Z-04 Z-4 |
| 3. |  | ISO 2575:2000 ( E) /Amd. 1:2001(E) Annex Z-Special Signs Z-05 Z-5 |

Re. Table 2

There is a need for the symbols to identify the controls, tell-tales and indicators, such as state of propulsion battery, electric motor, etc. to be used in electric or hybrid electric road vehicles.

_________________