| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRSG/2004/17 13 July 2004 ENGLISH Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on General Safety Provisions (GRSG)

(Eighty-seventh session, 12-15 October  2004,

agenda item 10.4.)

PROPOSAL FOR DRAFT AMENDMENTS TO ANNEX 7 OF THE CONSOLIDATED RESOLUTION R.E.3

(document TRANS/WP.29/78/Rev.1/Amend.2)

Transmitted by the expert from the Russian Federation

Note:  The text reproduced below is based on the text of informal document No. GRSG-86-6

(TRANS/WP.29/GRSG/65, para. 42.).

____________

_______________

Note: This document is distributed to the Experts on General Safety Provisions only.

Annex 7,

Paragraphs 1. to 1.5., amend to read:

| "1. | CATEGORY L – power driven VEHICLES WITH LESS THAN FOUR WHEELS |
| --- | --- |
| 1.1. | Category L1 A two-wheeled vehicle with a maximum design speed of not more than 45 km/h and an engine whose cylinder capacity does not exceed 50 cm3 in the case of the internal combustion type, or whose maximum continuous rated power is no more than 4 kW in the case of an electric motor. |
| 1.2. | Category L2 A three-wheeled vehicle with a maximum design speed of not more than 45 km/h and an engine whose cylinder capacity does not exceed 50 cm3 if of the spark (positive) ignition type, or whose maximum net power output does not exceed 4 kW in the case of other internal combustion engines, or whose maximum continuous rated power does not exceed 4 kW in the case of an electric motor. |
| 1.3. | Category L3 A two-wheeled vehicle without a side-car with an engine having a cylinder capacity of more than 50 cm3 if of the internal combustion type and/or a maximum design speed of more than 45 km/h. |
| 1.4. | Category L4 A two-wheeled vehicle with a side-car with an engine having a cylinder capacity of more than 50 cm3 if of the internal combustion type and/or a maximum design speed of more than 45 km/h. |
| 1.5. | Category L5 A vehicle with three symmetrically arranged wheels fitted with an engine having a cylinder capacity of more than 50 cm3 if of the internal combustion type and/or a maximum design speed of more than 45 km/h." |

Insert new paragraphs 1.6. and 1.7., to read:

| "1.6. | Category L6 A vehicle with four wheels whose unladen mass is not more than 350 kg, not including the mass of the batteries in the case of electric vehicles, whose maximum design speed is not more than 45 km/h, and whose engine cylinder capacity does not exceed 50 cm³ for spark (positive) ignition engines, or whose continuous rated power does not exceed 4 kW in the case of electric engines. |
| --- | --- |
| 1.7. | Category L7 A vehicle with four wheels, other than that classified for the category L6, whose unladen mass is not more than 400 kg (550 kg for vehicles intended for carrying goods), not including the mass of batteries in the case of electric vehicles, and whose maximum continuous rated power does not exceed 15 kW in the case of electric engines." |

________________