| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRSG/2004/19 13 July 2004 ENGLISH Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on General Safety Provisions (GRSG)

(Eighty-seventh session, 12-15 October 2004,

agenda item 10.8.)

### PROPOSAL FOR CORRIGENDA TO THE PROPOSAL FOR A DRAFT REGULATION ON VEHICLE HEATING SYSTEMS

(Document TRANS/WP.29/2004/22)

Transmitted by the expert from the Russian Federation

Note:  The text reproduced below was prepared by the experts from the Russian Federation in order to improve the text of the draft Regulation.  It is based on informal document No. WP.29-133-20 distributed during the one-hundred-and-thirty-third session of WP.29 (TRANS/WP.29/1016, para. 63.).

____________

_______________

Note: This document is distributed to the Experts on General Safety Provisions only.

A.		PROPOSAL

Paragraph 6.2., amend to read:

" …………….

………………

"The test procedures for verification of each of these requirements are set out in annexes 3, 4, 5 and 6."

Paragraph 6.2.1., the table, the header of the fifth column, correct the word "Exhaus" to read "Exhaust".

Annex 6, paragraph 3., amend to read:

"3.		The test shall be repeated in conditions equivalent to a vehicle speed of 100 km/h (or maximum design speed of the vehicle in cases where the maximum speed is less than 100 km/h).  Under these conditions …………. "

*        *        *

B.	JUSTIFICATION

Ref. to paragraph 6.2.,

Annex 6 concerns exhaust emissions from combustion heaters, so the reference to annex 6 should be included.  Furthermore, reference to annex 6 is included in the relevant paragraph in the EU Directive 2001/56/EC as well.

Ref. to annex 6, paragraph 3.,

The maximum design speed of some vehicles is less than 100 km/h.

____________