Informal Document  No.  GRSG-86-27

86th GRSG session, 19-23 April 2004

## agenda item 10.1.

## Comments on document: GRSG-86-1 (TRANS/WP.29/2000/8/Rev.3)

(Draft Global Technical Regulation – Uniform  Provisions  for Hand  Controls, Tell-tale  and Indicators  Present  on  Category  1  and  2  Vehicles)

Transmitted by India

1. Page No. 8 Table - 1 – Symbols  for controls, Tell-tales and Indicators.

Following symbols should be included  in Table - 1.

| No | Column 1 | Column 2 | Column 3 | Column 4 | Column 5 |
| --- | --- | --- | --- | --- | --- |
|  | ITEM | SYMBOL | FUNCTION | ILLUMINATION | COLOUR |
| 1. | Fuel selector switch In case of Bi-fuel1/ vehicles: For vehicles fitted with electronic fuel injection (Two position switch) a1) Vehicles running on CNG a2) Vehicles running on LPG |  | Control | Yes |  |

|  | For all other vehicles (Three position switch) b1) Vehicles running on CNG b2) Vehicles running on LPG |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

Justification:

India  is  one  of  the  largest  operator  of    Automotive Vehicles  running  on  Bi-fuel  i.e on  CNG / LPG   or  petrol.

1.  In Bi-fuel vehicles fuel selector switch (control) is required for the  selection of fuel to be used from the available fuels (e.g. CNG / LPG  and   petrol ) Identification of this switch (control) is necessary hence  symbol is suggested.

- In case of Bi-fuel vehicles fitted with electronic fuel injection systems, two-position switch (control) is required for selection of  fuel.

- In case of other Bi-fuel vehicles (e.g. carburetor fitted) three-position  switch ( control) is required particularly when switching over from petrol to  CNG mode to empty the petrol from the carburetor  bowl.

1/  Bi-fuel system is defined as a system equipped to operate with either  on CNG / LPG or some other fuel e.g. petrol.

2. Following symbols are to be added in table – 1 for Tell-tale and Indicators for CNG /

LPG fuel  level.

| No | Column 1 | Column 2 | Column 3 | Column 4 | Column 5 |
| --- | --- | --- | --- | --- | --- |
|  | ITEM | SYMBOL | FUNCTION | ILLUMINATION | COLOUR |
| 2 | CNG Fuel level |  | Tell-tale | Yes | Yellow |
|  |  |  | Indicator *(Example of indicator is given below) | Yes |  |
|  | LPG Fuel level |  | Tell-tale | Yes | Yellow |
|  |  |  | Indicator *(Example of indicator is given below) | Yes |  |

Justification:

- Symbol used for fuel level tell-tale and indicator at Sr. No.7 Table – 1 ( See Reference for symbols Sr. no.1) is normally used for fuel petrol / diesel. Separate symbol as given above is available in ISO: 2575-2000 for CNG / LPG fuel and suggested to be used in case of CNG / LPG fuel level tell-tale and indicators.

- * Example of indicator for fuel level.

F

E

Reference for symbols:

| 1. |  | ISO:2575-2000 ( E) Road Vehicles- Symbols for controls, indicators and tell-tales Annex G- Fuel System G-01 |
| --- | --- | --- |
| 2. |  | ISO:2575-2000 ( E) /Amd. 1: 2001(E) Annex Z-Special Signs Z-04 |
| 3. |  | ISO:2575-2000 ( E) /Amd. 1: 2001(E) Annex Z-Special Signs Z-05 |

3. Page 14 (TRANS/WP.29/2000/8/Rev.3)

Symbols  for  controls , tell-tales  and  indicators  required  in   electric  or  hybrid  electric  road  vehicles  should  be  included in other symbols.

Justification  :

There is  need  for  the  symbols  to identify the  controls , tell-tales  and indicators  such as  state  of  propulsion  battery, electric  motor etc.  to  be used  in electric  or  hybrid  electric  road  vehicles .