| Consequential: Table 1.10.5, for class 6.2, letter “a” in column “Bulk” should be replaced by “0”. |
| --- |
| UN No. | Name and description | Class | Classif. code | Packing group | Labels | Special provi-sions | LQ | Packaging | Portable tanks and bulk containers | ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identifi- cation No. |  |
|  |  |  |  |  |  |  |  | Pack. Instr. | Special pack. Prov. | Mixed pack. Prov. | Instr. | Special prov. | Tank code | Special prov. |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |  |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) | (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) |  |
| 2814 | INFECTIOUS SUBSTANCE, AFFECTING HUMANS | 6.2 | I1 |  | 6.2 | 318 634 | LQ0 | P620 |  | MP5 |  |  |  |  |  | 0 |  |  | CV13 CV25 CV26 CV28 | S3 S9 S15 | 606 RID only | Cat A |
| 2814 | INFECTIOUS SUBSTANCE, AFFECTING HUMANS (animal carcasses only) | 6.2 | I1 |  | 6.2 | 318 634 | LQ0 | P620 +P099 |  | MP5 | BK1 BK2 |  |  |  |  | 0 |  |  | CV13 CV25 CV26 CV28 | S3 S9 S15 | 606 | Cat A |
| 2900 | INFECTIOUS SUBSTANCE, AFFECTING ANIMALS only | 6.2 | I2 |  | 6.2 | 318 634 | LQ0 | P620 |  | MP5 |  |  |  |  |  | 0 |  |  | CV13 CV25 CV26 CV28 | S3 S9 S15 | 606 RID only | Cat A |
| 3291 | CLINICAL WASTE, UNSPECIFIED, N.O.S. or (BIO) MEDICAL WASTE, N.O.S. or REGULATED MEDICAL WASTE, N.O.S. | 6.2 | I3 | II | 6.2 | 565 634 | LQ0 | P621 IBC620 LP621 |  | MP6 | BK2 |  | L4BH S4AH | TU15 TE15 TE19 | AT | 2 | V1 | VV11 | CV13 CV25 CV28 | S3 | 606 |  |
| 3373 | DIAGNOSTIC SPECIMENS or CLINICAL SPECIMENS BIOLOGICAL SUBSTANCE, CATEGORY B | 6.2 | I4 |  | 6.2 | 319 | LQ0 | P650 |  |  | T1 | TP1 | L4BH | TU15 TU37 TE15 TE19 | AT |  |  |  |  | S3 | 606 | Cat B |
| UN No. | Name and description | Class | Classif. code | Packing group | Labels | Special provi-sions | LQ | Packaging | Portable tanks and bulk containers | ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identifi- cation No. |  |
|  |  |  |  |  |  |  |  | Pack. Instr. | Special pack. Prov. | Mixed pack. Prov. | Instr. | Special prov. | Tank code | Special prov. |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |  |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) | (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) |  |
| 2900 | INFECTIOUS SUBSTANCE AFFECTING ANIMALS only (animal carcasses and waste only) | 6.2 | I.2 | 6.2 |  | 318 614 | LQ0 | P620 P099 |  | MP5 | BK1 BK2 |  |  |  |  | 0 |  |  | CV13 CV25 CV26 CV28 | S3 S9 S15 | 606 |  |

# Text boxes

#### INF.60

#### INF.60

Page 2