PROPOSAL FOR A MODIFICATION TO DRAFT CORRIGENDUM 1 (TRANS/WP29/2005/81) TO DRAFT REGULATION ON HEATING SYSTEMS

(Heating system of vehicles)

#### Transmitted by the representative of the European Community

A.	PROPOSAL

Annex 8,

Paragraph 1., amend to read:

"1.	LPG HEATING SYSTEMS FOR ROAD USE IN MOTOR VEHICLES"

Paragraph 1.1.6.2., amend to read:

"1.1.6.2.	no uncontrolled release due to an accidental disconnection can occur.  Means shall be provided to stop the flow of LPG by installing a device directly after or in a cylinder or container mounted regulator or if the regulator is mounted remote from the cylinder or container, a device shall be installed directly before the hose or pipe from the cylinder or container and an additional device shall be installed in, or after the regulator."

Paragraph 2., amend to read:

"2.	LPG HEATING SYSTEMS FOR STATIONARY USE ONLY IN MOTOR VEHICLES AND THEIR TRAILERS"

B.	JUSTIFICATION

- For the sake of clarity, concerning the application of Annex 8 to caravans, it is necessary to amend the title of paragraphs 1 and 2.

-For the sake of clarity, paragraph 1.1.6.2 on how the safety device of the LPG installation shall operate in case of a rupture of the LPG gas pipe/hose, needs to be amended to specify that only a complete disconnection is considered.

- - - - -