Informal document No. GRB-42-3

(42nd GRB, 5-7 September 2005,

agenda item 1.2.1.)

ENGLISH

# Summary of discussion about limits values for HDV

### Transmitted by Germany / OICA

#### Proposal by Germany

| Vehicle categories | Limit values (dB(A)) |
| --- | --- |
|  | Stage 1 | Stage 2 | Stage 3 |
|  | M2 c | 75 | 73 | 71 |
|  | M2 c off Road | 76 | 75 | 73 |
|  | N2 | 78 | 76 | 74 |
|  | N2 off Road | 79 | 78 | 76 |
|  | M3 | 79 | 77 | 75 |
|  | M3 a off Road | 80 | 79 | 77 |
|  | N3 a | 80 | 78 | 76 |
|  | N3 a off Road | 81 | 80 | 78 |
|  | N3 b | 81 | 79 | 77 |
|  | N3 b off Road | 82 | 81 | 79 |

#### Proposal by OICA

| Vehicle categories | Limit values (dB(A)) |
| --- | --- |
|  | Stage 1 | Stage 2 | Stage 3 |
| 6.2.2.7 | M2 c* | 77 | 76 | 75 |
| 6.2.2.8. | M3 ** | 81 | 80 | 79 |
| 6.2.2.9. | N2 * | 80 | 79 | 78 |
| 6.2.2.10. | N3 a** | 82 | 81 | 80 |
| 6.2.2.11. | N3 b** | 83 | 83 | 82 |

*1 dB(A) in addition for vehicles which fulfill the criteria for off-road as defined in RE3

**2 dB(A) in addition for vehicles which fulfill the criteria for off-road as defined in RE3

Vehicles according to paragraph 6.2.2.7. are M2 vehicles as defined in R.E.3 with a gross vehicle mass exceeding 3.5 tonnes.

Vehicles according to paragraph 6.2.2.8. are M3 vehicles as defined in R.E.3.

Vehicles according to paragraph 6.2.2.9. are N2 vehicles as defined in R.E.3.

Vehicles according to paragraph 6.2.2.10. are N3 vehicles as defined in R.E.3. with a rated engine power not exceeding 300 kW.

Vehicles according to paragraph 6.2.2.11. are N3 vehicles as defined in R.E.3. with a rated engine power exceeding 300 kW.

- - - - -