Informal document No. GRRF-57-17

(57th GRRF, 31 January-4 February 2005,

agenda item 1.1.)

## PROPOSAL TO DRAFT AMENDMENT OF TRANS/WP.29/GRRF/2004/19

(Braking)

# Transmitted by the expert from Germany

- PROPOSAL

Paragraph 5.2.2.13., amend to read:

"5.2.2.13.	Trailers of category O3 shall be equipped with an anti-lock braking system in accordance with the requirements of annex 13 to this Regulation.  Trailers of category O4 shall be equipped with an anti-lock braking system in accordance with the category A requirements of annex 13 to this Regulation."

Insert a new paragraph 12.1.1.4., to read:

"12.1.1.4.	As from the official date of entry into force of Supplement [1 to the 10] */ series of amendments, no Contracting Party applying this Regulation shall refuse to grant approvals under this Regulation as amended by Supplement [1 to the 10] */ series of amendments."

Insert new paragraphs 12.1.2.8. to 12.1.2.10., to read:

"12.1.2.8.	During the 12 months’ period that follows the date of entry into force of Supplement [1 to the 10] series of amendments [but not before 24 month after the date of entry into force of the 10 series of amendments], Contracting Parties applying this Regulation shall grant approvals only if the vehicle type to be approved meets either:

12.1.2.8.1.	the requirements of this Regulation as amended by Supplement [1 to the 10] */ series of amendments, or

12.1.2.8.2.	the requirements of paragraph 5.2.2.13. of this Regulation as amended by Supplement 9 to the 09 series of amendments, together with all other requirements of this Regulation as amended by Supplement [1 to the 10] */ series of amendments.

12.1.2.9.	As from 12 months after the official date of entry into force of Supplement [1 to the 10] */ series of amendments [but not before 24 month after the date of entry into force of the 10 series of amendments], Contracting Parties applying this regulation shall grant ECE approvals only if the vehicle type to be approved meets the requirements of paragraph 5.2.2.13. of this Regulation as amended by Supplement [1 to the 10] */ series of amendments.

12.1.2.10.	Starting 24 months after the official date of entry into force of Supplement [1 to the 10] */ series of amendments to this Regulation [but not before 48 month after the date of entry into force of the 10 series of amendments] , Contracting Parties applying this Regulation may refuse first national registration (first entry into service) of a vehicle which does not meet the requirements of paragraph 5.2.2.13. of this Regulation as amended by Supplement [1 to the 10] */ series of amendments "

*          *          *

B.	JUSTIFICATION

The transitional provisions of the document (TRANS/WP.29/GRRF/2004/19) are not in line with the transitional provisions with those of the 10 series of amendments to Regulation No. 13 adopted by WP. 29 at ist June 2004 session. The new insertion prevents that the corresponding provisions of Supplement [1 to the 10] series of amendments become mandatory before the transitional positons of the 10 series.

________________