| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.15/2006/22 9 August 2006 ENGLISH Original: FRENCH |

###### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Eighty-first session
Geneva, 25-27 October 2006
Agenda item 4

# PROPOSALS FOR AMENDMENTS TO ANNEXES A AND B OF ADR

## Paragraph 5.3.2.1.4

## Transmitted by the Government of Belgium

### Introduction

1.	Paragraph 5.3.2.1.1 of RID stipulates that a numbered orange-coloured marking must be affixed to wagons used for bulk carriage.

2.	Paragraph 5.3.2.1.4 of ADR deals exclusively with the carriage of solids in bulk; therefore, the carriage of accumulators in bulk (UN No. 2794, etc. …) or other items containing hazardous substances do not require numbered orange-coloured plates.

3.	ADR and RID should be brought into line.

GE.06-24687  (E)    021006    051006

### Proposal

4.	Amend the first part of paragraph 5.3.2.1.4 thus:

“When a hazard identification number is indicated in Column (20) of Table A of Chapter 3.2, transport units and containers carrying dangerous solid substances in bulk or packaged radioactive material with a single UN number …”

### Justification

5.	ADR and RID should be brought into line because there is no reason why different markings should be used for the carriage of items and solids in bulk.

### Consequences

6.	Items transported in bulk, if authorized under Chapter 3.2 (Column 17), will be carried in vehicles or containers with conventional markings, namely numbered orange plates.  This measure raises no applicability issues.

-----