INF.12

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

# Working Party on the Transport of Dangerous Goods

(Eightieth session,

Geneva, 8-12 May 2006

agenda item 5 (c)

## DRAFT AMENDMENT OF CHAPTER 9.2

Requirements concerning the construction of vehicles

Transmitted by the International Organization of Motor Vehicles manufacturers (OICA)

Document ECE/TRANS/WP.15/186 proposes to amend 9.2.1, and the table there under, regarding the application of speed limitation devices. However, as currently drafted the amendment could be interpreted as dis-applying the application of speed limitation devices from motor vehicles exceeding 12 tonnes first registered after 31 December 2007. Therefore it is proposed to amend the previously adopted text as indicated below.

9.2.1	Second indent:

After "31 December 1987", insert "and all motor vehicles with a maximum mass exceeding 3.5 tonnes but not more than 12 tonnes first registered after 31 December 2007."

In the table 9.2.1, under 9.2.5 Speed limitation device, column "Comments", insert ", and all motor vehicles with a maximum mass exceeding 3.5 tonnes but not more than 12 tonnes first registered after 31 December 2007" at the end of comment f.

Justification

To clarify the intent of the amendment.

_______