| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/34 24 March 2006 Original: ENGLISH |
| --- | --- | --- |

##### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-thirty-ninth session

Geneva, 20-23 June 2006,

Item 4.2.13. of the provisional agenda

#### DRAFT CORRIGENDUM 1 TO THE 04 SERIES OF AMENDMENTS

#### TO REGULATION No. 44

#### (Child restraint systems)

Submitted by the Working Party on Passive Safety (GRSP)

Note:  The text reproduced below was adopted by GRSP at its thirty-eighth session and is submitted for consideration to WP.29 and AC.1 (TRANS/WP.29/GRSP/38, para. 24).  It is based on the text of annex 3 to the report.

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraph 15.2.1., amend to read:

"15.2.1.	For "universal" category child restraints the following label shall be clearly visible at the point of sale without removing the packing:

NOTICE 1. This is a "Universal" child restraint. It is approved to Regulation No. 44, 04 series of amendments, for general use in vehicles and it will fit most, but not all, car seats. 2. A correct fit is likely if the vehicle manufacturer has declared in the vehicle handbook that the vehicle is capable of accepting a "Universal" child restraint for this age group. 3. This child restraint has been classified as "Universal" under more stringent conditions than those which applied to earlier designs which do not carry this notice. 4. If in doubt, consult either the child restraint manufacturer or the retailer.

"

Paragraph 15.2.11., amend to read:

"15.2.11.	For an ISOFIX child restraint system, the following label shall be clearly visible at the point of sale without removing the packing:

NOTICE 1. This is an ISOFIX CHILD RESTRAINT SYSTEM. It is approved to Regulation No. 44, 04 series of amendments for general use in vehicles fitted with ISOFIX anchorages systems. 2. It will fit vehicles with positions approved as ISOFIX positions (as detailed in the vehicle handbook), depending on the category of the child seat and of the fixture. 3. The mass group and the ISOFIX size class for which this device is intended is: ………

"

- - - - -