| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/57 31 March 2006 ENGLISH Original: ENGLISH and FRENCH |

### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-thirty-ninth-session

Geneva, 20-23 June 2006

Item 4.2.17. of the provisional agenda

PROPOSAL FOR SUPPLEMENT 10 TO REGULATION No. 50

(Position, stop and direction indicator lamps for mopeds and motorcycles)

Submitted by the Working Party on Lighting and Light-Signalling (GRE)

Note:	The text reproduced below was adopted by GRE at its fifty-fifth session, and is submitted for consideration to WP.29 and to AC.1 (TRANS/WP.29/GRE/55, para. 24 as amended by ECE/TRANS/WP.29/1050, para. 23).  It is based on document TRANS/WP.29/GRE/2005/27, as amended by ECE/TRANS/WP.29/GRE/2005/27/Rev.1.

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

The title of the Regulation, amend to read:

"UNIFORM PROVISIONS CONCERNING THE APPROVAL OF FRONT POSITION LAMPS, REAR POSITION LAMPS, STOP LAMPS, DIRECTION INDICATORS AND REAR-REGISTRATION-PLATE ILLUMINATING DEVICES FOR VEHICLES OF CATEGORY L"

Paragraph 1., amend to read (including the insertion of a reference to a new footnote 1/ and a new footnote 1/):

"1.	SCOPE

This Regulation applies to front position lamps, rear position lamps, stop lamps, direction indicators, and rear-registration-plate illuminating devices for vehicles of category L 1/.

_________________

1/	As defined in Annex 7 to the Consolidated Resolution on the Construction of Vehicles (R.E.3), (document TRANS/WP.29/78/Rev.1/Amend.2 as last amended by Amend.4)."

Paragraph 5.5.1., the reference to footnote 1/ and footnote 1/, renumber as footnote 2/ and amend to read:

"2/	1 for Germany, .... 48 for New Zealand, 49 for Cyprus, 50 for Malta, 51 for the Republic of Korea, [52 for Malaysia and 53 for Thailand].  Subsequent numbers shall be assigned .... "

- - - - -