| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/67 31 March 2006 ENGLISH Original: ENGLISH and FRENCH |

### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-thirty-ninth-session

Geneva, 20-23 June 2006

Item 4.2.35. of the provisional agenda

PROPOSAL FOR SUPPLEMENT 7 TO REGULATION No. 112

(Headlamps emitting an asymmetrical passing beam)

Submitted by the Working Party on Lighting and Light-Signalling (GRE)

Note:	The text reproduced below was adopted by GRE at its fifty-fifth session, and is submitted for consideration to WP.29 and to AC.1 (TRANS/WP.29/GRE/55, para. 24 as amended by ECE/TRANS/WP.29/1050, para. 23).  It is based on document TRANS/WP.29/GRE/2005/27, as amended by ECE/TRANS/WP.29/GRE/2005/27/Rev.1.

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraph 0., amend to read (including the insertion of a reference to a new footnote 2/ and a new footnote 2/):

"0.	SCOPE  1/

This Regulation applies to headlamps for vehicles of categories L, M, N and T 2/.

_________________

1/	....

2/	As defined in Annex 7 to the Consolidated Resolution on the Construction of Vehicles (R.E.3), (document TRANS/WP.29/78/Rev.1/Amend.2 as last amended by Amend.4)."

Paragraph 3., the reference to footnote 2/ and footnote 2/, renumber as footnote 3/.

Paragraph 3.2., the reference to footnote 3/ and footnote 3/, renumber as footnote 4/.

Paragraph 4.2.1.1., the reference to footnote 4/ and footnote 4/, renumber as footnote 5/ and amend to read:

"5/	1 for Germany, .... 48 for New Zealand, 49 for Cyprus, 50 for Malta, 51 for the Republic of Korea, [52 for Malaysia and 53 for Thailand].  Subsequent numbers shall be assigned .... "

B. TECHNICAL REQUIREMENTS FOR HEADLAMPS, the reference to footnote 5/ and footnote 5/, renumber as footnote 6/.

Paragraph 5.3., the reference to footnote 6/ and footnote 6/, renumber as footnote 7/.

Paragraph 5.4., the reference to footnote 7/ and footnote 7/, renumber as footnote 8/.

Paragraph 6.2.2.1., the reference to footnote 8/ and footnote 8/, renumber as footnote 9/.

Paragraph 6.2.2.3., the reference to footnote 9/ and footnote 9/, renumber as footnote 10/.

Paragraph 6.2.3., the reference to footnote 10/ and footnote 10/, renumber as footnote 11/.

Paragraph 6.2.4., the reference to footnote 11/ and footnote 11/, renumber as footnote 12/.

Paragraph 6.2.7., the reference to footnote 12/ and footnote 12/, renumber as footnote 13/.

Paragraph 8., the reference to footnote 13/ and footnote 13/, renumber as footnote 14/.

- - - - -