DRAFT

Head Restraint GTR – Status of Requirements (December 2006)

Front outboard: mandatory installation

Rear outboard and front centre: optional, but if fitted, they must meet

Dimensional Requirements

| Seating Position | Height (5.1.1) | Width (5.1.2) | Gaps within HR (5.1.3) | Gaps between HR and seat back top (5.1.4) | Backset (5.1.5) |
| --- | --- | --- | --- | --- | --- |
| Front outboard (static system) | *Minimum of 800 mm in at least 1 position. *Minimum of 750 in any use position. *Exemption if roof contact | Minimum of 170 mm | Gaps > 60 mm must meet max 102 mm rearward displacement. Procedure: 165 mm sphere | *Not adjustable: max 60 mm. *Adjustable: max 25 mm when measured with linear ruler or max 60 mm when measured with 165 mm sphere | *[55-70] mm. Procedure: HRMD -or- *[40-55] mm. Procedure: R point and FARO arm |
| Front outboard (non-static system) -Same as front outboard static system, except for backset | *Minimum of 800 mm in at least 1 position. *Minimum of 750 in any use position. *Exemption if roof contact | Minimum of 170 mm | Gaps > 60 mm must meet max 102 mm rearward displacement. Procedure: 165 mm sphere | *Not adjustable: max 60 mm. *Adjustable: max 25 mm when measured with linear ruler or max 60 mm when measured with 165 mm sphere | *[80] mm. Procedure: HRMD -or- *[80] mm. Procedure: R point and FARO arm |
| Front centre | *Minimum of 750 mm in any use position. *Exemption if roof contact | Minimum of 170 mm | Gaps > 60 mm must meet max 102 mm rearward displacement. Procedure: 165 mm sphere | *Not adjustable: max 60 mm. *Adjustable: max 25 mm when measured with linear ruler or max 60 mm when measured with 165 mm sphere | -No requirement |
| Rear outboard | *Minimum of 750 mm in any use position. *Exemption if roof contact | Minimum of 170 mm | Gaps > 60 mm must meet max 102 mm rearward displacement. Procedure: 165 mm sphere | *Not adjustable: max 60 mm. *Adjustable: max 25 mm when measured with linear ruler or max 60 mm when measured with 165 mm sphere | -No requirement |
| Rear centre | No height requirement (not regulated as a head restraint if height is less than 700 mm) | Minimum of 170 mm | Gaps > 60 mm must meet max 102 mm rearward displacement. Procedure: 165 mm sphere | *Not adjustable: max 60 mm. *Adjustable: max 25 mm when measured with linear ruler or max 60 mm when measured with 165 mm sphere | -No requirement |

Static Requirements

| Seating Position | Energy absorption front surface (5.2) | Adjustable height retention (5.2) | Displacement Test & Backset retention (5.2) | HR strength (5.2) | Non-use positions (5.4) | Removability (5.5) |
| --- | --- | --- | --- | --- | --- | --- |
| Front outboard (static system) | Max 80g/3ms. Procedure: 165 mm sphere impact | Downward movement max 25 mm. Procedure: cylinder with 500N downward force | Max 102 mm rearward displacement. Procedure: see R17 __________ Adjustable backset: Contracting Party Option to test in rearmost (see above) or in any adjustment (see above procedure with additional displacement evaluation) | Resist load of 890 N | (Front passenger only) -Automatic return | Allowed when accompanied with a distinct action other than upward adjustment. |
| Front outboard (non-static system) | Max 80g/3ms. Procedure: 165 mm sphere impact | Downward movement max 25 mm. Procedure: cylinder with 500N downward force | Max 102 mm rearward displacement. Procedure: see R17 | No requirement | (Front passenger only) -Automatic return | Allowed when accompanied with a distinct action other than upward adjustment. |
| Front centre | Max 80g/3ms. Procedure: 165 mm sphere impact | Downward movement max 25 mm. Procedure: cylinder with 500N downward force | No requirement | Resist load of 890 N | Contracting Party Option: Either Automatic return, 10° torso angle change, 60° rotation, or discomfort metric Or all of the above or labels | Allowed when accompanied with a distinct action other than upward adjustment. |
| Rear outboard | Max 80g/3ms. Procedure: 165 mm sphere impact | Downward movement max 25 mm. Procedure: cylinder with 500N downward force | No requirement | Resist load of 890 N | Contracting Party Option: Either Automatic return, 10° torso angle change, 60° rotation, or discomfort metric Or all of the above or labels | Allowed when accompanied with a distinct action other than upward adjustment. |
| Rear centre | Max 80g/3ms. Procedure: 165 mm sphere impact | Downward movement max 25 mm. Procedure: cylinder with 500N downward force | No requirement | Resist load of 890 N | Contracting Party Option: Either Automatic return, 10° torso angle change, 60° rotation, or discomfort metric Or all of the above or labels | Allowed when accompanied with a distinct action other than upward adjustment. |

*Numbers in parenthesis in title row correspond to text in HR-8-2        **Definition required for either “static system” or “non-static system”