Transmitted by WMTC	Informal document No. GRPE-53-11

(53rd GRPE, 9-12 January 2007,

agenda item 3.)

Amended sections/paragraphs are highlighted as bold italic red text.

Global technical regulation No. 2 (WMTC)

-

Measurement procedure for two-wheeled motorcycles equipped with a positive or compression ignition engine with regard to the emission of gaseous pollutants, CO2 emissions and fuel consumption

The text reproduced below was prepared by the WMTC FE experts in order to:

- introduce in the GTR the necessary amendments to the WMTC classification and cycle modules that resulted from the incorporation and assessment of the Indian in-use data

- correct a number of typing errors and inconsistencies in the GTR and further improvements to requirements (eg. gearshift prescriptions)

- introduce a harmonized family concept

- update the Technical Report in line with the GTR

- Amendments to the GTR (ECE/TRANS/180/Add.2)

Section A.2., add additional paragraphs:

“…

At the WMTC/FEG meeting held in Pune, India in April 2006, it was agreed that the group would prepare new test cycle proposals and a new vehicle classification in order for WMTC to appropriately cover include low-powered vehicles, such as commonly used in India and China.

A small WMTC Task Force, coordinated by IMMA, was set up to prepare a proposal on the test cycle(s) and any new classification that might be necessary to achieve this objective. The Task Force was attended by Germany (TUV), India, Italy, Japan (JASIC) and IMMA. Task Force meetings were held in August and October 2006.

WMTC FEG at its meeting in Ann Arbor, US in November 2006 agreed a modified version of one of the WMTC TF proposals, forwarded it to WMTC Informal Group in January 2007 where it was approved for submission to GRPE.

”

Justification: Additional information is needed to complete the procedural sequence.

Section A.3., amend to read:

“…

EU:

Directive 2002/51/EC amending directive 97/24/EC:  The reduction of the level of pollutant emissions from two-and three-wheeled motor vehicles

Indian Regulation

MoSRT&H/ CMVR/ TAP-115/116 and Central Motor Vehicle Rule No. 115

Japanese Regulation Trias:

Road vehicle Act, Article 41 "Systems and Devices of Motor Vehicles"

Safety Regulations for Road Vehicles, Article 31 "Emission Control Devices"

United States of America regulation:

US-FTP Subpart F, Emission Regulations for 1978 and Later New Motorcycles

ISO standards:

ISO 11486 (Motorcycles - Chassis dynamometer setting method)

ISO 6460 (gas sampling)

ISO 7860 (fuel consumption)

ISO 4106 (Motorcycles -- Engine test code -- Net power)

…

“

Justification: Reference to relevant Indian Regulation has to be included and TRIAS is not a proper reference so has to be deleted; addition of ISO 4106.

Section A.4., add paragraph:

“…

Finally, a first draft of the World-wide Motorcycle Test Cycle (WMTC) was produced.  It was foreseen that this first draft needed to be modified on the basis of an evaluation concerning driveability and practical points concerning the measurement procedure.  Since this process is iterative by nature, several adaptation rounds including the driveability tests were carried out.

To account for the performance and use of low-powered motorcycles, additional data was supplied by India. After analysis it was agreed that the previously agreed reduced speed test cycles should be modified and that the class 1 vehicle subcategories could be merged.

In each of these steps, specific technical issues were raised, discussed, and resolved.  The technical report describes this information.  Additionally, other issues addressed in this gtr are identified below.

…

“

Justification: An additional reference to the result of the inclusion of the Indian in-use data is necessary.

Section A.4.d), amend last paragraph to read:

“

…

The Informal group will continue its work on the comparative database of results from the different test procedures, which will act as a major input for the discussion of limit values that are compatible to existing limit values in different regions/countries.

“

Justification: The future work programme for the WMTC Informal Group has to be reformulated in view of completion of the modification of the cycle modules as a result of the inclusion of the Indian in-use data.

Section B.3.9., add:

“3.9.	“Maximum net engine power” is the maximum net engine power of the vehicle as declared by the manufacturer, measured in accordance with ISO 4106:2004 (Motorcycles -- Engine test code -- Net power).”

Justification: Additional definition of net engine power on the basis of applicable ISO standard has to be included to enable GTR application.

Section B.6.2.1., amend to read:

“

6.2.1.	General

The test vehicle shall conform in all its components with the production series, or, if the motorcycle is different from the production series, a full description shall be given in the test report. [The following items shall be used to select the motorcycle model which is representative of the relevant family of vehicles:

(a)	 The vehicles covered in the application will be divided into groupings whose engines are expected to have similar emission characteristics. Each group of engines with similar emission characteristics shall be defined as a separate engine family.

(b) Reciprocating families. To be classed in the same engine family, the following variables shall be considered for reciprocating engines:

- Vehicle mass (the declared value ± up to 20%)

- Engine power (the declared value ± up to 30%)

- Total gear ratio (E ≤ 8% calculated by E = (V2 – V1) / V1. V1 and V2 mean the vehicle speeds corresponding to an engine speed of 1000 rpm)

- The combustion cycle.

- The cooling mechanism.

- The cylinder configuration (inline, vee, opposed, bore spacing, etc.).

- The number of cylinders.

- The engine displacement range (the declared value ± up to 30%. In no case may the range extend beyond the defined limits of the main vehicle classification, § 6.3.)

- The method of air aspiration.

- The number of catalytic converters, location, volume, and composition.

- The thermal reactor characteristics.

- The number of carburettors

- Number and type of injectors, e.g. sequential, port, throttle body etc.

- The pre-chamber characteristics.

- The presence of air injection: such as pulsed, forced, etc.

- The presence of exhaust gas recirculation (EGR)

(c)	 At the manufacturer's option, reciprocating engines listed in paragraph (b) of this section may be further divided into different engine families based upon a consideration of features such as:

- The bore and stroke.

- The combustion chamber configuration.

- The intake and exhaust timing method of actuation (poppet valve, reed valve, rotary valve, etc.).

- The intake and exhaust valve or port sizes, as applicable.

- The fuel system.

- The exhaust system.

- The presence of an oxygen sensor

(d)	Rotary families. To be classed in the same engine family, the following variables shall be considered for rotary engines:

- Vehicle mass (the declared value ± up to 20%)

- Engine power (the declared value ± up to 30%)

- Total gear ratio (E ≤ 8% calculated by E = (V2 – V1) / V1. V1 and V2 mean the vehicle speeds corresponding to an engine speed of 1000 rpm)

- The major axis of the epitrochoidal curve.

- The minor axis of the epitrochoidal curve.

- The generating radius of the epitrochoidal curve.

- The cooling mechanism.

- The number of rotors.

- The engine displacement range (the declared value ± up to [30%]. In no case may the range extend beyond the defined limits of the main vehicle classification, § 6.3.)

- The method of air aspiration.

- The number of catalytic converters, location, volume and composition.

- The thermal reactor characteristics.

- The number of carburettors

- Number and type of injectors, e.g. sequential, port, throttle body etc.

- The pre-chamber characteristics.

- The presence of air injection: such as pulsed, forced, etc.

- The presence of exhaust gas recirculation (EGR)

(e)	At the manufacturer's option, rotary combustion cycle engines listed in paragraph (d) of this section, may be further divided into different engine families based upon a consideration of features, such as:

- The width of the rotor housing.

- The type and location of intake port (side, peripheral, combination, etc.).

- The number of spark plugs per rotor.

- The fuel system.

- The exhaust system.]”

Justification: Additional parameters are necessary to define a family of vehicles from which the test vehicle will be selected.

Note: The above text in between square brackets is subject to further discussion in relation to alternative provisions in existing regulations and the possible deletion of references to “vehicle type” eg. in paragraph 3.1 and Annex 4.

Section B.6.3.1., amend to read:

“6.3.1.	Class 1

Vehicles that fulfil the following specifications belong to class 1:

| 50 cm³ < engine capacity < 150 cm³ and vmax < 50 km/h or engine capacity < 150 cm³ and 50 km/h ≤ vmax < 100 km/h | class 1 |
| --- | --- |

“

Justification: This is the new classification, resulting from the incorporation and assessment of the Indian in-use data.

Section B.6.3.3., figure 6-1, substitute:

“

”

Justification: The amended figure graphically illustrates the new classification.

Section B.6.5.4.1., amend to read:

“6.5.4.1.	Test cycles

Test cycles (vehicle speed patterns), for the Type I test consists of up to three parts that are shown in annex 5. Depending on the vehicle class (see paragraph 6.3.) the following test cycle parts have to be run:

| Class 1: | part 1, reduced speed in cold condition, followed by part 1 reduced speed in hot condition. |
| --- | --- |
| Class 2: |  |
| Subclass 2-1: | part 1, reduced speed in cold condition, followed by part 2, reduced speed in hot condition. |
| Subclass 2-2: | part 1 in cold condition, followed by part 2 in hot condition. |
| Class 3: |  |
| Subclass 3-1: | part 1 in cold condition, followed by part 2 in hot condition, followed by part 3 reduced speed in hot condition. |
| Subclass 3-2: | part 1 in cold condition, followed by part 2 in hot condition, followed by part 3 in hot condition. |

“

Justification: The amended table links the (sub)classes with the applicable test cycle parts to be run.

Section B. 6.5.5.2.1.2., amend to read:

“6.5.5.2.1.2.	Downshift speeds (vi→i-1) in km/h during cruise or deceleration phases in gears 3 (3rd gear) to ng shall be calculated using the following formula:

Equation 6-3:

, i = 4 to ng

Equation 6-4:

“

Equations in section 6 have to be renumbered accordingly.

Justification: An additional equation (6-4) is needed to ensure that downshift and upshift speeds are aligned.

Section B. 6.5.5.2.3.1, amend to read:

“6.5.5.2.3.1.The gear choice has then to be modified according to the following requirements:

a)	No gearshift at a transition from an acceleration phase to a deceleration phase: keep the gear that was used for the last second of the acceleration phase also for the following deceleration phase unless the speed drops below a downshift speed.

b)	No upshifts during deceleration phases.

c)	No gearshift in cycle phases, where "no gearshift" is indicated.

d)	No downshift to first gear at a transition from a deceleration or a cruise phase to an acceleration phase, if "no use of 1. gear" is indicated.

e)	If a gear is used for only one second, this gear shall also be assigned to the following second.  Since it could happen that the modifications according to this criterion create new phases where a gear is used for only one second, this modification step has to be applied several times.

[f)	Upshifts from gear i to gear i+1 lasting for up to two seconds followed by gear i again shall be replaced by gear i.

g)	Downshifts from gear i to gear i-1 lasting for up to two seconds followed by gear i again shall be replaced by gear i.

h)	The difference between the vehicle speeds

v3→2 and v2->cl,

v4→3 and v3→2,

v5→4 and v4→3,

v6→5 and v5→4,

shall be at least 5 km/h. Corrections have to be related to v2->cl.]

“

Justification: Additional rules are required to prevent unrealistic gearshift sequences.

Note: All of the above proposed amendments to the gearshift prescriptions are subject to final review by WMTC FE experts. Additional minor amendments are also envisaged (eg. downshift sequences). Also Annex 13 will be amended accordingly to include a description of the Indian gearshift behaviour.

Section B.6.5.6.1, amend to read:

“6.5.6.1.	Chassis dynamometer setting derived from on-road coast down measurements

To use this alternative on road coast down measurements have to be carried out as specified in Annex 7.”

Justification: Correction of typing error.

Section B.8.1.1.4.4, amend to read:

“DF	is the coefficient defined in paragraph 8.1.1.4.6 below.”

Justification: Correction of paragraph referencing.

Section B. Annex 5, figure A5-1, substitute:

“

”

Justification: Amendment of test cycle part traces in line with cycle module modifications.

Section B. Annex 5, figure A5-2, substitute:

“

”

Justification: Amendment of test cycle part traces in line with cycle module modifications.

Section B. Annex 5, Tables A5-1 to A5-15, substitute:

Table A5-1: Cycle part 1, 1 to 120 s

Table A5-2: Cycle part 1, 121 to 240 s

Table A5-3: Cycle part 1, 241 to 360 s

Table A5-4: Cycle part 1, 361 to 480 s

Table A5-5: Cycle part 1, 481 to 600 s

Table A5-6: Cycle part 1, reduced speed, 1 to 120 s

Table A5-7: Cycle part 1, reduced speed, 121 to 240 s

Table A5-8: Cycle part 1, reduced speed, 241 to 360 s

Table A5-9: Cycle part 1, reduced speed, 361 to 480 s

Table A5-10: Cycle part 1, reduced speed, 481 to 600 s

Table A5-11: Cycle part 2, 1 to 120 s

Table A5-12: Cycle part 2, 121 to 240 s

Table A5-13: Cycle part 2, 241 to 360 s

Table A5-14: Cycle part 2, 361 to 480 s

Table A5-15: Cycle part 2, 481 to 600 s

Table A5-16: Cycle part 2, reduced speed, 1 to 120 s

Table A5-17: Cycle part 2, reduced speed, 121 to 240 s

Table A5-18: Cycle part 2, reduced speed, 241 to 360 s

Table A5-19: Cycle part 2, reduced speed, 361 to 480 s

Table A5-20: Cycle part 2, reduced speed, 481 to 600 s

Table A5-21: Cycle part 3, 1 to 120 s

Table A5-22: Cycle part 3, 121 to 240 s

Table A5-23: Cycle part 3, 241 to 360 s

Table A5-24: Cycle part 3, 361 to 480 s

Table A5-25: Cycle part 3, 481 to 600 s

Table A5-26: Cycle part 3, reduced speed, 1 to 120 s

Table A5-27: Cycle part 3, reduced speed, 121 to 240 s

Table A5-28: Cycle part 3, reduced speed, 241 to 360 s

Table A5-29: Cycle part 3, reduced speed, 361 to 480 s

Table A5-30: Cycle part 3, reduced speed, 481 to 600 s

Justification: Amendment of test cycle second by second data tables in line with module modifications.

Note: The above tables will be reformatted to start the time column from 0 s.

- Amendments to the Technical Report (ECE/TRANS/180/Add.2/Appendix 1)

Note: The text of the Technical Report will be updated to include an explanation of all the points included in the amendments to the GTR.

# Text boxes

Figu

re 6

-

1

: vehicle classification

0

10

20

30

40

50

60

70

80

90

100

110

120

130

140

150

0

150

300

450

600

750

900

1050

1200

1350

1500

engine capacity in cm

3

max. vehicle speed in km/h

1

3

-

1

2

-

1

2

-

2

3

-

2

1