| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.15/2008/12 31 July 2008 ENGLISH Original: FRENCH |

###### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Eighty-fifth session
Geneva, 27-31 October 2008
Item 5 of the provisional agenda

# Proposals for amendments to Annexes A and B of ADR

## Electrical connections under 9.2.2.6.3

## Transmitted by the Government of France*

SUMMARY

Executive summary: This proposal is aimed at providing a transitional provision for existing EX/III and FL vehicles that do not meet the requirements of 9.2.2.6.3 adopted for ADR 2011, and at updating the reference to the ISO 7638 standard.

Action to be taken: Introduce a transitional measure in 1.6.5 and amend 9.2.2.6.3.

Related documents: ECE/TRANS/WP.15/2008/7, ECE/TRANS/WP.15/197, paras. 39 and 40.

### Introduction

1.	At its May 2008 session, the Working Party adopted France’s proposal (ECE/TRANS/WP.15/2008/7) aimed at making it mandatory to equip vehicles with electrical connections meeting the ISO 12098:2004 or ISO 7638:1997 standards.

2.	The following text was adopted in square brackets, as several delegations emphasized the importance of accompanying this new requirement with an appropriate transitional measure:

[9.2.2.6.3	Amend the last sentence to read as follows:

“Connections shall be in conformity with ISO 12098:2004 or ISO 7638:1997”.]

3.	We propose providing a transitional measure to allow existing vehicles to continue circulating without modification.

4.	Furthermore, we propose updating the reference to ISO 7638, the latest applicable version of which dates from 2003.

### Proposals

5.	In 9.2.2.6.3, Electrical connections, replace the last sentence with the following:

“Connections shall be in conformity with ISO 12098:2004 or ISO 7638:2003”.

6.	Add the following paragraph to 1.6.5:

“1.6.5.x	EX/III and FL vehicles registered or brought into service before 1 July 2011, whose electrical connections do not meet the requirements of 9.2.2.6.3, but meet the requirements applicable before 31 December 2010, may still be used.”

### Justification

Safety:	Improves safety.

Feasibility: 	No problem.

Enforcement:	This clarification makes it possible to avoid problems of enforcement of the ADR requirements for electrical connections.

-----

# Footnotes

*  The present document is submitted in accordance with paragraph 1 (c) of the terms of reference of the Working Party, as contained in document ECE/TRANS/WP.15/190/Add.1, which provides a mandate to “develop and update the European Agreement concerning the International Carriage of Dangerous Goods by Road (ADR)”.