| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2008/58 10 April 2008 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-fifth session

Geneva, 24-27 June 2008

Item 4.2.2 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Supplement 4 to the 06 series of amendments to Regulation No. 14

(Safety-belt anchorages)

Submitted by the Working Party on Passive Safety (GRSP) (/

The text reproduced below was adopted by GRSP at its forty-second session.  It is based on ECE/TRANS/WP.29/GRSP/2007/16, not amended.  It is submitted to WP.29 and AC.1 for consideration (ECE/TRANS/WP.29/GRSP/42, para. 29).

Paragraph 6.6.4.2., amend to read:

"6.6.4.2. 	…….. Full application of the load shall be achieved as rapidly as possible, and within a maximum load application time of 30 seconds.  However, the manufacturer may request the application of the load to be achieved within 2 seconds.  The force shall be maintained for a minimum period of 0.2 s.

All measurement shall…. "

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.