| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2008/97 24 July 2008 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-sixth session

Geneva, 11-14 November 2008

Item 4.2.26 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Supplement 1 to the 04 series of amendments to Regulation No. 105

(ADR vehicles)

Submitted by the Working Party on General Safety Provisions (/

The text reproduced below was adopted by the Working Party on General Safety Provisions (GRSG) at its ninety-fourth session (ECE/TRANS/WP.29/GRSG/73, para. 27).  It is based on ECE/TRANS/WP.29/GRSG/2008/11, superseded by GRSG-94-30, as reproduced in Annex II of the report.  It is submitted to WP.29 and AC.1 for consideration.

Paragraph 1., amend to read:

"1.	The provisions of this Regulation apply to the construction of base vehicles of motor vehicles of category N and their trailers of category O, intended for the transport ..."

[Paragraph 3.2.2., amend to read:

"3.2.2.	Vehicle designation, according to Paragraph 9.1.1.2 of the ADR (EX/II, EX/III, AT, FL, OX, MEMU);"

Paragraph 4.4.3., add a new sentence, to read:

"4.4.3.	An additional symbol separated from the approval number and consisting of the symbol identifying the vehicle designation in accordance with paragraph 9.1.1.2. of the ADR.  In the case of MEMU vehicles, the identifying symbol may be "EX/III". "

Paragraph 5.1., amend to read (footnote 3/ remains unchanged):

"5.1.	Vehicles shall, depending on the vehicle designation, comply with the provisions below as assigned in the table overleaf. 3/

For the purpose of this Regulation, MEMU vehicles shall comply with the requirements applicable to EX/III vehicles.

Vehicles approved as being in compliance with the requirements applicable to EX/III under this Regulation, as amended by the 04 series of amendments, shall be deemed to comply with the requirements applicable to MEMU vehicles."

Paragraph 5.1.1.6.3., amend to read:

" ... accidental disconnection. Examples of appropriate connections are given in ISO 12098:2004 and ISO 7638:1997."

Paragraph 5.1.2.4., amend to read:

" … to the load through heating or ignition.  In the case of EX/II, EX/III and MEMU vehicles the engine shall be of compression-ignition construction."

Paragraph 5.1.2.5., amend to read:

" ... The exhaust system of EX/II, EX/III and MEMU vehicles shall be so constructed and situated ..."

Paragraph 5.1.3.1., amend to read:

"5.1.3.1.	EX/III, AT, FL, OX and MEMU vehicles shall fulfill all ..." ]

Annex 1,

Item 2., amend to read:

"2.	Vehicle category:  N1, N2, N3, O1, O2, O3, or O4:

(chassis-cab, tractor for semi-trailer, trailer-chassis, trailer with a self-supporting body 2/)."

[Item 4., amend to read:

"4.	Vehicle designation (EX/II, EX/III, FL, OX, AT, MEMU):" ]

________________

Note by the secretariat:  GRSG agreed that WP.29 would decide about the deletion of the square brackets.

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.