REGULATIONS Nos. 13 AND 13-H (Braking)

Emergency Stop Signal

# INDIA’S COMMENTS ON PROPOSED AMENDMENTS TO REGULATIONS Nos. 13 and 13-H by ECE/TRANS/WP.29/GRRF/2008/17 of OICA

India suggests the following proposal for better clarity:

#### Proposal for draft amendments to Regulation No. 13-H

A.	PROPOSAL

Paragraph 5.2.23.1., amend to read:

"5.2.23.1.	The signal shall not be activated below 6m/s2 by the application of the service brake system for vehicles of M1 and N1 categories.

The signal shall be ……."

OR

"5.2.23.1.	The signal shall be activated by the application of the service braking system at a deceleration of or above 6 m/s2; as follows:

|  | Shall be activated at or above |
| --- | --- |
| M1, N1 | 6 m/s2 |

The signal shall be ……."

OR

"5.2.23.1.	The signal shall be activated on or above 6m/s2 by the application of the service brake system for vehicles of M1 and N1 categories.

The signal shall be ……."

Paragraph 5.2.23.2., amend to read:

"5.2.23.2.	The following conditions may also be used:

- The signal shall not be activated below 6m/s2 by the application of the service braking system in such a manner that it would produce, in an unladen condition and engine disconnected, under the test conditions of Type-0 as described in Annex 3, for M1 & N1 Category.

The signal shall be ……."

OR

"5.2.23.2.	The following conditions may also be used:

- The signal may be activated by the application of the service braking system in such a manner that it would produce, in an unladen condition and engine disconnected, under the test conditions of Type-0 as described in Annex 3, a deceleration of or above 6 m/s2; as follows:

|  | Shall be activated at or above |
| --- | --- |
| M1, N1 | 6 m/s2 |

OR

5.2.23.1.	The signal shall be activated at or above 6 m/s2 deceleration by the application of the service brake System for vehicles of M1 and N1 category in such a manner that it would produce, in an unladen condition and engine disconnected, under the test conditions of Type-0 as described in Annex 3.

B.	JUSTIFICATION

India proposes to have a better clarity to the OICA proposal for aligning the Emergency Stop Signal (ESS) requirements with those of Regulation No. 13.

- - - - -