| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/84 29 July 2009 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-ninth session

Geneva, 10 - 13 November 2009

Item 4.2.6 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Corrigendum 4 to the 03 series of amendments to Regulation No. 19

(Front fog lamps)

Submitted by the Working Party on Lighting and Light-Signalling (/

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-first session.  It is based on ECE/TRANS/WP.29/GRE/2009/29, not amended.  It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/61, para. 28).

Paragraph 6.4.3., amend to read:

"6.4.3.	Photometric requirements

When so adjusted, the front fog lamp shall meet the photometric requirements in the table below (refer also to Annex 4, paragraph 2.2. of this Regulation):

| Designated lines or zones | Vertical position */ above h + below h - | Horizontal position */ left of v: - right of v: + | Luminous intensity (in cd) | To comply |
| --- | --- | --- | --- | --- |
| Point 1, 2 **/ | + 60° | ± 45° | 60 max | All points |
| Point 3, 4 **/ | + 40° | ± 30° |  |  |
| Point 5, 6 **/ | + 30° | ± 60° |  |  |
| Point 7, 10 **/ | + 20° | ± 40° |  |  |
| Point 8, 9 **/ | + 20° | ± 15° |  |  |
| Line 1 **/ | + 8° | - 26° to + 26° | 90 max | All line |
| Line 2 **/ | + 4° | - 26° to + 26° | 105 max | All line |
| Line 3 | + 2° | - 26° to + 26° | 170 max | All line |
| Line 4 | + 1° | - 26° to + 26° | 250 max | All line |
| Line 5 | 0° | - 10° to + 10° | 340 max | All line |
| Line 6 ***/ | - 2.5° | from 5° inwards to 10° outwards | 2,000 min | All line |
| Line 7 ***/ | - 6.0° | from 5° inwards to 10° outwards | < 50 per cent of max. on line 6 | All line |
| Line 8L and R ***/ | -1.5° to - 3.5° | - 22° and + 22° | 800 min | One or more points |
| Line 9L and R ***/ | -1.5° to - 4.5° | - 35° and + 35° | 320 min | One or more points |
| Zone D ***/ | - 1.5° to - 3.5° | - 10° to + 10° | 8,400 max | Whole zone |
| */ The co-ordinates are specified in degrees for an angular web with a vertical polar axis. **/ See paragraph 6.4.3.4. ***/ See paragraph 6.4.3.2. |

"

Paragraph 6.4.3.2., amend to read:

"6.4.3.2. 	At the request of the applicant, two front fog lamps constituting a matched pair corresponding to paragraph 4.2.2.5. may be tested separately. In this case the specified requirements for lines 6, 7, 8, 9 and the Zone D in the table in paragraph 6.4.3. apply to half the sum of readings of the right-hand and left-hand side front fog lamp. However each of the two front fog lamps shall meet at least 50 per cent of the minimum value required for line 6."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.