Proposal for corrigendum to document ECE/TRANS/WP.29/2009/39

(Regulation No. 107)

A.	PROPOSAL:

Annex 8, paragraph 3.6.1., correct to read:

"3.6.1.	For each wheelchair user provided for in the passenger compartment there shall be a special area at least 750 mm wide and 1300 mm long.  The longitudinal plane of the special area shall be parallel to the longitudinal plane of the vehicle and the floor surface of the special area shall be slip resistant and the maximum slope in any direction shall not exceed 5 percent.  In the case of a rearward facing wheelchair complying with the requirements specified in paragraph 3.8.4., the slope in the longitudinal direction shall not exceed 8 per cent provided that this slope inclines upwards from the front end to the rear end of the special area.

In the case of a wheelchair space designed for a forward facing wheelchair, the top of preceding seat-backs may intrude into the wheelchair space if a clear space is provided as shown in Annex 4, Figure 22."

B.	JUSTIFICATION:

One part of the second sentence of paragraph 3.6.1. agreed by GRSG has been inadvertently   deleted by the secretariat when preparing the document.  The deleted text is reintroduced in bold characters.

- - - - -