Proposal for corrigendum to ECE/TRANS/WP.29/GRE/2009/20

In view of the corrigendum proposed to Regulation 48 Supplement 3 to the 04 Series, above, it is also necessary to introduce a corresponding amendment to the proposal in GRE/2009/20 as follows:

Paragraph 6.22.9.3., amend to read:

"6.22.9.3. The aggregate maximum intensity of the lighting units that can be energized simultaneously to provide the main-beam lighting or its modes, if any, shall not exceed 300,000 cd  430,000 cd, which corresponds to a reference value of 75  100.

This maximum intensity shall be obtained by adding together the individual reference marks indicated on the several installation units that are simultaneously used to provide the main-beam."

- - - - -