| Transmitted by the expert from India | UInformal Document No. GRRF-65-29 (65th GRRF, 2-6 February 2009, Agenda item 3 g) |
| --- | --- |

REGULATIONS Nos. 13 AND 13-H (Braking)

Brake Assist System (BAS)

INDIA’S COMMENTS ON PROPOSED AMENDMENTS TO REGULATIONS No. 13-H

A.    PROPOSAL :

Proposed modification to document ECE/TRANS/WP.29/GRRF/2008/15 submitted by the experts of the informal working group on Brake Assist Systems.

4.2  Test 2: for activation of BAS

,

Second Paragraph of this clause should read:

It shall be demonstrated to the satisfaction of the Technical Service that the BAS activates under the conditions specified by the manufacturer in accordance with paragraph 22.1.2. or 22.1.3 of Annex 1.

Third Paragraph should read:

After t = t0 + 0.8 s and until the vehicle has slowed down to a speed of 15 km/h, the brake pedal

force shall be maintained in a corridor between FABS, upper and FABS, lower., Where where      FABS, upper is 0.7 FABS and FABS, lower is 0.5 FABS.

Following clause should read:

4.3. Data evaluation

The presence of BAS 'B' is proven proved if a mean deceleration (aBAS) of at least 0.85 ∙ aABS is maintained from the time when t = t0 + 0.8 s to the time when the vehicle speed has been reduced to 15 km/h.

Figure 2: Example of test 2 of a category "B" BAS system

1/2

Annex 10, Appendix 1

METHOD FOR DETERMINATION OF FABS AND aABS

Following clause should read:

1.3. The example in Figure 3 has its origin at the time t0 crossing the aABS line at 2 seconds.  Once full deceleration has been achieved the pedal travel Sp shall not be decreased for at least 1 s.  The time of full activation of the ABS system is defined as the time when pedal force FABS is achieved.  The measurement shall be within the corridor for variation of increase in decleration variance of deceleration increase (see Figure 3).

B.   JUSTIFICATION :

India proposes the changes in italics to have a better clarity to the proposal from the experts of the informal working group on Brake Assist Systems for draft amendments to R13H on Brake Assist Systems (BAS). The suggested corrections are basically editorial in nature.

- - - - -

2/2

# Text boxes

t0 + 0.8 seconds

Initial pedal force

FABS,lower

FABS,upper

t0

aBAS

aABS

Phase of BAS-evaluation

(ending at speed of 15 km/h)

Phase of panic pedal application

Deceleration ax

Brake pedal force F

deceleration

time

Brake pedal force