# Proposal for a corrigendum to ECE/TRANS/WP29/GRRF/2009/10 (TPMS)

Amendments to the current proposal are indicated in bold and strike-out characters

A.	PROPOSAL

Paragraph 6.2.5.4., amend to read:

“6.2.5.4.	In both cases above, a tolerance of [5 per cent] of Ptest Pwarm shall be added to the deflation percentages for the actual test.]”

B.	JUSTIFICATION

In working document TPM_04_02, the definition of Ptest was the same as the current definition of Pwarm. This document served as the base for discussion at the final meeting.

"2.8. Test Pressure (Ptest) means the actual pressure of the tyre(s) selected to be deflated during the test procedure."

For this reason, at the final meeting of the GRRF informal group, it was decided to refer the additional tolerance of 5% with respect to Ptest. However, the definition of Ptest was changed in the final proposal doc GRRF/2009/10:

"2.5. "Test Pressure (Ptest)" means the actual pressure of the tyre(s) selected for each tyre position after deflation during the test procedure."

There is an impact of this change to the tolerance which was not intended by the informal group. In order to keep the same value for the tolerance, the 5% tolerance should continue to relate to Pwarm (which is the former " Ptest ").

In addition, for scientific reasons, it is convenient that the test pressure and its tolerance refer to the same value. The whole test method is constructed taking Pwarm as the reference pressure for testing. It is hence consistent that the tolerance is calculated relative to this same reference pressure Pwarm.

For the above reasons it is recommended to refer the tolerance mentioned in paragraph 6.2.4.5. to Pwarm rather than Ptest.

- - - - -