PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 80

(Seat anchorages in large passenger vehicles)

Submitted by the experts from Germany and Belgium

Note: The text reproduced below was prepared by the experts from Germany and Belgium in order to introduce prescriptions for side-facing seats in vehicles of category M3 (Class II, III and B).

The modifications to the current text of the Regulation are marked in bold and strikethrough characters.

The modifications to the current text of the regulation are marked in bold characters or marked as strikethrough.

A.	PROPOSAL

Insert new line in "Regulation" of "Contents"

"Appendix 7		Requirements for the safeguarding of passengers in side-facing seats 					according to paragraph 7.4"

Insert new paragraphs 1.4, 1.5, 1.6 to read:

"1.4		The installation of side-facing seats shall be prohibited in vehicles of categories 			M2 (class B) and M3 (of class II, III or B).

1.5		Paragraph 1.4 shall not apply to vehicles of category M3 (of class II, III or B) of a 			technically permissible maximum laden mass exceeding 10 tonnes with side-facing 			seats provided the requirements of paragraph 7.4. are met.

1.6 		Paragraph 1.4 shall not apply to ambulances or to vehicles intended for use by the 			armed services, civil defence, fire services and forces responsible for maintaining 			public order,"

Paragraph 2.5., amend to read:

"2.5.	… more adult persons. Depending on its orientation, a seat is defined as follows:"

Insert new paragraphs 2.5.1. to 2.5.3., to read:

"2.5.1. 	"Forward-facing seat"

means a seat which can be used whilst the vehicle is in motion and which faces 			towards the front of the vehicle in such a manner that the vertical plane of symmetry 		of the seat forms an angle of less than + 10° or - 10° with the vertical plane of 				symmetry of the vehicle;

2.5.2.		"Rearward-facing seat"

means a seat which can be used whilst the vehicle is in motion and which faces 			towards the rear of the vehicle in such a manner that the vertical plane of symmetry 		of the seat forms an angle of less than + 10° or – 10° with the vertical plane of 			symmetry of the vehicle;

2.5.3.		"Side-facing seat"

means a seat which, with regard to its alignment with the vertical plane of symmetry 		of the vehicle, does not meet either of the definitions given in 2.5.1 or 2.5.2 above;"

Paragraph 2.20. amend to read:

"2.20.		"Manikin",
		a manikin corresponding to the specifications for HYBRID II or III 2) for forward-				facing seats; or a manikin corresponding to the specifications for side impact dummy 		according to Regulation No. 95, annex 6 for side facing seats;"

Paragraph 5.1. amend to read:

"5.1.		Each type of forward facing seat shall be subject to the test requirements of either 			appendix 1 (dynamic test) or appendices 5 (static test) and 6 at the request of the 				manufacturer.

Paragraph 7.2.1. amend to read:

"7.2.1.		Test 1 shall not apply where the rear of the seat cannot be struck by an unrestrained 			passenger (i.e. there is no forward- or side-facing seat directly behind the seat to be 			tested).

Paragraph 7.2.2.2. amend to read:

"7.2.2.2.	if the seat behind is a forward facing seat fitted with a 3-point belt with anchorages that 			comply fully with Regulation No. 14 (without derogation); or"

Paragraph 7.3.1. amend to read:

"7.3.1.		The test of appendix 5 shall not apply if the rear of the seat cannot be struck by an 			unrestrained passenger (i.e. there is no forward- or side-facing seat directly behind the seat 		to be tested)."

Paragraph 7.3.2.2. amend to read:

"7.3.2.2.	if the seat behind is a forward facing seat fitted with a 3-point belt with anchorages that 			comply fully with Regulation No. 14 (without derogation)."

Insert new paragraph 7.4, to read:

"7.4.		The installation of side-facing seats shall be subject to the following conditions:

7.4.1.		the seat shall have a reference height of at least 1 m; and

7.4.2.	the plane through the H-points of adjacent side-facing seats shall be

parallel to the reference plane;

7.4.3.		the horizontal distance between the H-point line between

two adjacent side facing seats shall not exceed 725 mm and

shall not be less than 450 mm, measured horizontally between the vertical
	longitudinal planes passing through the centres of these seating positions,. (see 		Appendix 7, figure 1); and

7.4.4.		the passengers in side-facing seats shall be safeguarded by a vehicle part (e.g. 			partition, wall or seat back of a forward-facing seat) forward of the foremost side-			facing 	seat. This vehicle part shall meet the requirements of Appendix 7."

Title of appendix 1, amend to read:

"Appendix 1

TEST PROCEDURES FOR SEATS ACCORDING TO PARAGRAPH 5

AND/OR ANCHORAGES ACCORDING TO PARAGRAPH 6.1.2. AND/OR THE INSTALLATION OF SIDE-FACING SEATS ACCORDING TO PARAGRAPH 3 OF APPENDIX 7."

Appendix 1, insert paragraph 1.1.2.2. to read

1.1.2.2.	For a manikin in an auxiliary forward-facing seat the following biomechanical 			acceptability criteria have to be met:

Appendix 1, renumber paragraphs 1.1.2.2 – 1.1.2.3

1.1.2.2.1	the head acceptability criterion HIC is less than 500;

1.1.2.2.2.	the thorax acceptability criterion (ThAC) is less than 30g except for periods totalling less 			than 3 ms (g = 9.81 m/s);

1.1.2.2.3.	the femur acceptability criterion (FAC) is less than 10kN and the value of 8 kN is not 			exceeded for periods totalling more than 20 ms.

Appendix 1, insert new paragraph1.1. 2.3. to read

1.1.2.3.	For a manikin in an auxiliary side-facing seat the following biomechanical 				acceptability criteria have to be met:

1.1.2.3.1.	the head acceptability criterion HIC is less than 500;

1.1.2.3.2.	the thorax acceptability criteria:

(a) Rib Deflection Criterion (RDC) less than or equal to 42 mm;

(b) Soft Tissue Criterion (VC) less or equal to 1.0 m/sec;

1.1.2.3.3.	the pelvis acceptability criterion:

Pubic Symphysis Peak Force (PSPF) less than or equal to 6 kN;

1.1.2.3.4.	the abdomen acceptability criterion:

Abdominal Peak Force (APF) less than or equal to 2.5 kN internal force (equivalent 			to external force of 4.5 kN).

Appendix 1, paragraph 3.3.2. amend to read

"3.3.2.		Irrespective of the seating position of the dummy, the angle between the upper arm and the 		torso arm reference line on each side shall be 40° ± 5°. The torso arm reference line is 			defined as the intersection of the plane tangential to the front surface of the ribs and the 			longitudinal vertical plane of the dummy containing the arm. The legs shall be extended to 		the maximum and shall, if possible, be parallel; the heels shall touch the floor."

Appendix 1, paragraph 3.3.3.3.2. amend to read

3.3.3.3.2.	without the torso moving, the head shall be placed in a position such that the platform 			supporting the measuring instruments contained in the head is horizontal and that the 			median sagittal plane of the head is parallel to that of the vehicle (for side-facing seats, 			the median saggital plane of the head shall be parallel to the vertical median plane of 		the seat).

Appendix 1, insert new paragraph 3.5.3. to read

"3.5.3.		Test 2 may also be applied to vehicle parts other than a seat, as referred to in 				Paragraph 8.1.7 of Regulation No. 16 and Paragraph 5.3.5. of Regulation No. 14."

Renumber old paragraph 3.5.3 to 3.5.4.

3.5.3.4.	In the case where Test 2 is conducted with the manikin restrained by a 3-point belt and the 		injury criteria are not exceeded, the auxiliary seat shall be considered to have met the 			requirements relating to the static test loads and movement of the up-per anchorage during 		the test specified in Regulation No. 14 with regard to this installation.

Appendix 1, insert new paragraph 3.5.5. to read

"3.5.5		Test 2 may also be applied to side-facing seats. In this case the auxiliary seat as 			mentioned in Paragraph 3.2 shall be a side-facing seat and shall be located as 			specified in Appendix 7."

Appendix 3, amend paragraph 2.2.2 to read:

2.2.2.		Measurements in the thorax of the manikin

The resultant acceleration at the centre of gravity shall be measured with a CFC of 180. 			The deflection of the ribs and the viscous criterion (VC) shall be measured with a 			CFC of 180.

Appendix 3, insert new paragraphs 2.2.4 – 2.2.5. to read:

2.2.4	Measurements in the abdomen of the manikin

The abdominal forces shall be measured with a CFC of 600.

2.2.5	Measurements in the pelvis of the manikin

The pubic force shall be measured with a CFC of 600.

Appendix 4, amend to read:

Appendix 4

DETERMINATION OF ACCEPTABILITY CRITERIA

1.	Frontal Impact (forward-facing seat)

1.1.	Head acceptability criterion (HIC)

1.1.1.	This injury criterion (HIC) is calculated on the basis of the resultant triaxial acceleration measured 	according to appendix 3, paragraph 2.2.1. by the following expression:

in which t1 and t2 are any values of time during the test, HIC being maximum value for and 	interval t1, t2. The values of t1 and t2 are expressed in seconds.

1.2.	Thorax acceptability criterion (ThAC)

1.2.1.	This criterion is determined by the absolute value of resultant acceleration, ex-pressed in g and 	measured according to Appendix 3, paragraph 2.2.2, and by the ac-celeration period, expressed in 	ms.

1.3.	Femur acceptability criterion (FAC)

This criterion is determined by the compression load expressed in kN, transmitted axially on each 	femur of the manikin and measured according to appendix 3, paragraph 2.2.3., and by the 	duration of the compression load, expressed in ms.

2.	Side Impact (side-facing seat)

2.1.	Head acceptability criterion (HIC)

see App. 4, 1.1.

2.1.	Thorax acceptability criterion

2.1.1.	Chest deflection:

the peak chest deflection is the maximum value of deflection on any rib as deter-mined by 	the thorax displacement transducers.,

2.1.1.	Viscous criterion (VC):

the peak viscous response is the maximum value of VC on any rib which is calculated from 	the instantaneous product of the relative thorax compression related to the half thorax and 	the velocity of compression derived by differentiation of the compression. For the purposes 	of this calculation the standard width of the half thorax rib cage is 140 mm.

where D (metres) = rib deflection

The calculation algorithm to be used is set out in Regulation No. 95, annex 4, appendix 2.

2.2.	Abdomen acceptability criterion

The peak abdominal force is the maximum value of the sum of the three forces measured by 	transducers mounted 39 mm below the surface on the crash side.

2.3.	Pelvis acceptability criterion

The pubic symphysis peak force (PSPF) is the maximum force measured by a load cell at the 	pubic symphysis of the pelvis.

Appendix 6, insert new paragraph 3. to read:

3.		This test may be applied to parts of a vehicle other than a seat (Paragraph 3.5.3 of 	Appendix 1 and Paragraph 2.3 of Appendix 7).

Insert new Appendix 7, to read:

"Appendix 7

REQUIREMENTS FOR THE SAFEGUARDING OF PASSENGERS IN SIDE-FACING SEATS ACCORDING TO PARAGRAPH 7.4.4.

1.		The distance between the foremost side-facing seat and the vehicle part forward of 			this foremost side-facing seat shall not exceed 450 mm.  All measurements are to be 			taken 1000 mm above the foot contact area of the foremost side-facing seat
		(see Figure 1).

2.		The vehicle part (e.g. partition, wall or seat back of a forward facing seat) in front of 		the foremost side-facing seat shall fulfil the following requirements in order to 			safeguard the passenger in that foremost side-facing seat (see Figure 2):

2.1.		The height of the vehicle part, based on the foot contact area of the foremost 				side-facing seat, must not be less than 1020 mm; and

2.2.		the effective impact surface of the vehicle part has a width of 200 mm and a height of 		580 mm. This surface shall be positioned so that the vertical centre-line is located 50 			mm behind the H-point of the foremost side-facing seat; and

2.3.		the corresponding surface of the vehicle part in place projected onto a vertical plane 		through this H-point, shall cover at least 95% of the effective impact surface. This 			vehicle part shall fulfil the energy absorption requirement by appendix 6.

2.3.1.		If there is a gap in the corresponding surface (typically two forward-facing seats with 		a gap in between) a distance shall be determined for each gap by means of a sphere 			having a diameter of 165 mm. The sphere shall be put into contact with the gap in a 			point of the gap area which allows the maximum sphere intrusion, considering no 			load is to be applied. The distance between the two points of contact of the sphere 			must be less than 60 mm;

3. 		At the manufacturers choice a test according to appendix 1 with the appropriate 			manikin for side-facing seats may be conducted."

B. 		Justification

In order to take into account the installation of side-facing seats under certain conditions, the proposal introduces the necessary requirements.

- - - - -

# Text boxes

min. 450 mm
max. 725 mm

Figure 2 :	positioning requirements for the vehicle part forward of the foremost side-facing seat

Figure 1,	Positioning requirements for side-facing seats

1000 mm

min. 450 mm