|  | United Nations | ECE/TRANS/WP.29/2010/125 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 4 August 2010 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-fifty-second session

Geneva, 9–12 November 2010

Item 4.8.2 of the provisional agenda

1958 Agreement – Consideration of draft corrigenda
to existing Regulations proposed by GRSP

Proposal for Corrigendum 2 to the 06 series of amendments to Regulation No. 16 (Safety-belts)

Submitted by the Working Party on Passive Safety *

The text reproduced below was adopted by the Working Party on Passive Safety (GRSP) at its forty-seventh session. It is based on ECE/TRANS/WP.29/GRSP/2010/10, not amended (ECE/TRANS/WP.29/GRSP/47, para. 22). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Paragraph 8.1.1., amend to read:

“8.1.1.	With the exception of seating intended solely for use when the vehicle is stationary, the seats of vehicles of categories M1, M2 (of Class III or B 9/), M3 (of Class III or B 9/) and N shall be equipped with safety-belts or restraint systems which satisfy the requirements of this Regulation.

Contracting Parties applying this Regulation may demand the installation of safety belts on M2 and M3 vehicles belonging to Class II.

When fitted, the safety belts and/or restraint systems in Class I, II or A vehicles belonging to category M2 or M3 have to be in compliance with the requirements of this Regulation.

Contracting Parties may, under national law, allow the installation of safety belts or restraint systems other than those covered by this Regulation provided that they are intended for disabled people.

Restraint systems complying with the provisions of Annex 8 of the 02 series of amendments to Regulation No. 107 are exempted from the provisions of this Regulation.

Class I, or A vehicles belonging to category M2 or M3 may be fitted with safety belts and/or restraint systems conforming to the requirements of this Regulation.”

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.