| Transmitted by the experts from OICA | Informal document No. GRSG-98-13 (98th GRSG, 3-7 May 2010 agenda item 10) |
| --- | --- |

Proposal for amendment to Regulation No. 121
(Identification of controls, tell-tales and indicators)

A.	PROPOSAL

Table 1, item 28, amend to read (addition of a reference to the existing footnote 18/):

| No. | Column 1 | Column 2 | Column 3 | Column 4 | Column 5 |
| --- | --- | --- | --- | --- | --- |
|  | ITEM | SYMBOL 2/ | FUNCTION | ILLUMINATION | COLOUR |
| …. | …. | …. | …. | …. | …. |
| 28 | Parking brake applied | ,18/ | Tell-tale | Yes | Red |
| …. | …. | …. | …. | …. | …. |

18/	Symbol may be shown in other colours than specified in column 5 in order to convey different meanings according to the general colour coding as proposed in paragraph 5. of standard ISO.

B.	JUSTIFICATION

Regulations Nos. 13/13-H specify which conditions must be indicated by red/yellow warning. The use of different symbols according to each specific condition is permitted. This proposal allows to use the indicated symbol for different meanings in other colours than red (e.g. yellow).

- - - - -