| Transmitted by the expert from Canada | Informal document No. GRSG-98-19 (98th GRSG, 3-7 May 2010, agenda item 10) |
| --- | --- |

Proposal for amendments to Regulation No. 121
(Identification of controls, tell-tales and indicators)

# A.	PROPOSAL

Table 1, amend to read:

| 43. | Electronic stability control system malfunction | or ESC | Tell-tale | Yes | Yellow |
| --- | --- | --- | --- | --- | --- |
| 44. | Electronic stability control system "OFF" | 20/ or ESC OFF | Control | Yes |  |
|  |  |  | Tell-tale | Yes | Yellow |
| 45. | Daytime running light |  | Tell-tale | Yes | Blue or Green |
| 46 | Automatic upper beam switching | or AUTO | Control | Yes |  |
|  |  |  | Tell-tale | Yes |  |
| 47 | Automatic lower beam switching | or | Control | Yes |  |
|  |  |  | Tell-tale | Yes |  |
| 48. | Automatic vehicle speed (cruise control) |  | Control | Yes |  |
|  |  |  | Tell-tale | Yes | Green |

20/ The English word “OFF” can be adjacent to the symbol Electronic stability control system malfunction.

B.	JUSTIFICATION

Table 1:

Symbols No. 44: In addition to the proposal from the expert of U.K. (addition of symbol no 43, see document ECE/TRANS/WP.29/GRSG/2010/12), symbol 44 has as well been added in Regulation No. 13-H.

Symbol No. 45: regulation 48 requires the installation of daytime running lamp. Although a tell-tale is optional, no symbol has been specified.

Symbol No. 46: GRE is in process of amending Regulation No. 48 to include specifications for automatic upper beam switching and this system will require a tell-tale.  As ISO has decided on the symbol to identify such system activation, it would be reasonable to assure that all drivers are uniformly informed of the system’s functioning.

Symbol No. 47: Regulation No. 48 requires that vehicles equipped with DRL must be also equipped with automatic headlamp (lower beam) switch. If all vehicles would be equipped with such automatic system, the argument could be made that a special indicator is not required. However, Regulation No. 48 allows for alternative options to the automatic headlamp switch. In view of this it would be prudent to uniformly inform drivers if the automatic system is activated or not.

Symbol No. 48: This ISO symbol is also proposed for the Canadian regulation to identify automatic vehicle speed system (cruise control).

- - - - -

# Text boxes

A