UN/SCETDG/40/INF.48

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 2 December 2011 Fortieth session Geneva, 28 November – 7 December 2011 Item 2 (c) of the provisional agenda Listing, classification and packing: miscellaneous

Amendment to P602 (alternative proposal to INF.28)

Transmitted by the European Chemical Industry Council (CEFIC)

Add the following sentence to the new 4.1.1.5.2 (new text underlined).

4.1.1.5.2.	Use of supplementary packagings within an outer packaging (e.g. an intermediate packaging or a receptacle inside a required inner packaging) additional to what is required by the packing instructions is authorized provided all relevant requirements are met, including 4.1.1.3, and, if appropriate, adequate cushioning is provided to protect against movement within the packaging.

For supplementary packagings that are used as receptacles inside required inner packagings, volume or filling limits otherwise applicable to the required inner packagings, shall be applicable to the supplementary packaging.

The capacity of the required inner packaging may be increased to accommodate the supplementary packaging and cushioning material.