|  | United Nations | ECE/TRANS/WP.29/2011/7 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 17 December 2010 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

153rd session

Geneva, 8–11 March 2011

Item 4.7.1 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 19 to the 02 series of amendments to Regulation No. 7 (Front and rear position lamps, stop lamps and end-outline marker lamps)

Submitted by the Working Party on Lighting and Light-Signalling (GRE)*

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-fourth session. It is based on informal document No. GRE-64-43 as reproduced in Annex VI to the report. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/64, para. 25).

Paragraph 6.1.6., amend to read:

"6.1.6.		When an assembly of two independent lamps to be type approved as "D" lamps having the same function is deemed to be a single lamp, it shall comply with the requirements for:

(a)	Maximum intensity if all lamps together are lit

(b)	Minimum intensity if either lamp has failed."

Paragraph 6.1.8., amend to read:

"6.1.8.		When all light sources are illuminated the maximum intensity specified for a single lamp shall not be exceeded while, in the case of a lamp marked "D", the maximum intensity specified for the lamp marked "D" shall not be exceeded."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.