|  | United Nations | ECE/TRANS/WP.29/2011/10 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 17 December 2010 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

153rd session

Geneva, 8–11 March 2011

Item 4.7.4 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 37 to the 03 series of amendments to Regulation No. 37 (Filament lamps)

Submitted by the Working Party on Lighting and Light-Signalling (GRE)*

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-fourth session. It is based on ECE/TRANS/WP.29/GRE/2010/51, not amended, on ECE/TRANS/WP.29/GRE/2010/35, as amended by Annex II to the report and on informal document No. GRE-64-39, as reproduced in Annex II to the report. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/64, para. 5).

Insert a new paragraph 3.1.10., to read:

"3.1.10. 	Filament light source (filament lamp): a light source where the element for visible radiation is one or more heated filaments producing thermal radiation."

Insert a new paragraph 3.2.3., to read:

"3.2.3. 	The filament(s) as specified in the data sheet of the relevant category in Annex 1 shall be the only element(s) of the filament lamp that generate and emit light when energised."

Paragraph 3.4.1., amend to read:

"3.4.1.	Filament lamps shall first be aged at their test voltage for approximately one hour. For dual-filament lamps, each filament shall be aged separately. In the case of filament lamps, for which more than one test voltage is specified, the highest test voltage value shall be used for ageing."

Paragraph 3.4.3., amend to read:

"3.4.3.	The position and dimensions of the filament shall be measured with the filament lamps being supplied with current at from 90 per cent to 100 per cent of the test voltage. In the case of filament lamps, for which more than one test voltage is specified, the highest test voltage value shall be used for measurement of the position and dimensions of the filament."

Paragraph 3.4.4., amend to read:

"3.4.4.	Unless otherwise specified, electrical and photometric measurements shall be carried out at the test voltage(s)."

Paragraphs 8.3. and 8.4., amend to read:

"8.3.	No filament lamps of the categories listed below shall be used in lamps submitted for type approval after the period following the entry into force of Supplements to 03 series of amendments, as indicated for each category in the table below:

| Category | Supplement | Period |
| --- | --- | --- |
| C21W | 28 | 12 months |
| P19W | [37] | 60 months |
| PC16W | [37] | 60 months |
| PCR16W | [37] | 12 months |
| PCY16W | [37] | 60 months |
| PR19W | [37] | 12 months |
| PR24W | [37] | 12 months |
| PSR19W | [37] | 12 months |
| PSR24W | [37] | 12 months |
| PY19W | [37] | 60 months |
| R2 | 28 | 12 months |
| S1 | 28 | 12 months |

8.4.	However, Contracting Parties applying this Regulation may continue to grant approvals for lamps in which filament lamps of categories listed below are used, provided that these…for the period after entry into force of the Supplements to the 03 series of amendments as indicated below:

| Category | Supplement | Period |
| --- | --- | --- |
| C21W | 28 | unlimited |
| P19W | [37] | unlimited |
| PC16W | [37] | unlimited |
| PCR16W | [37] | unlimited |
| PCY16W | [37] | unlimited |
| PR19W | [37] | unlimited |
| PR24W | [37] | unlimited |
| PSR19W | [37] | unlimited |
| PSR24W | [37] | unlimited |
| PY19W | [37] | unlimited |
| R2 | 28 | unlimited |
| S1 | 28 | unlimited |

"

Annex 1,

The list of categories of filament lamps and their sheets, amend to read:

"....

| Group 2 |
| --- |
| Only for use in signalling lamps, cornering lamps, reversing lamps and rear registration plate lamps: |
|  | Category |  | Sheet number(s) |  |
|  | C5W |  | C5W/1 |  |
|  | ... |  |  |  |
|  | P13W |  | P13W/1 to 3 |  |
|  | P21W |  | P21W/1 to 2 |  |
|  | ... |  |  |  |
|  | P27/7W |  | P27/7W/1 to 3 |  |
|  | PR21W |  | PR21W/1 | (P21W/2) |
|  | PR21/4W |  | PR21/4W/1 | (P21/5W/2 to 3) |
|  | PR21/5W |  | PR21/5W/1 | (P21/5W/2 to 3) |
|  | PR27/7W |  | PR27/7W/1 | (P27/7W/2 to 3) |
|  | PS19W |  | P19W/1 to 3 |  |
|  | PS24W |  | P24W/1 to 3 |  |
|  | PSY19W |  | P19W/1 to 3 |  |
|  | PSY24W |  | P24W/1 to 3 |  |
|  | PW13W |  | P13W/1 to 3 |  |
|  | ... |  |  |  |
|  | PWY24W |  | P24W/1 to 3 |  |
|  | PY21W |  | PY21W/1 | (P21W/2) |
|  | ... |  |  |  |
|  | WY21W |  | WY21W/1 to 2 |  |

| Group 3 |
| --- |
| For replacement purposes only (see transitional provisions of paragraphs 8.3. and 8.4.): |
|  | Category |  | Sheet number(s) |  |
|  | C21W |  | C21W/1 to 2 |  |
|  | P19W |  | P19W/1 to 3 |  |
|  | PC16W |  | PC16W/1 to 3 |  |
|  | PCR16W |  | PC16W/1 to 3 |  |
|  | PCY16W |  | PC16W/1 to 3 |  |
|  | PR19W |  | P19W/1 to 3 |  |
|  | PR24W |  | P24W/1 to 3 |  |
|  | PSR19W |  | P19W/1 to 3 |  |
|  | PSR24W |  | P24W/1 to 3 |  |
|  | PY19W |  | P19W/1 to 3 |  |
|  | R2 |  | R2/1 to 3 |  |
|  | S1 |  | S1/S2/1 to 2 |  |

"

Sheet H9/3, the table, amend to read:

"

| …. |
| --- |
| ELECTRICAL AND PHOTOMETRIC CHARACTERISTICS |
| Rated values | Volts | 12 | 12 |
|  | Watts | 65 | 65 |
| Test voltage | Volts | 13.2 | 12.2 | 13.2 | 12.2 |
| Objective values | Watts | 73 max. | 65 max. | 73 max. | 65 max. |
|  | Luminous flux | 2,100 ( 10% | 1,650 ( 10% |  |
| Reference luminous flux at approximately | 12 V | 1,500 |
|  | 12.2V | 1,650 |
|  | 13.2 V | 2,100 |

"

Annex 5, Paragraph 1.3., amend to read:

"1.3.	Tests shall be made at test voltage(s) as specified in the relevant lamp data sheet."

Paragraph 1.5., amend to read:

"1.5.	Before starting a test, the stabilisation of the temperature of the filament lamp shall be obtained by operating at test voltage for 10 minutes. In the case of filament lamps, for which more than one test voltage is specified, the relevant test voltage value shall be used for achieving stabilization."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.