|  | United Nations | ECE/TRANS/WP.29/2011/138 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 2 August 2011 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on General Safety Provisions

One-hundred-and-fifty-fifth session

Geneva, 15–18 November 2011

Item 4.12.5 of the provisional agenda

1958 Agreement – Consideration of draft corrigenda 
to existing Regulations submitted by GRSG

Proposal for Corrigendum 1 to Supplement 3 to Regulation No. 125 (Forward field of vision of drivers)

Submitted by the Working Party on General Safety Provisions *

The text reproduced below was adopted by the Working Party on General Safety Provisions (GRSG) at its 100th session. It is based on ECE/TRANS/WP.29/GRSG/2011/17, not amended (ECE/TRANS/WP.29/GRSG/79, para. 36). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

I.	Proposal

Paragraph 5.1.3., amend to read (including the footnote 4):

"5.1.3	Except as provided in 5.1.3.1 or 5.1.3.2., other than the obstructions created by the A pillars, the fixed or movable vent or side window division bars, outside radio aerials, rear-view mirrors and windscreen wipers, there should be no obstruction in the driver’s 180° forward direct field of vision below a horizontal plane passing through V1, and above three planes through V2, one being perpendicular to the plane X-Z and declining forward 4° below the horizontal, and the other two being perpendicular to the plane Y-Z and declining 4° below the horizontal (see Annex 4, appendix, figure 4).

The following are not considered to be obstructions to the field of vision:

(a)	Embedded or printed "radio aerial" conductors, no wider than the following:

(i)	Embedded conductors: 0.5 mm,

(ii)	Printed conductors: 1.0 mm. These "radio aerial" conductors shall not cross zone A4. However, three "radio aerial" conductors may cross zone A if their width does not exceed 0.5 mm.

(b)	Within zone A located "defrosting/demisting" normally in "zigzag" or sinusoidal form having the following dimensions:

(i)	Maximum visible width: 0.030 mm,

(ii)	Maximum conductor density:

a.	If the conductors are vertical: 8/cm,

b.	If the conductors are horizontal: 5/cm.

4	As defined in Annex 18, paragraph 2.2. of Regulation No. 43 concerning the approval of safety glazing and glazing material. "

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.